ABSURD (CCP4: Supported Program)
                                       
NAME

   absurd - for initial processing of intensity files from MADNES
   
SYNOPSIS

   absurd madhkl foo_in.mtz hklout foo_out.mtz absin foo.clm plot foo.plt
   [Keyworded input]
   
DESCRIPTION

   The program ABSURD is used for initial processing of intensity files
   created by the FAST data collection program MADNES. It can apply an
   absorption correction measured by direct-beam attenuation, it will
   reduce the indices to the asymmetric unit of the Laue group, and batch
   the data for further scaling and merging. The output is a multi-record
   MTZ file containing orientation blocks with the crystal and goniostat
   information: this file is suitable for input to SCALA for
   scaling/merging, after sorting by SORTMTZ.
   
   The input intensity file(s) may be either the INTFIL output from
   Madnes itself (eg using Eval 6) (see FILE keyword), or the binary
   unmerged file from PROCOR (see UFILE keyword): in the latter case, a
   corresponding Madnes savefile must be read as well.
   
KEYWORDED INPUT

   The various data control lines are identified by keywords with those
   available being:
   
     ABSCOR, ACCEPT, BATCH, BTITLE, CRYSTAL, FILE, LIMITS, NOABSCOR,
     OBLIQUE, PROCESS (compulsory), REINDEX, REJECT, SCALE, SPLIT,
     SYMMETRY (compulsory), TITLE, TOOFAR, UFILE
     
  ABSCOR [ <filename> ] [ <keywords> ]
  
   Apply absorption correction from direct-beam attenuation measurements.
   The absorption data taken from a file created by MADNES: if no
   filename is given, the program expects an assignment to logical name
   ABSIN. The absorption data are smoothed using spherical harmonic
   coefficients, forcing the surface to be centrosymmetric, since
   reversal of the direction of the beam should not change the
   absorption. Deviations from symmetry can be caused by misalignment of
   the X-ray beam relative to the rotation axis: this causes spuriously
   high transmission where the beam misses the crystal. Such regions may
   be omitted from the fitting, since each point on the centrosymmetric
   surface is determined twice, see OMIT option below. Individual bad
   measurements may be omitted by setting their intensity to a neagtive
   value in the input file: note that the program assumes that a value is
   present for each omega/phi position
   
   The spherical harmonic coefficients which define the calculated
   surface, and the observed data are written out to a file filename.CLM.
   This can be processed into a form which can be viewed with Frodo (see
   below).
   
   Keywords PLOT & NOPLOT control whether the observed and fitted
   absorption curves are plotted to a plotfile (logical name PLOT). The
   default is to plot them. The curves are expressed in the polar angles
   theta (latitude) and phi (longitude, not to be confused with the
   Eulerian or diffractometer angles phi), relative to the diffactometer
   Phi spindle. The observed values are plotted as a solid line (dashed
   for regions OMITted, see below).The calculated line is drawn dotted.
   
   The keyword OMIT introduces one or more ranges of Phi to be omitted
   from the fitting. This may be used to exclude regions of the measured
   curves where the X-ray beam have missed the crystal. The Phi range may
   either be specified as the Eulerian angle Phi as output by Madnes
   (default, or keyword EULERIAN preceeding OMIT), or as the polar angle
   Phi as output by ABSURD (keyword POLAR preceeding OMIT). This second
   option allows the curve to be processed once, plotted, and a region to
   omit determined from the plot. In order to fit the curve, the PROCESS
   keyword must be used, so that the save data is read from the
   reflection input file. If you are just processing the absorption curve
   to check the fit, a Save file may be given instead of a reflection
   data file. Note that the OMIT keyword must follow all other keywords
   on the line, and is followed by one or more pairs of numbers giving
   the phi ranges.
   
   Each ABSCOR command will cause the curve to be read & fitted when the
   next PROCESS command is read. This curve will then be used for all
   subsequent PROCESS commands until the next ABSCOR or NOABSCOR command.
   
  NOABSCOR
  
   Cancel application of absorption correction for subsequent files
   
  SYMMETRY <space-group name | space-group number | symmetry>
  
   (compulsory)
   
   Read the symmetry operations, specified as the name (eg P212121), the
   International Tables number, or as a series of SYMMETRY commands
   giving the symmetry operations (eg SYMMETRY X,Y,Z * -X,Y+1/2,-Z)
   
   This last option is not recommended. The symmetry matrices are read
   from a standard file (logical name SYMOP), are printed, and are used
   to reduce the reflections to an asymmetric unit. The column M/ISYM in
   the output file contains the number of the symmetry operation used to
   do this, odd numbers correspond to +hkl, even numbers to
   Bijvoet-related reflections -hkl. The asymmetric unit is selected
   according to the rule printed out with the symmetry
   
  FILE <filename>
  
   Filename for input MADNES file. If this command is not given, data
   will be read from logical name MADHKL.
   
  UFILE <filename>
  
   Filename for binary input file from PROCOR. This is the PROFIT.HKL
   (INTOUT) file from Procor: it does not contain all the necessary
   information from Madnes, so if you are taking output from Procor into
   Absurd you must read a corresponding Madnes savefile.
eg
 file Madnes_save_file
 process
 ufile profit.hkl
 process

  SCALE <scale-factor>
  
   Set output scale factor (default = 1.0). This can be adjusted to give
   intensities in a suitable range. Allowance may need to be made for
   scaling later in BEAMCOR or SCALA.
   
  TITLE <title>
  
   Set file title for output MTZ file.
   
  BTITLE <title>
  
   Set batch title for output MTZ file (defaults = file title TITLE)
   
  BATCH <batch number> [ <maximum batch number> ]
  
   Set BATCH number for output file. If the SPLIT option is used (qv),
   this will be the first batch number. Remember that batch numbers must
   be unique for all batches in an MTZ file. If several FILE & PROCESS
   commands follow a single BATCH command, all those input files will be
   assigned to the same batch. If you want different input files assigned
   to different batches, put a new BATCH command before each PROCESS
   command. Watch out if using the SPLIT option as well; batch numbers
   must be unique, and no check is made of this, so the starting batch
   number for each group must be sufficiently well separated. The
   optional maximum batch number may be used to avoid having a final
   batch with very few reflections in it.
   
  ACCEPT n1 n2 n3 . . .
  
   Set flags to accept reflections labelled with error flags n1,n2 etc
   (cf REJECT command below). MADNES sets a bit flag for each reflection
   for error conditions: this command (and REJECT) allow selection of
   which classes of reflection to accept. The flags are as follows:-

   Flag   Default        Error
  Number  Setting       Condition

     1    accept      Not found (ie weak)
     2    accept      On YMS edge
     3    accept      On ZMS edge
     4    accept      On Phi edge
     5    reject      Too far from YMS
     6    reject      Too far from ZMS
     7    reject      Too far from Phi
     8    reject      Too big in YMS
     9    reject      Too big in ZMS
    10    reject      Too big in Phi
    11    reject      Background bad
    12    reject      Background sd bad
    13    reject      Negative sd
    14    accept      Fobs <= 0.0
    15    reject      Bad pixels
    16    reject      Overflow

  REJECT n1 n2 n3 . . .
  
   Set flags to reject reflections labelled with error flags n1,n2 etc
   (cf ACCEPT command above).
   
  LIMITS <Ymin> <Ymax> <Zmin> <Zmax>
  
   Set limits on detector position Y,Z for reflection to be accepted This
   may be used to exclude reflections near the edge of the detector The
   default is not to check detector position
   
  TOOFAR <Yshift> <Zshift> <Phishift>
  
   Sets values for the maximum difference between calculated and observed
   position for a reflection to be accepted. Yshift and Zshift are in
   pixels, Phishift is in degrees. This may be used as an alternative to
   rejecting reflections using the too far flags set in Madnes. The
   default is not to check the difference in position.
   
  CRYSTAL <crystal-number>
  
   Set crystal number, a number defining a crystal which may contain a
   number of batches. This number is not currently used, but may be in
   future. The crystal number defaults to the first batch number.
   
  SPLIT <psi-range>
  
   Split data into ranges of rotation angle psi (== MADNES phi). This
   option should be used if the data are to be scaled with SCALA, ie they
   are treated as pseudo-rotation films for scaling. Each psi-range will
   be labelled as a different batch. If the data are to be scaled with
   BEAMCOR, this option should not be used.
   
  OBLIQUE
  
       [air-absorption]
       [window-absorption]
       [window-thickness]

   Apply oblique incidence correction to data, to correct for absorption
   by air and by the black-paper window. This should be done if it has
   not been included in the non-uniformity correction (from June 1989
   Phase1 onwards). If omitted, the parameters default to those for
   CuKalpha

air-absorption    [0.00108] absorption coefficient of air / mm
window-absorption [0.552]   absorption coefficient of window / mm
window-thickness  [0.1634]  thickness of window (mm)

  REINDEX <reindexing-rule>
  
   Reindex data, according to a matrix specified in a similar way to
   symmetry operations
eg reindex   k, h, -l
 reindex   h, -k, -h/2-l/2

   Cell dimensions will be recalculated for the redefined cell. Be
   careful that the index transformation preserves the hand of the axes,
   ie that the matrix has a positive determinant. The program will not
   allow you to invert the hand (eg k,h,l is forbidden, k,h,-l is
   allowed). If the transformation leads to fractional indices for some
   cases (as in the 2nd example above), these reflections will be
   rejected. If the reindexing operations include translations, then the
   orientation data in the output file will not be strictly correct.
   Translations (eg h,k,l+1) can be useful if you have misindexed your
   crystal by eg 1 lattice point (usually along the spindle axis).
   However, in this case, you OUGHT to reprocess the data.
   
  PROCESS
  
   (compulsory)
   
   Process the currently-defined input file (from FILE command or logical
   name MADHKL).
   
INPUT AND OUTPUT FILES

   The input files are
   
   MADHKL
          input Madnes intensity files, defined either as logical name
          MADHKL (as $ABSURD MADHKL file) or with a FILE command. Several
          files may be read into the same MTZ output file by a series of
          FILE & PROCESS commands (see example)
          
   The output files are
HKLOUT      MTZ file output. Each batch has an orientation
            block as defined in mtzlib.doc for area detectors.
            The columns for each reflection are

    H K L       indices
    M/ISYM      symmetry number, ie number of the
                Laue-group matrix used to reduce
                this reflection to the asymmetric unit
    BATCH       batch number
    I, SIGI     intensity and standard deviation
    IERROR      error flag from Madnes
    TIME        accumulated exposure time in minutes
    XDET,YDET   detector coordinates of reflection (pixels)
                XDET = Yms, YDET = Zms (ie Mosflm convention)
    ROT         rotation angle (degrees)

   This file must be sorted on H K L M/ISYM BATCH before processing by
   BEAMCOR or SCALA. Several files may be sorted together by SORTMTZ.
ABSIN.CLM  if the ABSCOR option is used, file containing
           spherical harmonic coefficients and observed
           absorption data. See below for further processing
           of this file.

      The file contains:-

 line 1: LMAX, LORD, NCLM, CUT

    LMAX =    maximum order of spherical harmonics
    LORD = 2  for centro-symmetric surface (always)
    NCLM =    number of coefficients
    CUT  =    standard deviation cutoff for observations

 line 2,3: NCLM coefficients

 rest of file:

theta, phi, reject-flag, relative observed intensity,
observed intensity, calculated intensity

VIEWING ABSORPTION DATA WITH frodo

   The program ABSTOFRODO reads the file absin.CLM created by ABSURD. The
   spherical harmonic coefficients which give the fitted absorption
   surface are used to generate a map of the calculated surface (logical
   name MAPOUT): this can be contoured by Frodo, with a contour level of
   0.125. The program also writes the relative observed intensities of
   the absorption measurements to a file of pseudo-atoms, in Brookhaven
   format (logical name XYZOUT). These may then be displayed on top of
   the contoured calculated surface in Frodo.
   
   The program takes one line of input, a title for the output map (see
   example)
   
EXAMPLES

absurd    hklout junk     plot absplot  << eof
TITLE This is the overall title for the file
SYMMETRY   19
CRYSTAL 1
ABSCOR abscurve.dat  PLOT   POLAR OMIT -70 +20
#
# Abscurve.dat is the file written by Madnes>Det>abscol
#
SCALE 2.5
#
# Process three files in succession. The absorption
# correction applies to all 3
# (unless there is another ABSCOR command)
#
FILE mmndump1_001.dat
BATCH 41
BTITLE  Crystal 1, run 1  # this title is for this batch only
PROCESS
FILE mmndump1_002.dat
BATCH 42
BTITLE  Crystal 1, run 2
PROCESS
FILE mmndump1_003.dat
BATCH 43
BTITLE  Crystal 1, run 3
PROCESS
eof
#
# Send plotfile to plotter
pltdev  absplot.plt
#
exit



   A VMS example

$ absurd hklout x12_absd plot x12plot
TITLE  RBP x12 3.3A with absorption correction, Q85C + MeHg
ABSCOR  x12.ABS
SPLIT 4
SYMMETRY  I4132
CRYSTAL 12
BTITLE x12 rotated about arbitrary axis, 3.3A
BATCH 100
FILE  x12_b_001
PROCESS
FILE  x12_c_001
PROCESS
FILE  x12_c_002
PROCESS
$!
$ laserprint /port=laser4port /plot x12plot.plt
$!
$ sort: sortmtz hklin x12_absd hklout x12_absd_s -
             H K L M/ISYM BATCH
$!
$UNDUPL
x12_absd_s.mtz
x12_absd_su.mtz
/lims on dx,dy (mm), phi,chi,omega
x12_rej.lis
$!

AUTHOR

   MTZ version May 1991 Phil Evans