NAME 
        HBOND  (Unsupported Program)

C  Jiffy program to calculate possible main chain hydrogen
C  bonds.
C  Main chain amide hydrogen positions are calculated from
C  input coordinates.
C	INPUT: 
C	Input coordinate file should be assigned to XYZIN
C	Unit 5:
C	1) EMIN (suggested value -0.5, but could be -1.5 for well
C	  refined high resolution structures...see reference below).
C	2) INTER
C	The program will list all hydrogen bonds with 
C	energies less than EMIN, using the equation given by Kabsch
C	and Sander, Biopolymers 22, 2577-2637 (1983).
C	The second card is optional, if present as INTER then
C	inter-subunit hydrogen bonds ONLY will be calculated. In this case
C	a new subunit is detected as a decrease in residue number
C	in the input file, and subunits are labelled sequentially
C	A,B,C,D if the  chain identifier is blank in Brookhaven file
C	otherwise the identifier in the file will be used.
C	Output is self-explanatory.
C