This is part of Gerard Bricogne's original write-upof Skewplanes,
and needs to be read in conjunction with SKEW.DOC



                          THE  JOY  OF  SKEWING
                         -----------------------
                         -----------------------

                                                   (in part)



              III.2            GENERATE
                              ----------


              III.2.1          Purpose
                               -------


	This program generates the mapping between grid coordinates in
    the final and initial maps. It can work in several modes;  mode  1
    corresponds to skew-section calculation with  optional  averaging.
    Its output is a file of records of the form :
                             _
                        I2 , X1(Tm I2)          m=1....n



              III.2.2    Algebra of coordinate frame
                         ---------------------------

	The notation may not be everywhere identical to that  of  §II,
    but this should not lead to any confusions.

              FRAMES

	(a, b, c) : crystallographic frame, on which grid G1 is based.
    Origin O. Coordinates E1, n1, C1 are dimensionless, and vary  from
    0 to 1 in the unit cell.

	(i, j, k) : orthogonal frame of 1Å-length vectors, 
    "canonically" associated to the crystallographic frame. Origin  O.
    Coordinates x,y,z in this frame are in Å. This frame is used as  a 
    reference to define the orientation of the skew grid.
	The convention used to  define  this  frame  for  some  common 
    crystal classes are shown below :


                           j    i
                        b O_________________a
                         /l  
                        / l k
                       /  l
                      /   l                  i.e. NCODE=1 in York
                     /    l                         convention
                    /     l
                 c /      l c*

 
                      MONOCLINIC
                      ----------

                      (i, j, k)= normalised    b // k and out of page

                      (a, b, c*) frame


                           k
                        c O___________________b
                          l          j
                          l
                          l
                          l i
                          l                     NCODE=1
                          l
                          l
                          l
                         a 

                       ORTHOROMBIC
                       -----------

                       (i, j, k)= normalised   c // k and out of page

                       (a, b, c) frame

                



                          k
                        c O____________________ b
                         /      .
                        /  90          .
                       /                      .
                      /                      j
                     /
                  a /
                   / i

                      RHOMBOHEDRAL
                      ------------

                      (i, j, k)= normalised   c // k and out of page

                      (a, b*, c) frame


 
           N.B. A 'normalised' frame is a frame of 1Å-long vectors


	(i', j', k') : normalised  frame  (not necessarily orthogonal)
    on which the output grid G2 is based. The origin of this frame can
    be an arbitary point O', with crystallographic  coordinates  noted
    (E°1, n°1, C°1). Coordinates in this frame are denoted x2, y2, z2;
    and are in Å, but not necessarily orthogonal.
	


                  b l           j' \     / i'
                    l               \   /
                    l                \ /
                    l                 O'
                    l                    °
                    l                        ° k'
                    l
                    l
                 j  l
                    l
                    l       i
                    O------------------------ a
                 . /
               .  /
             .   / k
           .    /
         .     /
       .      /                      For monclinic
     . c     /
            /c*                      (a, b, c) crystallographic frame

                                     (i, j, k) intermediate frame

                                     (i', j', k') new frame





               GRIDS
               -----

	  Intial grid G1.
	Based on (a, b, c).  Defined  by  na, nb, nc,  numbers  of map
    divisions along a, b, c respectively. The grid coordinates  in  G1
    will be denoted by x1, y1, z1.
	The initial domain D1 is defined by na(i), na(f), nb(i), nb(f)
    , nc(i),nc(f)  initial  and  final  values  of  intergral  grid 
    coordinates for which the density is given in  the  original  map. 
    The relation of these numbers to na, nb, nc will be discused below
    in §III.2.3.
          Final grid G2.
	Based on (i', j', k'). Defined by Dx, Dy, Dz,  grid  intervals 
    in Å along i', j', k' respectively. Grid  coordinates  in  G2  are 
    intergral and are denoted by i2, j2, k2.
	The final domain D2 is defined by  nx(i), nx(f), ny(i), ny(f),
    nz(i), nz(f), initial and final values of grid  coordinates  along 
    i', j', k' for which the density is calculated.

      	       MATRICES
               --------

	     na   0   0                Dx   0   0
	G1=   0  nb   0       and G2=   0  Dy   0
              0   0  nc                 0   0  Dz

                   define grids G1 and G2.

	Q= the transition matrix from (a, b, c) to (i, j, k).  Q  thus
    discribes the relation of the intermediate  orthonormal  frame  to 
    the crystallographic frame. It is  calculated  in  a  space  group 
    specific routine (see III.2.3)

            1/a     0    -cot(B)/a
	Q=    0   1/b       0            for a monoclinic space group
              0     0   1/(c sin(B))

            1/a     0     0
	Q=    0   1/b     0            for an orthorombic space group 
              0     0   1/c

            1/a   -1*tan(60°)/a     0
	Q=  1/b   +1*tan(60°)/b     0     for a triclinic space group 
             0         0          1/c

	P = transition matrix from (i, j, k) to (i', j', k').  P  thus
    describes the orientation of the skew relative to the intermediate
    orthonormal frame.
	It may be useful at this point to recall the definition  of  a 
    transition matrix. The transitionmatrix P from an 'old' base to  a
    'new' base has its ith column the coordinates in the old base  of 
    the the ith vector of the new base. If x is a vector,  represented
    by the 1-column matrices Xold and Xnew in the old  and  new  bases
    respectively, then one has the well known contravariance  property
    that :

                         Xold = P Xnew
                         ~      ~ ~

	(Um, Vm) , m=1...n : rotation matrix and translation vector of
    the mth averaging operation, expressed in (i', j', k').


                      TRANSFORMATION OF INDICES
                     ---------------------------


            x             x2               -1   E°1
            y     =   P * y2        +     Q   * n°1
            z         ~   z2              ~     C°1

        Å coords          Å coords              coords of O' in
      in (i,j,k)         in (i',j',k')            (a,b,c)


           E1            x                x2           E°1
           n1     =  Q * y      =    QP * y2     +     n°1
           C1        ~   z           ~~   z2           C°1

     crystallographic
     coords in (a,b,c)

                                  
	in matrix notation :      E  =  QP * X2 + X°
                                  -     ~~   

	Now :        x1     na    0    0      E1
                     y1 =    0   nb    0  *   n1     i.e. X1 = G1*E1
                     z1      0    0   nc      C1               ~  -


                     x2     Dx    0    0      i2
                     y2 =    0   Dy    0  *   j2     i.e X2 = G2*I2
                     z2      0    0   Dz      z2              ~
  

	thus,      X1 = G1[QP(G2*I2) + X°] = (G1*QP*G2)I2 + G1*X°

 	If the averaging transformations have the form :

                   X2(m)  = Um*X2 + Vm = Um(G2*I2) + Vm    m=1...n

                   X1(m)  = G1[QP(Um*G2*I2) + X°]

	Therefore 

                   X1(m)  = (G1 * QP * Um * G2)I2 + (G1*QP*Vm + G1*X°)





              IV.          THE  PROCEDURE - See new procedure for 
                          ----------------     alterations


	A  commented  procedure  is  provided  to  run  skew-section 
    calculations. It is listed on the next pages, followed by EXEC and 
    data cards. These data cards are :

    //SHNK.SYSIN DD *

    1)	SCALE	(E10.1)

	Multiplicative scale factor applied to the REAL*4 map before
    the shrinking operation (§III.1)

    //GNRT.SYSIN DD *

    1)	MODE	(1I5)                              *

	Option number, should be 1 for skew-section calculations
    (§III.2.1)

    2)	A,B,C,ALPHA,BETA,GAMMA	(6F10.5)           *

	Unit cell parameters in Å and degrees.

    3)	NA,NB,NC	(3I5)                      *

	Numbers of divisions along a,b,c  (§III.2.2, GRIDS)

    4)	NAI,NAF,NBI,NBF,NCI,NCF	  (6F10.5)         *


	Initial and final grid coordinates along a,b,c defining the
    asymmetric unit of the initial space group (do see §III.2.3).

    5)	Dx,Dy,Dz	(3F10.5)                   *

	Grid intervals in Å along skew axes (§III.2.2 GRIDS)

    6)	NXI,NXF,NYI,NYF,NZI,NZF	  (6I5)            *

	Initial and final grid coordinates along skew axes, defining
    the domain desired on output (§III.2.2, GRIDS)

    7)	Xo,Yo,Zo	(3F10.5)                   *

	Crystallographic coordinates of origin of new frame (E°1,n°1
    ,C°1 of §III.2.2, FRAMES).

    8.1) to 8.3)    P	(3F10.5/3F10.5/3F10.5)     *

	Transition matrix is defined in §III.2.2, MATRICES.

    BEWARE: As P is read in  array  notation,  cards   correspond   to 
    columns of P.

    Thus

	Card 8.1 contains the direction cosines of i' in frame (i,j,k)
        Card 8.2 --------------------------------- j' ----------------
        Card 8.3 --------------------------------- k' ----------------

    9)	NROT	(1I5)                              *

	Number of operations on skew coordinates by which the skew map
    is averaged, including the identity if it needs to be used.
	if NROT=0 the identity is assumed

    10) et seq.  (omitted if NROT=0) :             *
                
                    (ROT(I,J,N),I=1,3),J=1,3     3*(3F10.5)
         N=1, NROT 
                    TRANSL(I,N),I=1,3              (3F10.5)

	The rotation matrix and translation vector for each  averaging
    transformation, expressed in the normed skew frame (i',j',k');  be
    careful if the frame is not orthogonal since  in  this  case  your 
    rotation matrices may not be orthogonal.
	Here again, each of the first three  cards  corresponds  to  a
    column of the rotation matrix, and the 4th to the components (in Å
    ) of the translation vector. There is such a pack  of  four  cards 
    for each transformation.
	NOTE : to compute these matrices and vectors,  bear  in  mind 
    that the translation is applied after the rotation (as in x'=Rx+T)

    10 + 4*NROT)   JSEC,JFAST,JSLOW	(3I5)      *

	Sectioning flags for envelope array (omitted in mode 1, so you
    may ignore it)

    //SRT1.SYSIN DD *

	See example deck and §III.3

    //INTP.SYSIN DD *

    1)	JSECI,JFASTI,JSLOWI	(3I5)

	Sectioning flags for initial map (§III.4). Other columns are
    reserved for other options of the program. A 1 in column 30 will
    cause a detailed account of the interpolation to be printed.

    //SRT2.SYSIN DD *

	See example deck in §III.5

    //RECN.SYSIN DD *

    1)	NXI,NXF,NYI,NYF,NZI,NZF	 (6I5)

	Same card as card 6 in step GNRT

    2)	JSECF,JFASTF,JSLOWF	(3I5)

	Sectioning flags fro skew map (§III.6).  Other  columns  are 
    reserved for other options of the program.

    3) NROT 	(1I5)

	Same card as card 9 of step GNRT.

    4)	TITLE	(A80)                              *

	Any 80-character title for final skew map

    5) et seq. : any cards you want ; the program will not read 
                 them.


      *  Cards needed for new procedure

    //