MLPHARE (CCP4: Supported Program)
                                       
NAME

   mlphare - maximum likelihood heavy atom refinement and phase
   calculation
   
SYNOPSIS

   mlphare hklin foo.mtz hklout foo_out.mtz newparm foo_out.com [xyzout
   foo.brk]
   [Keyworded input]
   
DESCRIPTION

   This program will refine heavy atom parameters and error estimates,
   then use these refined parameters to generate phase information. The
   maximum number of heavy atoms which may be refined is 130 over a
   maximum of 20 derivatives. The program was originally written for MIR,
   but may also be used for phasing from MAD data, where the different
   wavelengths are interpreted as different "derivatives".
   
   Beware: This program is fundamentally different from the old PHARE,
   even though some of the code looks familiar. The incorporation of the
   concepts of Maximum Likelihood means that the refinement of parameters
   is much more robust, and the generation of phases and figures of merit
   is more realistic. See NOTES ON USAGE.
   
   Note: heavy atom parameters can also be refined in vector-space using
   the program VECREF.
   
   Ref: Z.Otwinowski: Daresbury Study Weekend proceedings, 1991
   
KEYWORDED INPUT

   Keywords are divided into two sets.
   
    Set 1: general keywords
    
   These keywords control the calculation. Compulsory keywords are:
      LABIN
      CYCLE or PHASE
      LABOUT - essential if you wish to output an HKLOUT file.
      END - to designate the end of input; if more than one
            derivative is described, the keyword DERIV
            designates the end of input for the previous derivative.

   Optional keywords are:
   
     ANGLE, APPLY, CENTRIC, COORDS, EXCLUDE, SKIP, FHOUT, HLOUT, PRINT,
     RESOLUTION, SCALE, SCRIPT, THRESHOLD, TITLE
     
   In addition, the following optional keywords control the data
   harvesting functionality:
   
     PNAME, DNAME, PRIVATE, USECWD, RSIZE, NOHARVEST
     
    Set 2: derivative keywords which MUST follow the above list
    
   These are repeated once for each derivative.
   
   Compulsory keywords are:
   
     ATOM, ATREF, DCYCLE, DERIVATIVE
     
   Optional keywords are:
   
     ANOERROR, EXCLUDE, ISOERROR, RESOLUTION, SCALE, WAVE
     
  Set 1: general keywords
  
  CYCLE <ncycle> [ <kcycle1> <kcycle2> ...]
  
   <ncycle> sets the number of cycles that the program will run (default
   10). The first (<ncycle>-1) cycles are used for refinement of the
   heavy atom parameters and the error estimates. The phases for ALL
   reflections in the file to the outer resolution limit are calculated
   on the final cycle. Statistics may be collected for both the final
   cycle of refinement, and the phasing cycle.
   
   <kcycle1> <kcycle2> ... are flags for externally calculated phases and
   need only be set if you want to use these. In general the refinement
   procedure works out the likely weighting of all possible protein
   phases sampled round the phase circle and uses this information to do
   a phased refinement. Any particular derivative contribution will be
   controlled by the parameters on the DCYCLE input line.
   
   If you want to input phases calculated elsewhere and use them in
   refinement for some cycles, list these cycle numbers here. E.g.:
   CYCLE 10 2 3 5 7 9
   would mean that 10 cycles will be run, 9 for refinement and a final
   phasing cycle, and that external phases would be used during
   refinement on cycles 2, 3, 5, 7 and 9. If these flags are set you must
   assign a column for PHIC, and for either WC or FC. See NOTES ON PHIC
   for details of how these are used. A contribution may be added to the
   phase likelihood calculated from derivatives to favour the external
   phase or it may be used alone.
   
  PHASE
  
   This keyword signals that you ONLY want to calculate phases and not to
   do any refinement. It is equivalent to CYCLE 1. The phases for ALL
   reflections in the file to the outer resolution limit are calculated.
   
  LABIN <program label>=<file label> ...
  
   Associates the column labels that the program expects with column
   labels in the input file. The following <program label>s can be
   assigned:
        FP      SIGFP
        FPH1    SIGFPH1    DPH1    SIGDPH1
        FPH2    SIGFPH2    DPH2    SIGDPH2
        FPH3    SIGFPH3    DPH3    SIGDPH3
        FPH4    SIGFPH4    DPH4    SIGDPH4
        FPH5    SIGFPH5    DPH5    SIGDPH5
        .
        .
        .
        FPH20   SIGFPH20   DPH20   SIGDPH20
        FC      PHIC      WC
        F0      F1        F2       F3   ..F19

   Where:
   
   H, K, L
          
   FP
          Native F
          
   SIGFP
          sigma(FP)
          
   Then for each derivative (i=derivative number)
   
   FPHi
          Derivative F
          
   SIGFPHi
          sigma(FPHi)
          
   [DPHi]
          Anomalous difference (if anomalous data are used)
          
   [SIGDPHi]
          sigma(DELi)
          
   For externally calculated phases
   
   PHIC
          The phases to be used in refinement. This is only needed if the
          <kcycle> flags have been set. See keyword CYCLE.
          
   [WC]
          Weight for these phases. Defaults to 1.0.
          
   [FC]
          Fcalc value. Used to estimate Sim Weight for calculated phases.
          
   F0 F1 .. Assignments for selected extra columns to be copied to the
   output file
   
   Assignments are required for FP, SIGFP, and at least one derivative
   (FPH1, SIGFPH1). The number of derivatives is deduced from the FPHi
   assignments.
   
   If you wish to copy all columns from input to output file, specify
   ALLIN on the LABOUT line. If you wish to copy selected columns from
   input to output file, you may assign up to 19 columns, using F0 F1 ...
   F19
   
  LABOUT [ ALLIN | [ <program label>=<file label> ... ] ]
  
   Associates column labels in the output file with labels used by the
   program.
   
   Specifying ALLIN copies all input columns to output.
   
   The following extra labels can be assigned.
        PHIB    FOM
        HLA     HLB        HLC     HLD
        FH1     PHIH1      FHA1    PHIHA1
        FH2     PHIH2      FHA2    PHIHA2
        .....
        FH20    PHIH20     FHA20   PHIHA20

   where
   
   PHIB
          maximum likelihood phase
          
   FOM
          figure of merit
          
   HLA,HLB,HLC,HLD
          Hendrickson-Lattman coefficients output if HLOUT requested
          
   FHi PHIHi FHAi PHIHAi
          give the heavy atom real and imaginary structure factors.
          Output if FHOUT is requested for this derivative (the FPHi
          SIGFPHi [ DPHi SIGDPHi ] will also be copied to the output
          file). This information is needed if you want to do double
          difference Fourier to find more heavy atom sites. See the FFT
          documentation.
          
   FP SIGFP PHIB and FOM
          are always output.
          
   The following are copied from the input file if they have been
   assigned.
        FC      PHIC      WC
        F0      F1        F2       F3   ..F11

   If LABOUT is specified the program outputs a file assigned to HKLOUT
   containing at least H K L FP SIGFP PHIB FOM and other optional columns
   FOR ALL REFLECTIONS to the outer resolution cut off. IF LABOUT is NOT
   specified you get no output file.
   
   For certain problems it is convenient to assign FP and FPHi to the
   same column.
   
  Optional keywords:
  
  ANGLE <iangle>
  
   <iangle> is the angle interval in degrees for calculation of the phase
   probability curve (default 10).
   
   N.B.: The program speed is proportional to 360/<iangle>. ZO recommends
   <iangle>=20 except when the derivative has high phasing power, then
   <iangle>=10. EJD always uses <iangle>=10 - time is not so valuable...
   
  APPLY
  
   The final overall scale and B values for each derivative are applied
   to FPHi, SIGFPHi, DPHi, SIGDPHi before these are written to HKLOUT.
   The default is to simply echo the columns which are input.
   
  CENTRIC
  
   This restricts the program to use only centric reflections for
   refinement. This is sensible if you have enough centric data. In
   general there are many many more observations than heavy atom
   parameters to refine, and the coordinates and relative real
   occupancies can often be accurately refined from the centric data
   alone. You will however have to use acentric data to refine the
   anomalous occupancy. In that case, it is sensible to refine the
   coordinates and real occupancies against centric data first, and
   include acentric data in a second run.
   
  SKIP <nskip>
  
   <nskip> The program only uses every "Icycle+nskip-th" reflection for
   refinement. This saves a great deal of time. The reflection set
   changes with each cycle. The final phasing cycle uses all reflections.
   
  EXCLUDE [SIGFP <siglim>]
  
   If SIGFP is followed by a number <siglim> reflections are excluded if
   FP < siglim*SIGFP. Other EXCLUSION tests are given for each derivative
   in turn.
   
  FHOUT [DERIV] <i1> <i2> ...
  
   <i1> <i2>... give the derivative numbers for which you want FHi PHIHi
   [FHAi PHIHAi] output ready for double difference maps.
   
  HLOUT
  
   Causes output of Hendrickson-Lattman coefficients.
   Default labels HLA HLB HLC HLD
   
  PRINT [STATS] [AVF] [AVE] .... [NOSTATS] [MON <nmon>] [COR]
  
   The subsidiary keywords control the type of output. Default is to
   output statistics for the final cycle only. Refinement statistics only
   include reflections used for a REFINEMENT pass for that derivative.
   The final statistics will include information from all reflections. If
   you are only doing phasing, for instance after changing hand, no
   statistics are output.
   
   Possible keywords are:
   
   STATS
          statistical output and xloggraphs for last refinement cycle and
          final phasing cycle.
          
   NOSTATS
          no statistics output.
          
   MON <nmon>
          Set this if you want to monitor every <nmon>-th reflection. The
          default is every 10-th reflection.
          
   COR
          Output correlation matrix (default: do not)
          
   Keywords to control type of statistical analysis.
   
   AVF
          gives unweighted Average FP FPH FH
          
   AVE
          gives unweighted Average Lack_of_closure terms.
          
   RMSF
          gives unweighted rms FP FPH FH
          
   RMSE
          gives unweighted rms Lack_of_closure terms.
          
   WiAVF
          gives weighted Average FP FPH FH summed over the phase circle
          
   WiAVE
          gives weighted Average Lack_of_closures summed over the phase
          circle
          
   WiRMSF
          gives weighted rms FP FPH FH summed over the phase circle
          
   WiRMSE
          gives weighted rms Lack_of_closures summed over the phase
          circle
          
   There is some debate over which type of statistic is the most useful.
   EJD uses AVE and AVF. It is important to use only ONE option,
   otherwise you are swamped with information, and to stick to that
   option. To assess whether new sites are contributing EJD looks for a
   reduction in the Cullis R-factors as new sites are added. See NOTES ON
   USAGE for hints on using this information.
   
   W1 refers to this weight:
  W1 = phase prob(PHIx) / ( SIGFPH**2 + VCALC + ISOERROR**2 )
for this derivative at this resolution for each possible phase, where

  VCALC = SIGFP**2 *
        ((FPSQ + FPA * FHA + FPB * FHB) / (FP * FPH))**2

  FPA = FP * COS(PHIx) , FPB = FP * SIN(PHIx)
    where PHIx takes all values round the phase circle

    and  FHA = FH * COS(PHIH)   FHB = FH * SIN(PHIH)
         This seems the best error.


W2 refers to this weight:


  W2 =  phase_prob(PHIx) /(SIGFP**2 + SIGFPH**2)
        where SIGFP = sig(Fp) and SIGFPH = sig(Fph)

  RESOLUTION [ <rmin> ] <rmax>
  
   Overall resolution range for all refinement and phasing in Angstroms
   (or as 4sin(theta)**2/lambda**2 limits iff both are <1.0). If only one
   limit is given, it is the upper limit; otherwise the limits can be in
   either order. The default is to use the resolution from the MTZ file.
   Data for derivatives can each be limited by a further RESOLUTION
   keyword after the DERIVATIVE definitions.
   
  SCALE SIGFP <scale>
  
   Specifies the scale factor by which to multiply SIGFP. The default is
   <scale>=1.
   
  THRESHOLD <thr> <acl>
  
   These parameters allow you to modify large shifts in any parameter. If
   any parameter_shift exceeds <thr>*SD_parameter_shift then the shift is
   dampened by <acl>. The default is <ac1>=1, <thr> not set.
   
  TITLE <title>
  
   The specified title is written to the HKLOUT file. The default is the
   title from the MTZ file.
   
  SCRIPT
  
   This will produce a COM file (VMS) or unix script. One can then run
   MLPHARE again but with the refined heavy atom parameters in the ATOM,
   ISOERROR and ANOERROR cards. The other input cards will be the same as
   in the original script. However, the ATREF cards will allow refinement
   of all parameters in every cycle. The output script file is assigned
   to NEWPARM.
   
  COORDS
  
   This will cause the program to output the refined coordinates of the
   heavy atom sites into the external file with logical name XYZOUT, in a
   pseudo-PDB format suitable for input into a viewing program e.g.
   RASMOL.
   
   The file contains CRYST1 and SCALE cards, and the following data for
   each site appears on an ATOM record (from left-to-right):
   
   Position in pseudo-PDB file Quantity
   7-12 (Atom serial number) Position of the site in the list
   13-14 (Chemical symbol) Chemical symbol of heavy atom (supplied on
   ATOM keyword)
   23-26 (residue number) Derivative number
   31-54 (angstrom orthogonal coordinates) Refined X,Y,Z orthogonal
   coordinates of the site
   55-60 (occupancy) Refined occupancy of the site
   61-66 (iso b-factor) Refined isotropic B-factor
   
    Data Harvesting keywords
    
   Provided a Project Name and a Dataset Name are specified (either
   explicitly or from the MTZ file) and provided the NOHARVEST keyword is
   not given, the program will automatically produce a data harvesting
   file. This file will be written to
   
   $HARVESTHOME/DepositFiles/<projectname>/ <datasetname>.mlphare
   
   The environment variable $HARVESTHOME defaults to the user's home
   directory, but could be changed, for example, to a group project
   directory.
   
  PNAME<project_name>
  
   Project Name. In most cases, this will be inherited from the MTZ file.
   
  DNAME<dataset_name>
  
   Dataset Name. In most cases, this will be inherited from the MTZ file.
   
  PRIVATE
  
   Set the directory permissions to '700', i.e. read/write/execute for
   the user only (default '755').
   
  USECWD
  
   Write the deposit file to the current directory, rather than a
   subdirectory of $HARVESTHOME. This can be used to send deposit files
   from speculative runs to the local directory rather than the official
   project directory, or can be used when the program is being run on a
   machine without access to the directory $HARVESTHOME.
   
  RSIZE<row_length>
  
   Maximum width of a row in the deposit file (default 80). <row_length>
   should be between 80 and 132 characters.
   
  NOHARVEST
  
   Do not write out a deposit file; default is to do so provided Project
   and Dataset names are available.
   
  Set 2: derivative keywords
  
   Next cards are repeated once for each derivative
   
  DERIV <title>
  
   <title> is used to flag the output. Be informative! (Compulsory for
   each derivative assigned on the LABIN line.)
   
  DCYCLE [PHASE] i1 i2 [REFCYCLE] j1 j2 [KBOVERALL] k1 k2
  
   Subsidiary keywords PHASE, REFCYCLE, KBOVERALL control the use of this
   derivative. Default is NOT to use the derivative for PHASE, REFC and
   KBOV.
  PHASE [ALL] or i1 i2 ...
  REFCYCLE [ALL] or j1 j2 ...
  KBOVERALL [ALL] or k1 k2 ...

   Then the derivative is used for:
   phasing on cycles i1 i2 ... refining on cycles j1 j2 ...
   The overall scale and B are refined on cycles k1 k2 ...
   (The word ALL means act on all cycles...)
   
  EXCLUDE [SIGFPH <siglim>] [DISO <isolim>] [DANO <anolim1 anolim2>]
  
   SIGFPHi <siglim>
          Reflections are excluded if FPHi < siglim*SIGFPHi. Default is
          <siglim>=0.
          
   DISO <isolim>
          Reflections are excluded if abs(FPHi-FP) > <isolim>. The
          default is <isolim> unset and unused.
          
   DANO <anolim1> [ <anolim2> ]
          Reflections are excluded if abs(FPHi(+) -FPHi(-)) > <anolim1>.
          The default is unset. Reflections can also be excluded if
          abs(FPHi(+) -FPHi(-)) < <anolim2>. EJD feels it is very unwise
          to use this.
          
  SCALE FPHi <scale> <b>
  
   (i=1,2...) followed by <scale> and <b> to apply to FPHi and SIGFPHi as
   exp(-<b>*ss)/<scale>. The defaults are <scale>=1, <b>=0 which should
   be sufficient if the data has been through FHSCAL or SCALEIT.
   <scale> and <b> may subsequently be refined by the program, see DCYCLE
   keyword.
   
  SCALE SIGFPHi <scale2>
  
   <scale2> is used to further scale up SIGFPHi. Final SIGFPHi =
   <scale2>*exp(-<b>*ss)/<scale>
   The default is <scale2>=1.
   
  RESOLUTION [ <rmin> ] <rmax>
  
   Specify resolution limits to use for this derivative (as above for the
   overall resolution).
   
  RESOLUTION ANO <rmin> <rmax>
  
   Resolution range for use of anomalous data for this derivative
   (defaults to limits for isomorphous data).
   
  ISOERROR <ierr1> <ierr2> ... <ierr8>
  
   Eight numbers giving the estimated isomorphous lack of closure error
   as a function of resolution. For initial refinements do not give
   these, and allow the program to evaluate them. If running a final
   phasing pass, take the values output at the end of the refinement
   cycle.
   
  ANOERROR <aerr1> <aerr2> ... <aerr8>
  
   Eight numbers giving the estimated anomalous lack of closure error as
   a function of resolution. For initial refinements allow the program to
   evaluate these. For a final phasing pass, take the values output at
   the end of a refinement cycle.
   
  ATOM <ID> <Xfrac> <Yfrac> <Zfrac> <occ> [<aocc>] BFAC <b1> [<b2> <b3> <b4>
  <b5> <b6>]
  
   One for each site (at least one site must be given for each
   derivative).
   
   <ID>
          Atom identifier which must match a form factor given in the
          file assigned to ATOMSF (default $CLIBD/atomsf.lib). The
          standard form factors are given for the CuKa wavelength, so the
          values of f' and f'' may not be appropriate for other
          wavelengths. You will need to interpret your occupancies
          intelligently: the refinement of the real and anomalous
          occupancies models f' and f'' perfectly well, and can be used
          to phase and refine with heavy atom data collected at multiple
          wavelengths. Selecting <ID> = Ano sets f' and f'' equal to 1 so
          that everything is included in the real and anomalous
          occupancies. In fact using MLPHARE for multiple wavelength data
          has generally been found to be better, and easier than the
          geometric phasing method proposed by Karle and Hendrickson.
          
   <Xfrac> <Yfrac> <Zfrac>
          atomic coordinates given as fractions of unit cell.
          
   <occ>
          atom occupancy. Remember this will probably be on an arbitrary
          scale. At this stage you are unlikely to have amplitudes on the
          absolute scale.
          
   <aocc>
          anomalous occupancy. Remember this will probably be on an
          arbitrary scale too. See NOTES ON USAGE for interpretation of
          sign.
          
   <b1> [<b2> <b3> <b4> <b5> <b6>]
          If only <b1> is set, <b1> is the isotropic temperature factor
          If <b1> <b2> <b3> <b4> <b5> <b6> are set, they define the
          anisotropic <b> factor. The temperature factor is defined as:
          exp(-(h*h*<b1> + h*k*<b2> + h*l*<b3> + k*k*<b4> + k*l*<b5> +
          l*l*<b6>))
          For a rough approximation to give an anisotropic B factor take
          <b1> = <b4> = <b6> = <b>, <b2> = <b3> = <b5> = 0.
          
   The isotropic B factor is approximated by 1/3(<b1>+<b4>+<b6>).
   
   Following Willis and Pryor conventions, I think
           b1 = k*beta11, b4 = k*beta22, b6=k*beta33
           b2 = k*beta12, b3 = k*beta31, b5=k*beta23
where their temperature factor is expressed as:

 exp(-0.25(  h**2 * (a*)**2 * beta11 + k**2 * (b*)**2 * beta22
           + l**2 * (c*)**2 * beta33  + 2*k*l*(b*)*(c*)*beta23
           + 2*l*h*(c*)*(a*) *beta31 + 2*h*k*(a*)*(b*) *beta12))

   This means the Uij terms of an anisotropic temperature factor is equal
   to betai */(8*pi**2).
   
  ATREF [ [X | AX] [ALL | <k1> <k2>...] ] [Y | AY ... Z | AZ ...] [OCC [ALL |
  <i1> <i2>... ]] [AOCC [ALL | <j1> <j2> ...]] [ [B | AB] [ALL | <l1> <l2>...]
  ]
  
   The keywords X or AX, Y or AY, Z or AZ, OCC, AOCC, B or AB flag which
   parameter should be refined. X Y Z mean refine coordinate to fit the
   isomorphous differences. AX AY AZ mean refine coordinates to fit the
   anomalous differences (only one of X or AX can be used). Similarly for
   B and AB. The keyword ALL means refine parameter on all cycles.
   Numbers <i1> <i2> etc. mean refine parameters on the numbered cycles
   only.
   
  WAVE [LAM <wavelength>] [FPR <f'>] [FDP <f">]
  
   The keyword WAVE specifies the wavelength for this derivative. It
   allows the user to alter the default values of f' and f" for the heavy
   atom. Specify the f' (FPR) and f" (FDP) at this wavelength.
Example:

  WAVE  0.9000  FPR -1.622  FDP 3.285
  WAVE  0.9795  FPR -8.198  FDP 2.058
  WAVE  0.9809  FPR -6.203  FDP 3.663

  END
  
   Each DERIVATIVE set finishes with another DERIV card or END.
   
INPUT AND OUTPUT FILES

   The input files are:
    a. The control data file
    b. The input reflection data file in standard MTZ format.
       
   The output files are:
    a. A log file which contains a complete description of the
       calculation plus some extremely useful XLOGGRAPH tables (see
       xloggraph documentation for instructions on how to display these).
       The final lines are in the format for updating the control data
       file; containing refined heavy atom scale factors, calculated lack
       of closure errors and parameters. You can edit these back into the
       next control data file or set the SCRIPT keyword. Take care to
       reset the ATREF flags to do what you want to do.
    b. A reflection data file which will copy some or all of the input
       reflection data file with the following additional columns:
       
        PHIB
                Phase
                
        FOM
                Figure of merit
                
        [HLA,HLB,HLC,HLD]
                Hendrickson-Lattman coefficients if required
                
        [FHi PHIHi [ FHAi PHIHAi ] ]
                Two or four items per derivative if FHOUT requested.
                
    c. A script/COM file which can run mlphare again but contains the
       refined heavy atoms parameters mentioned in a).
       
NOTES ON USAGE - Eleanor Dodson

   Definitions of abbreviations:
   
   MIR
          Multiple Isomorphous Replacement - generating protein phases
          from the observed differences between FP and several FPHi, and
          the FHi vectors calculated from the various sets of heavy atom
          positions.
          
   MIRAS
          Multiple Isomorphous Replacement - generating protein phases
          from the observed differences between FP and the FPHi(+) and
          FPHi(-) + FHi
          
   SIR
          Single Isomorphous Replacement - generating protein phases from
          the observed differences between FP and one FPH + FHi
          
   SIRAS
          Single Isomorphous Replacement - generating protein phases from
          the observed differences between FP and one FPH(+) and FPH(-)
          and FHi
          
   MAD
          Multi-wavelength Dispersion - generating protein phases from
          the observed differences between several sets of FPH(+) and
          FPH(-) measured at different wavelengths where the f' and f of
          the heavy atom scatterer are different, and the FH vectors
          calculated from these heavy atom positions.
          
   See the EXAMPLES for detailed comments on heavy atom analysis.
   
   This program refines heavy atoms without significant bias, and
   estimates figure of merits realistically. THIS MEANS THAT THE OUTPUT
   WILL PERFORM MUCH BETTER AFTER SOLVENT FLATTENING OR DENSITY
   MODIFICATION THAN BEFORE. Mlphare is NOT usually used to generate the
   phases for the map to be interpreted - it is giving you an INITIAL
   STARTING point for 'dm' or some other phase improvement procedure.
   Thus the reliability of the Figure of Merits is the most important
   information it gives.
   
   It is sensible to refine heavy atoms occupancies first against the
   centric data, if you have some. This gives very similar answers to 3D
   data in a fraction of the time. It is possible to phase on some
   derivatives and refine others. In my experience this gives answers
   very close to the default procedure of including all parameters for
   both phasing and refinement.
   
   It is sensible to exclude any suspect data from the heavy atom
   refinement. Using a sigma cutoff and values for DISO and DANO chosen
   using SCALEIT output reduced the standard deviation of parameters.
   Phases are calculated for all reflections to the outer resolution
   limit on the final cycle. The option to input external phases seems to
   work. But I am not sure of the theoretical correctness of this. There
   can't be much maximum likelihood going on. See NOTES ON PHIC - I think
   the relative weighting of the PHIC contribution is probably not very
   sensible. But it is really not necessary - there is so little evidence
   of bias in standard calculations I would never recommend using it
   here. (Of course externally obtained phases can be very helpful in
   doing difference Fourier to help you find the sites in the first
   place...)
   
   For the best phasing you need to find all the significant sites in a
   derivative. After you have found and refined the first set of sites
   you can use a difference Fourier with these SIR phases to find other
   sites. However these maps will usually show confusing ghosting in the
   vicinity of the existing sites. Alternatively, you can use the
   procedure below which uses cross difference Fouriers to find sites in
   other derivatives. If you have several independent derivatives, one
   good procedure is to refine the heavy atom sites of the first, use the
   SIR phases from this one to do difference Fouriers for the second;
   check that sites found in the second derivative difference maps
   correspond to Patterson peaks. Repeat the procedure with the SIR
   phases from the second derivative and confirm these maps show the
   sites in the first derivative, and so on. HOWEVER many things can go
   wrong! The most troublesome is trying to decide whether the
   derivatives have common sites. The SIR phases usually generate ghost
   peaks and holes in the neighbourhood of the first site, which can be
   very confusing. And very often heavy atom sites sit on symmetry
   points, so the SIR phases are essentially centric, and maps phased
   with them contain peaks at both xyz AND -x,-y,-z...
   
   The advantage of this cross difference Fourier approach is that your
   sites for a second derivative will be determined relative to the same
   origin as the first. Pattersons alone in P212121 can give solutions of
   either (x,y,z) + (n1/2,n2/2,n3/2) or (-x,-y,-z) + (n1/2,n2/2,n3/2)
   where n1,n2,n3 can be either 0, or 1; i.e. there are 16 possibilities
   to consider. It doesn't matter for the first site you choose but all
   others within that derivative and all others must follow the same
   convention.
   
   Assuming you now have two derivatives consistent with each other, you
   can refine the anomalous occupancies of both beginning with AOCC =
   0.00 and they should all become either positive, in which case you
   have chosen the right hand, or negative, so you need to use the
   enantiomorph if you wish to see right handed alpha helices. Note that
   FOM will not be able to distinguish between the enantiomorphs. You can
   visualise this by appreciating that changing hand generates phase
   circles which are mirrored through the line PHI=0 and therefore have
   the same quality crossings. One hand gives phases PHIB and the other
   phases -PHIB.
   
   Another approach which is worth following in cases where you have
   anomalous data (and there should not be any where you don't..) is the
   following:
   Refine the single derivative heavy atom real occupancies (using
   centric data if you have enough) then start refining the anomalous
   occupancies (using all the data). You will need to start them all at
   some positive value; otherwise they will stick at 0.0000. If the
   derivative and data are OK all occupancies should stay with the same
   sign. You then need to recalculate the phases with the other
   enantiomorph; here the FOM will be the same, but the phases will not
   be just the mirror image of the first set. Don't forget: Changing the
   enantiomorph requires changing the space-group as well for some
   space-groups, e.g. P41/P43; P31/P32, P61/P65 P62/P64 and variants.
   There is even an awful cubic one where you have to move the origin.
   This requires you run mtzutils or cad to produce a new mtz file with a
   different spacegroup defined in the header. Now you have two sets of
   SIRAS phases, you choose between them by looking at maps. Difference
   Fouriers for one enantiomorph SHOULD give clearer peaks than for the
   other. 'dm' output for one set of phases should give better statistics
   than for the other. BUT this distinction can be very marginal; if your
   anomalous occupancies refine away towards 0.0 there will be no
   distinction of course.
   
   Here are some specific notes on using mlphare to refine and phase from
   MAD data. This is simply a special case of MIR phasing, where now the
   real occupancies will be proportional to the f'(j) -f'(P), and the
   anomalous occupancies are proportional to f(j) . The FP assignment
   must be the same as one of the FPHi and that DERIVATIVE will have all
   real occupancies == 0.0 and these cannot be refined. The enantiomorph
   problem is now particularly serious; since all the FH vectors are
   parallel to each other, it is possible to reflect the phase circle
   diagram both about AlphaH ( equivalent to changing coordinates to the
   other hand) AND about the direction AlphaH +90 ( equivalent to getting
   the sign of the f'(j) -f'(P) reversed.) and in each case to get
   exactly the same Figures of Merit. Since the wavelength for each data
   set is known it is possible to get the signs of the real occupancies
   correct. Be careful!! It may be best to have as the 'native', the data
   set collected at the lowest f' wavelength so that all real occupancies
   should be positive, but if this data set is incomplete there may be a
   good reason to choose another.
   
   Our procedure is summarised here:
  Find anomalous scatterer sites
  ( Patterson? Shelx90?? However..)

  Refine real occupancies and XYZ using CENTRIC option for
  MLPHARE doing each pair of wave lengths independently.
  This is very quick - seems more accurate than using all
  data, and gives independent estimates of how good your f'
  estimates are.

  ( the ratios of f'(j)-f'(P) should be constant for all
  sites - they will NOT be on the absolute scale though..)

  Then we take those real occupancies and ISOE tables and
  hold them fixed while refining the anom occupancies ( you
  must remember to use ATREF AX ALL AY ALL AZ ALL etc  if you
  want to refine any other parameter to make sure the
  anomalous differences are used)

  As I said push the occupancies towards the positive sign
  by a bit. Obviously it is bad if you get some positive and
  some negative, and again the ratio of the different
  occupancies should reflect the expected f'' values ( I am
  afraid they are never spot on for us - we can't be so good
  at staying on the inflection point..)

  This refinement with all the data will give sites and
  ANOEs, and these can be cut and pasted into a test where
  the x y z sign is reversed.

  THEN we do two things: look at maps - one map should have
  a clearer solvent boundary than the other, and run DM -
  and one hand should give marginally better statistics than
  the other.

  It works - providing the data is good enough, the anomalous
  scatterer is correctly positioned, and none of the other
  disasters which can occur have occurred!

   A common one is: Starting X Y Z refinement with ALL occupancies zero.
   This means there are no sensible gradients for x y z and they can
   slide about.
   
NOTES ON PHIC

   In order to merge information about external phases with MIR phase
   information, an extra calculated phase probability contribution is
   calculated.
 PROB(PHASEi)= PROB(PHASEi) + exp(-((FPAi-WC*FCA)**2
                            + (FPBi-WC*FCB)**2))/
                    ((FC*(1-WC))**2 + sigma(fnat)**2)
     FPAi = FP*cos(PHASEi)
     FPBi = FP*sin(PHASEi)
     FCA  = FC*cos(PHIC)
     FCB  = FC*sin(PHIC)
  if FC is not input, then FC equals FP
  if WC is not input WC = 1.

   See examples.
   
NOTES ON OCCUPANCIES

   The occupancies used by heavy atom refinement programs are on the same
   scale as FP, so if you haven't put your data on an absolute scale (and
   you can't without using high resolution data) the occupancies will not
   be absolute. E.g., if your FPs are 10 times absolute, your occupancies
   should be in the range 0 to 10. Because all your derivatives have to
   be on the same scale as FP, using relative occupancies will not affect
   the results in any way (except of course for the apparent non-physical
   meaning of occupancies >1!).
   
PRINTER OUTPUT

   The printer output starts with details from the control data file
   followed by details of the input reflection data file and the header
   information written to the output reflection data file.
   
   After each cycle the current error estimates and figure of merit are
   tabulated over the resolution range. The new parameters and their
   standard deviations are listed. N.B.: If an occupancy becomes near to
   0.0 the coordinate shifts will possibly be meaningless.
   
   Then for the last cycle of the refinement the following sections are
   output giving an extensive statistical analysis of the results of the
   refinement. This is repeated for the final phasing cycle, which may
   well involve more reflections.
   
   For each compound the following sections are output:
    i. Details of the parameters for each heavy atom site of the
       compound, details of the correlation matrix if requested. The
       determinant of the normal matrix.
   ii. The refinement parameter for isomorphous and anomalous
       differences. At convergence these should be ~1.0
   iii. Analysis of Differences between Heavy Atom and Protein Phases:
         a. as a Function of Figure of merit
         b. as a Function of Resolution
       
   Note:
    i. The mean difference should be ~90. If it is not, the scale between
       FP and FPH is probably wrong.
   ii. The standard deviation of the distribution should be 51.96 for
       acentric reflections, and 90 for centric reflections if the
       protein phases are based on several independent derivatives. The
       table gives:
          <FOM> range
     or [ <4SSQ/LL>  range
          Resolution (Angstroms) ]
          Number of reflections                  (acentrics)
          Average Phase difference               (acentrics)
          Standard deviation of phase difference (acentrics)

          Number of reflections                  (centrics)
          Average Phase difference               (centrics)
          Standard deviation of phase difference (centrics)
   iii. Analysis of average or rms FP FPH and FH as a Function of
       Resolution. For acentric reflections the FH components derived
       from the fh-fh' and from the fh'' are listed separately. The
       values can be weighted - see keyword PRINT for details.
       The table gives:
          <4SSQ/LL>  range
          Resolution (Angstroms)
          Number of reflections                  (acentrics)
          Mean or rms FP                         (acentrics)
          Mean or rms FPH                        (acentrics)
          Mean or rms calculated FH_real         (acentrics)
          Mean or rms calculated FH_imag         (acentrics)

          Number of reflections                  (centrics)
          Mean or rms FP                         (centrics)
          Mean or rms FPH                        (centrics)
          Mean or rms calculated FH_real         (centrics)
   iv. Analysis of average or rms isomorphous lack of closure as a
       function of resolution. The values can be weighted - see keyword
       PRINT for details.
       Isomorphous difference is |FPHi -FP|.
       Lack of closure is |FPHi - |FP+FH|| where |FP+FH| is a vector sum
       of the calculated FH, phase PHIH and FP with the protein phase.
       For the unweighted averages or rms entries the protein phase is
       that obtained by MLPHARE.
       For the weighted tables every value of PHIx around the phase
       circle is included with the appropriate weight. Since the weights
       for most values of PHIx are ~0.0 these tables should give similar
       results to the unweighted ones.
       Phasing power is <FH/ Lack_of_closure>.
       Cullis R factor is <Lack_of_closure>/<Isomorphous difference>.
       N.B.: This is tabulated for acentric and centric terms, extending
       the former definition.
       It is the most useful signal for a usable derivative. Values < 0.6
       for centric data are excellent; values < 0.9 are usable. If a new
       site does not reduce the Cullis R factor it is probably not
       correct.
       The table gives:
          <4SSQ/LL>  range
          Resolution (Angstroms)
          Number of reflections                  (acentrics)
          Mean or rms isomorphous difference     (acentrics)
          Mean or rms lack of closure            (acentrics)
          Phasing power                          (acentrics)
          Cullis R factor                        (acentrics)

          Number of reflections                  (centrics)
          Mean or rms isomorphous difference     (centrics)
          Mean or rms lack of closure            (centrics)
          Phasing power                          (centrics)
          Cullis R factor                        (centrics)
    v. Analysis of average or rms anomalous lack of closure as a function
       of resolution. The values can be weighted - see keyword PRINT for
       details.
       Anomalous difference is |FPHi(+) -FPHi(-)|.
       Calculated anomalous difference is 2 * FHi * sin(PHIx) where PHIx
       is the protein phase.
       Lack of closure is | Anom.Diff - Calc.Anom.Diff|.
       Cullis R factor is <Lack_of_closure>/ <Anomalous difference>. This
       is tabulated for acentric terms. Any value <1.0 means there is
       some contribution to the phasing from the anomalous data.
       The table gives:
          <4SSQ/LL>  range
          Resolution (Angstroms)
          Number of reflections                  (acentrics)
          Mean or rms anomalous difference       (acentrics)
          Mean or rms calculated anomalous difference     (acentrics)
          Mean or rms lack of closure            (acentrics)
          Cullis R factor                        (acentrics)
   vi. Table of estimated error in the isomorphous and anomalous
       differences. These are the values to enter with keywords ISOERROR
       and ANOERROR.
   vii. Table of figure of merit as a function of resolution. The table
       gives:
          <4SSQ/LL>  range
          Resolution (Angstroms)
          Number of reflections                  (acentrics)
          Mean figure of merit                   (acentrics)

          Number of reflections                  (centrics)
          Mean figure of merit                   (centrics)
   viii. The refinement parameter
   ix. If anomalous data are being used for the compound then the
       anomalous refinement parameter is given.
       
ERRORS DURING PHASE CALCULATION

   If the lack of closure is very bad and the phase is virtually
   undetermined, the following error message is output, and the program
   continues.
   
     Reflection HKL: 0 4 1 has inconsistent phase likelihood, log Pmax=
     0.13E+05
     
ERRORS DURING MATRIX SOLUTION

   If there are problems in solving the matrix for the refinement of the
   heavy atom parameters then the following message may be printed and
   the program will stop. This often means occupancies have become 0.00.
   Trying to refine coordinates for a site at a special position can also
   give this error.
   
     **** IN SUBROUTINE MATSOL DET IS LESS THAN 10E-30 ****
     
CAVEAT

   Note the comment above about errors during matrix solution when trying
   to refine coordinates for a site at a special position. In certain
   cases, this might not cause an error per se, but simply yield
   less-than-perfect occupancies etc. Check that the fixed parameters for
   the special position are NOT refined!
   
SEE ALSO

   VECREF - vector-space refinement of heavy atom sites
   
EXAMPLES

  Example 1
  
  Simple unix example script found in $CEXAM/unix/runnable/
  
     mlphare.exam (heavy atom refinement and phasing).
   
   (A vms version found in $CEXAM/vms/mlphare.com)
   
  Also found combined with other programs in the example scripts
  ($CEXAM/unix/runnable/)
  
     phistats.exam (phase analysis)
   
     mir_steps (heavy atom refinement and phasing)