MTZLIB (CCP4: Library)

NAME

   mtzlib - Subroutine Library for Reflection data file handling

CONTENTS

    1. DESCRIPTION
    2. THE MTZ FILE FORMAT
    3. IMPLEMENTING MTZ FILES
    4. STORAGE OF DATA ITEMS
    5. STANDARD ITEM NAMES
    6. COLUMN TYPES
    7. DATASETS
    8. SUBROUTINES IN MTZLIB
    9. MTZ INTERNAL COMMON BLOCKS
   10. C INTERFACE
   11. EXAMPLE PROGRAM USING AN MTZ FILE
   12. AUTHORS AND HISTORY

DESCRIPTION The library mtzlib contains subroutines used for reading, writing
and handling the CCP4 reflection data files.

All the routines contained in this library are written in ANSI standard FORTRAN
77.

The first argument to all the subroutine calls in MTZLIB is MINDX. This
mechanism allows more than one pair of MTZ files to be open for read and write
at the same time, without the need for separate subroutines. At present a
maximum of 8 files can be opened simultaneously (4 for read and 4 for write),
but this could be increased easily.

The subroutines of a set share an area of storage for the header data (e.g. for
the cell parameters, label and title information) so that when an input file
has been opened the header information is available for writing to an output
file, without being explicitly copied by the calling program. This information
may be replaced or new information may be added depending on the requirements
of the output file or it may be created if no input file was read.

THE MTZ FILE FORMAT General description

The MTZ reflection file format uses fixed length logical 'records' written in a
byte stream with, in general, four bytes for each data item (REAL*4), with a
minimum of 3 columns and currently a maximum of 200 columns of data per record,
although these limits could easily be increased. Additional information (title,
cell dimensions, column labels, symmetry information, resolution range, history
information and, if necessary, batch titles and orientation data) is contained
in labelled header records. The columns of the reflection data records are
identified by alphanumeric labels held as part of the file header information.
The user relates the item names used by the program to the required data items,
as identified by the labels, by means of assignment statements in the program
control data.

Record Formats

The file contains basically two classes of records - header records and
reflection data records. A standard reflection data file contains the following
items, in the order given, not necessarily all items have to be present:

     * The first 4 bytes should be "MTZ " (if the first 3 characters are
       not "MTZ" then the library will complain that the file is not an
       MTZ file). This is followed by an integer indicating the location
       of the header records (which occur at the end after the
       reflections records). The integer occupies sizeof(int) bytes
       (typically 4).
     * Next is the "machine stamp" held as 4 characters. This encodes the
       number formats of the of the architecture the file was written on.
       (In fact, the machine stamp is positioned 2 words from the start,
       where a word is sizeof(float), i.e. typically 8 bytes in. The
       first 4 half-bytes represent the real, complex, integer and
       character formats, and the last two bytes are currently unused.)
     * Reflection data starting at byte 21:
       Columns of data held as REAL*4
     * A beginning of header record
     * A set of keyworded records containing

   VERS
          Version stamp (Character*10, currently MTZ:V1.1)

   TITLE
          File Title - short identification of file (Character*70)

   NCOL
          number of columns, number of reflections in file, number of
          batches (Integer) if number of batches > 0 this indicates
          multi-record file

   CELL
          Cell Parameters (Real(6))

   SORT
          Sort order of 1st 5 columns in file (Integer(5))

   SYMINF
          Number of Symmetry operations (Integer)
          Number of Primitive operations (Integer)
          Lattice Type (Character*1)
          Space Group Number (Integer)
          Space Group Name (Character*10)
          Point Group Name (Character*6)

   SYMM
          Symmetry operations in international tables style

   RESO
          Minimum (smallest number) and Max (largest number) resolution
          stored as 1/d-squared (Real(2))

   VALM
          Value with which Missing Number Flag is represented.

   COL
          Column Label (Character*30)
          Column Type (Character*1) for each column
          Minimum and Maximum value in each column (Real)
          ID of corresponding dataset (Integer)

   NDIF
          Number of datasets represented in the file.

   PROJECT
          ID of dataset (Integer)
          Project Name (Character*64). Normally one for each structure
          determination.

   CRYSTAL
          ID of dataset (Integer)
          Crystal Name (Character*64). May be several for each structure
          determination, representing the different crystals used.

   DATASET
          ID of dataset (Integer)
          Dataset Name (Character*64). May be several for each structure
          determination, representing the different datasets measured.

   DCELL
          ID of dataset (Integer)
          Cell dimensions (Real) for dataset.

   DWAVEL
          ID of dataset (Integer)
          Wavelength (Real) for dataset.

   BATCH
          Batch Serial Number for each batch present (Integer). This line
          is only present in `multi-record' files.

     * END of main header card
     * Up to 30 Character*80 lines containing history information
     * For multi-record files:
       Batch title (Character*70) and (optionally) orientation data for
       each batch present in the file
     * End of all headers record

   NB: Column Types are an extra check that the user input assignment for
   a requested program label is of the correct type. For a list of all
   column types see section COLUMN TYPES.

   Normally the Miller indices will be held in the first three columns
   though, within the definition of the format, there is no restriction
   on the use of the columns of the reflection data records. However, the
   subroutines which output the MTZ header information in a formatted way
   (e.g. Subroutine LHPRT) presume that the first 3 columns of a standard
   MTZ file are the Miller Indices, and the first 5 columns of a
   multi-record MTZ file are H,K,L,M/ISYM and Batch number.

IMPLEMENTING MTZ FILES Source file mtzlib.f contains all the subroutines. These
are included in the CCP4 library. It requires subroutines from the library
modules `symlib', `diskio', `parser'. STORAGE OF DATA ITEMS This section
describes the way in which some standard data items are stored in an MTZ file.

   Item
          Storage

   h,k,l
          The Miller indices are held as REAL*4

   Structure Factors
          The structure factor magnitude is held as a REAL*4

   Phases
          Phases are held as REAL*4 values in degrees.

   S
          There is no need for an S column in MTZ files - values of (4
          sin**2 theta / lambda**2) are calculated and returned, for each
          reflection, by the calls to LRREFF and LRREFL, and the max and
          min values are stored in the header of the MTZ file as REAL*4
          (cf old-LCF as 10000*S as INTEGER*2).

   Centric flag
          0 for centric, 1 for acentric.

   A,B,C,D
          Hendrickson-Lattman coefficients

   Figures of merit
          Figures of merit.

STANDARD ITEM NAMES Standard names are normally used for the following items:

   Name
          Item

   H, K, L
          Miller indices.

   IC
          Centricity flag,0 for centric, 1 for acentric..

   M/ISYM
          Partial flag and symmetry number. 256M+Isym, where M is the
          partiality flag (0 for full, 1 for partial) and the `symmetry
          number' Isym is normally 0 (with F=(F+ - F-)/2 for anomalous
          data with both components measured) but is 1 if F=F+ or 2 for
          F=F-.

   BATCH
          Batch number.

   I
          Intensity.

   I'
          Selected mean intensity.

   SIGI
          sigma(I).

   SIGI'
          sigma(I').

   FRACTIONCALC
          Calculated partial fraction of spot.

   IMEAN
          Mean intensity.

   SIGIMEAN
          sigma(IMEAN). obsolete .IP RATDELSD Agreement factor between
          films in a pack.

   FP
          Native F value.

   FC
          Calculated F.

   FPH<n>
          F value for derivative <n>.

   DP
          Anomalous difference for native data.

   DPH<n>
          Anomalous difference for derivative <n>.

   SIGFP
          sigma(FP).

   SIGDP
          sigma(DP).

   SIGFPH<n>
          sigma(F<n>).

   SIGDPH<n>
          sigma(DEL<n>).

   PHIC
          Calculated Phase.

   PHIM
          Most probable phase.

   PHIB
          Phase.

   FOM
          figure of merit.

   WT
          weight

   HLA,HLB,HLC,HLD
          ABCD H/L coefficients

   FREE
          Free R flag (program label)

   FreeR_flag
          Free R flag (file label)

COLUMN TYPESThe column types are as follows:

   H
          index h,k,l
   J
          intensity
   F
          structure amplitude, F
   D
          anomalous difference
   Q
          standard deviation of J,F,D or other (but see L and M below)
   G
          structure amplitude associated with one member of an hkl -h-k-l
          pair, F(+) or F(-)
   L
          standard deviation of a column of type G
   K
          intensity associated with one member of an hkl -h-k-l pair,
          I(+) or I(-)
   M
          standard deviation of a column of type K
   P
          phase angle in degrees
   W
          weight (of some sort )
   A
          phase probability coefficients (Hendrickson/Lattmann)
   B
          BATCH number
   Y
          M/ISYM, packed partial/reject flag and symmetry number
   I
          any other integer
   R
          any other real

DATASETS An MTZ file can contain many columns of data, and these can often be
grouped into distinct "datasets". For example, columns FPH1 SIGFPH1 DPH1
SIGDPH1 for a particular derivative can be considered as part of the same
dataset, and distinct from the equivalent columns for the native which may also
be present in the file.

A dataset is identified by a "project name", which specifies a particular
structure determination (and is equivalent to the mmCIF data item _entry.id),
and a "dataset name", which specifies the particular crystal or derivative (and
is equivalent to the mmCIF data item _diffrn.id). Normally, there will be
several datasets with the same "project name" and different "dataset names".

The total number of datasets represented in a file is given by the keyword NDIF
in the main file header (see above), and a list of the project and dataset
names associated with each dataset is given by the PROJECT and DATASET keywords
also in the main file header. Each dataset is identified internally by an
integer "dataset ID". For a merged single-record-per-reflection MTZ file, each
column has as one of its attributes (included in the COL keyword) a "dataset
ID", which acts as a pointer to the main list of datasets. For unmerged
multi-record MTZ files, a column may be associated with several datasets
(corresponding to different batches) and the "dataset ID" is not used. Instead,
each batch header contains a "dataset ID", which points to the dataset
associated with that batch.

The main file header also contains properties of each dataset. Each dataset can
have its own cell dimensions identified by the keyword DCELL, e.g. native and
derivative crystals may well have significantly different cells. The
information held in DCELL records is distinct from the general cell held in the
CELL record, and programs may make use of either. A wavelength can also be
attributed to each dataset via the keyword DWAVEL. Other dataset information
may be added in the future. The records DCELL and DWAVEL are optional; the
header reading routines assume that if they are present, then they will occur
immediately after the relevant PROJECT and DATASET keywords.

In mtzlib, the COMMON blocks /HARINT/, /HARREA/ and /HARCHA/ include 8
variables or arrays for each file or file pair opened. NSETW is the number of
datasets, read from the file header keyword NDIF. ENTRY_ID, DIFFRN_ID and
SET_ID are the "project name", "dataset name" and "dataset ID" for each
dataset, read from the PROJECT and DATASET file keywords. CSET_ID is the
dataset pointer for each column read from the COLU file keyword. (The
corresponding dataset pointer for batches is held as the variable LBSETID in
the COMMON block for that batch.) DCELL and DWAVEL hold the dataset cell and
wavelength information. Finally, IDEFSET is a default dataset ID for each file,
which is used for associating a dataset with a new column when there is no
other information available.

  Future developments

In future, it is planned to work within a hierarchical data model for
reflection data. The hierarchy is crystal/dataset/[datalist]/column. The
project name will be an attribute of the crystal, and will be used principally
for data harvesting. This hierarchy is represented in the MTZ file by the
existing PROJECT and DATASET keywords, together with a new CRYSTAL keyword.

The new hierarchy will be fully supported in the forthcoming C-language
libraries. Meanwhile, there is partial support in MTZLIB, see the LRIDX and
LWIDX keywords. However, no programs currently make use of these routines.

SUBROUTINES IN MTZLIB The following subroutines are available.

  The initialisation routine for the file handling system

   MTZINI
          This MUST be called first

  Subroutines for reading an MTZ file

   LROPEN
          Open MTZ file for read

   LRASSN
          Set up the input column assignments

   LRBATS
          Return the number of batches present and their serial numbers
          from the MTZ header (for multi-record files)

   LRBRES
          Reset batch header reading pointer

   LRCELL
          Return the Cell dimensions from the MTZ header

   LRCLAB
          Return the Column labels and types from the MTZ header

   LRHIST
          Returns history information from the MTZ header

   LRINFO
          Return general info (number of columns etc.) from the MTZ
          header

   LRNCOL
          Returns number of columns from the MTZ header

   LRRSOL
          Return the minimum and maximum resolution from the MTZ header
          (1/d**2)

   LRSORT
          Return the sort order from the MTZ header

   LRSYMI
          Return symmetry information (if available) from the MTZ header

   LRSYMM
          Return symmetry operations (if available) from the MTZ header

   LRTITL
          Return the title from the MTZ header

   LRREFL
          Read a reflection record in file order from the MTZ file

   LRREFF
          Read a reflection record in Lookup order from the MTZ file

   LRNREF
          Return the number of the reflection record last read (i.e. the
          current position in the file)

   LRSEEK
          Move to a specific reflection record number

   LRREWD
          Rewind an MTZ file for re-read

   LRCLOS
          Close an MTZ file which has been opened for read

  Subroutines for writing an MTZ file

   LWOPEN
          Open MTZ file for write

   LWASSN
          Set up the output column assignments, new columns etc.

   LWCELL
          Update the Cell dimensions in the MTZ header

   LWCLAB
          Write Column labels and types to an output MTZ file

   LWHIST
          Append to the history information in the MTZ header

   LWHSTL
          Simple way of appending standard history line

   LWSORT
          Update the Sort order in the MTZ header

   LWSYMM
          Update the Symmetry operation in the MTZ header

   LWTITL
          Append to or replace the title in the MTZ header

   LWREFL
          Write a reflection record to the MTZ file

   LWCLOS
          Close an MTZ file which has been opened for write

  Subroutines for multi-record MTZ files

   LRBAT
          Return batch information from the header for one batch

   LWBAT
          Write updated batch header for one batch

   LRBSCL
          Return selected values from the header for one batch

   LRBTIT
          Return the batch title from the header for one batch

   LWBTIT
          Write batch title and dummy orientation block for one batch

   LWBSCL
          Update selected values in the header for one batch

   LBPRT
          Print batch information in pretty format - called by LRBAT -
          calls LBPRTH (does the actual print)

  Subroutines for handling Missing Number Flags

   EQUAL_MAGIC 
          Initialises an array so all elements are set to MNF

   IS_MAGIC 
          Routine that checks any datum to see if datum=MNF

   RESET_MAGIC 
          Alters the MNF per reflection in the data itself

   SET_MAGIC 
          Either returns the value of MNF in the MTZ header or overwrites
          it.

   LRREFM 
          Returns a logical array identifying which data of a
          reflection=MNF

  Subroutines for handling Project Name and Dataset Name

   LRIDX 
          Subroutine to return information for all datasets from the MTZ
          file header, including crystal names.

   LRIDC 
          Subroutine to return information for all datasets from the MTZ
          file header.

   LRID 
          As LRIDC, but without cell and wavelength information (for
          backwards compatbility).

   LWIDX 
          Subroutine to add dataset information to the output MTZ file
          header, including crystal names.

   LWIDC 
          Subroutine to add dataset information to the output MTZ file
          header.

   LWID 
          As LWIDC, but without cell and wavelength information (for
          backwards compatbility).

   LRCLID 
          Subroutine to return the ID of the related dataset for each
          column of the input MTZ file, as obtained from the header.

   LWIDAS 
          Subroutine to associate dataset entry with each column for the
          output MTZ file.

   LRBSETID 
          Subroutine to read dataset ID for batch BATNO from batch
          headers for multi-record file open on index MINDX.

   LWBSETID 
          Subroutine to write dataset ID for batch BATNO to batch headers
          for multi-record file open on index MINDX.

  Utility subroutines

   LKYIN
          Used to parse any label assignments (input and output) made by
          the user

   LKYSET
          Similar to LKYIN except the lookup array is passed back to the
          program

   LKYOUT
          parse any label assignments (input and output) made by the user

   LKYASN
          Jiffy to call LKYIN and LRASSN, no need for parser in main
          program

   LHPRT
          Subroutine to output data from an MTZ header

   LPHIST
          Prints history information from the MTZ header

  Internal routines

   There are 13 more subroutines which are internal to the package and
   are included here for completeness, but should not be called by the
   user program:

   RBATHD
          read the actual header from the file and return the data items
          packed into a REAL and a CHAR array - called by LROPEN

   WBATHD
          write the batch headers to the MTZ file open for write the
          batch headers are written at the end of the file - called by
          LWCLOS

   LRHDRL
          read one line from the header on the file (calls qread)

   LBPRTH
          does the actual printing for LBPRT

   LABPRT
          Subroutine used to output character strings (e.g. column
          labels) nicely across 80 character page

   SORTUP
          INTEGER version of indexed Singleton sort - copied from STILLS
          program.

   ADDLIN
          Subroutine to add a new line to a character array

   NEXTLN
          Function to find the next empty line in a character array

   LSTRSL
          Routine to calculate coefficients for (sin(theta)/lambda)**2
          from h,k,l for general axes

   LSTLSQ
          Function to calculate (sin(theta)/lambda)**2 from h,k,l
          coefficients set by call to LSTRSL, for the file open on index
          MINDX

Subroutine MTZINI

   This Subroutine initialises the MTZ file handling system.

   This subroutine must be called before any other mtzlib subroutine.
   Failure to do so may result in unpredictable behaviour.

Subroutine LROPEN(MINDX,FILNAM,IPRINT,IFAIL)

   Subroutine to open an MTZ file for read. This should be the first MTZ
   subroutine called in a set of operations on a pair of files (i.e. one
   input and one output). The subroutine zeros all the Header COMMON
   block entries, opens the specified file and loads the header into the
   COMMONs, and positions the file ready to read the first data record.

   Arguments:

   MINDX (I) INTEGER
          indicates which MTZ file - one index points to both input and
          output files

   FILNAM (I) CHARACTER*(*)
          name of file to be opened

   IPRINT (I) INTEGER
          print indicator:

   =0
          No MTZ info printed at all

   =1
          Brief header info printed (default)

   =2
          as above plus history info

   =3
          Full header dump; symmetry

          any other value; nothing happens

   IFAIL (O) INTEGER
          error indicator: meaning: on output

   =0
          OK

   =-1
          no such file

   all other errors cause stop

   LROPEN calls the following which are external to MTZLIB:

   External Functions: INTEGER LENSTR
   External Subroutines: BLANK,GTPINT,GTPREA,LERROR,PARSER,PUTLIN,QOPEN,
   QSEEK,QMODE,QREAD,SYMFR3

   Function:

   Subroutine LROPEN checks that nothing is already open for required
   index
   If it is continue, but print warning
   If already open for read, then probably forgot to call LRCLOS from a
   previous file
   If already open for write, then programmer hasn't read manual - ie has
   called LWOPEN on this index before LROPEN
   If already open for read and write then the program stops
   Then opens the file and record the stream
   CALL QOPEN(IUNIN,FILNAM,'READONLY')
   CALL QMODE(IUNIN,2,NITEM)
   Then Zero the header arrays etc.
   Read the 1st record of the file, check it's an MTZ file, and go to the
   start of the header records - first record of file contains the offset
   in the file of the start of the header records. Put this offset into a
   call to QSEEK ( CALL QSEEK(RLUN(INDEX),1,HDRST(INDEX),1)) to position
   file at start of headers.
   Then reads and parses the header, and load COMMON blocks
   Passing header line to MRC parser:
   CALL PARSER(KEY,LINE,IBEG,IEND,ITYP,FVALUE,CVALUE,
   + IDEC,NTOK,LEND,.FALSE.)
   and loops over possible keywords


VERS - version of routines which wrote the file
       could test versions here in the future
TITL - read file title
NCOL - no. of cols and refls in file and batches in file
       if no. of batches=0 then this is a standard file
CELL - read in the Cell parameters
SORT - read in sort order
SYMI - various symmetry stuff
SYMM - read in the symmetry cards and convert to matrices
       If present then calls SYMFR3
RESO - resolution limits for the file (1/d-squared)
COLU - column labels, types and ranges
BATC - batch serial numbers - hopefully only if nbatch >0
END    of header card

   Ignores unrecognised lines.
   If end of header reached, but no END card, print warning
   Check no. of column cards input equals NCOLS from 1st line
   Check correct number of symmetry cards
   If NBATCH>0 prepare to read the batch headers
   Loop over the rest of the header lines looking for MTZHIST or MTZBATS
   as keyword, and proceed accordingly.
   Finally, hopefully hit the MTZENDOFHEADERS line.
   Output information with CALL LHPRT(INDEX,IPRINT,IFAIL) (if IPRINT>0)
   Finally positions the file ready to read reflection records with
   CALL QSEEK(RLUN(INDEX),1,SIZE1+1,1),
   where SIZE1 is the size of the first record in the file (which
   contained the offset).

Subroutine LRASSN(MINDX,LSPRGI,NLPRGI,LOOKUP,CTPRGI)

   Subroutine to apply the input column label assignments to the MTZ file
   which is open for read and setup the Lookup pointer array

   If the program is going to allow user input column assignments, then
   you MUST call subroutine LKYIN to parse these input label assignments,
   before LRASSN is called, as LKYIN sets up arrays which are then used
   by LRASSN.

   Note that user input labels and file labels are case sensitive - the
   input label must match the file label exactly.

   Also note that having an unassigned program label is a fatal error,
   but this subroutine uses LERROR to report this as a warning, so that
   all the program label assignments can be checked before stopping.

   Arguments:

   MINDX (I) INTEGER
          indicates which MTZ file - one index points to both input and
          output files

   LSPRGI (I) CHARACTER*30
          array of dimension at least NLPRGI containing the program label
          strings

   NLPRGI (I) INTEGER
          number of input program labels

   LOOKUP (I/O) INTEGER
          array of dimension at least NLPRGI containing index from
          program labels to file labels. On input these should be set to
          -1 for compulsory labels, 1 for soft compulsory labels and 0
          for optional labels, and on exit labels which are not present
          in the file have their lookup entry set to 0. Both types of
          compulsory label will be assigned automatically if the
          LSPRGI=MTZfile_label, so this status should be used carefully.
          If they are assigned explicitly (typically in the LABIN
          keyword) this overrides the above assignment. For compulsory
          labels (lookup=-1) it is an error if the labels are not
          assigned in the calling program. For soft compulsory and
          optional labels no error is given if they are not assigned to a
          column in the MTZ file.

   CTPRGI (I) CHARACTER*1
          array of dimension at least NLPRGI containing the program label
          types

   LRASSN calls the following which are external to MTZLIB:

   External Functions: INTEGER LENSTR
   External Subroutines: BLANK,LERROR,PUTLIN

   Function:

   This subroutine references the internal COMMON Blocks /MTZLBC/ and
   /MTZLAB/ which are set up by LKYIN.
   Rpoint is the same as lookup, but held in the MTZWRK COMMON work with
   this and copy to LOOKUP at the end, so set to 0.
   Also store the number of program labels in MTZWRK, and the program
   labels in MTZWRC
   First loop over user input labels (if any) and assign them to file
   labels.
   Now loop over program labels for those not yet assigned
   Copy RPOINT to LOOKUP
   If we had some errors then return or stop now
   Print out program labels, column labels and lookup
   Check the column types if any given

Subroutine LRBATS(MINDX,NBATX,BATCHX)

   Return the number of batches and their batch serial numbers from the
   header of a multi-record MTZ file

   Arguments:

   MINDX (I) INTEGER
          indicates which MTZ file - one index points to both input and
          output files

   NBATX (I/O) INTEGER
          On input, dimension of BATCHX; on exit number of batches in the
          file.

   BATCHX (O) INTEGER
          array of dimension at least NBATX containing the serial numbers
          of the batches in the file

   LRBATS calls the following which are external to MTZLIB:

   External Subroutines: LERROR

Subroutine LRBRES (MINDX,BATNO)

   Reset the batch header info pointer to the batch BATNO, for re-read by
   subroutine LRBAT, for an MTZ file which has been opened for read on
   index MINDX.

   Arguments:

   MINDX (I) INTEGER
          indicates which MTZ file - one index points to both input and
          output files

   BATNO (I) INTEGER
          batch number to reset pointer to If BATNO = 0, reset to
          beginning of batch headers.

   LRBRES calls the following which are external to MTZLIB:

   External Subroutines: LERROR

Subroutine LRCELL(MINDX,CELLP)

   Return Cell Parameters from header of MTZ file open for read on index
   MINDX

   Arguments:

   MINDX (I) INTEGER
          indicates which MTZ file - one index points to both input and
          output files

   CELLP (O) REAL(6)
          array of dimension (6) containing cell parameters from header
          on exit

   LRCELL calls the following which are external to MTZLIB:
   External Subroutines: LERROR

Subroutine LRCLAB(MINDX,CLABS,CTYPS,NCOL)

   Return the column labels, column types and number of columns from the
   header of an MTZ file.

   Arguments:

   MINDX (I) INTEGER
          indicates which MTZ file - one index points to both input and
          output files

   CLABS (O) CHARACTER*30
          array of dimension at least NCOL containing the column labels
          on exit

   CTYPS (O) CHARACTER*1
          array of dimension at least NCOL containing the column types on
          exit

   NCOL (I/O) INTEGER
          On entry the dimension of CLABS and CTYPS; on exit the number
          of columns in the MTZ file

   LRCLAB calls the following which are external to MTZLIB:

   External Functions : INTEGER LENSTR
   External Subroutines: LERROR

Subroutine LRHIST(MINDX,HSTRNG,NLINES)

   Return the history information from the MTZ file header.

   Arguments:

   MINDX (I) INTEGER
          indicates which MTZ file - one index points to both input and
          output files

   HSTRNG (O) CHARACTER*(*)
          array of (NLINES) with the history lines

   NLINES (I/O) INTEGER
          On entry the dimension of HSTRNG; on exit the number of history
          lines being returned

   LRHIST calls the following which are external to MTZLIB:

   External Functions: INTEGER LENSTR
   External Subroutines: LERROR

Subroutine LRINFO(MINDX,VERSNX,NCOLX,NREFLX,RANGES)

   Return information about the MTZ file open for read on index MINDX.

   Arguments:

   MINDX (I) INTEGER
          indicates which MTZ file - one index points to both input and
          output files

   VERSNX (O) CHARACTER*10
          version stamp of MTZ subroutines used to write the file

   NCOLX (I/O) INTEGER
          On entry, the last dimension of RANGES; on exit the number of
          columns in the file

   NREFLX (O) INTEGER
          number of reflection records in the file

   RANGES (O) REAL
          array(2,NCOLX) containing the minimum and maximum values in
          each column

   LRINFO calls the following which are external to MTZLIB:
   External Subroutines: LERROR

Subroutine LRNCOL(MINDX,NCOLX)

   Return the number of columns in the MTZ file open for read on index
   MINDX. A simpler call than LRINFO.

   Arguments:

   MINDX (I) INTEGER
          indicates which MTZ file - one index points to both input and
          output files

   NCOLX (O) INTEGER
          number of columns in MTZ file

   LRNCOL calls the following which are external to MTZLIB:
   External Subroutines: LERROR

Subroutine LRNREF(MINDX,REFNUM)

   Return the current reflection number from an MTZ file opened for read.
   Files are normally read sequentially. The number returned is the
   number of the *NEXT* reflection record to be read. If you are going to
   jump about the file with LRSEEK then use this to record the current
   position before you start, so that it can be restored afterwards, if
   required.

   Arguments:

   MINDX (I) INTEGER
          indicates which MTZ file (up to MFILES possible open at once)

   REFNUM (O) INTEGER
          the reflection record number of the next reflection to be read

   LRNREF calls the following which are external to MTZLIB:
   External Subroutines: LERROR

Subroutine LRREFF(MINDX,RESOL,ADATA,EOF)

   Subroutine to read a reflection record from an MTZ file which has been
   opened for read. This returns the record in `lookup' order (as set by
   LRASSN). The subroutine also returns the resolution (1/d**2). This
   resolution calculation only works if there are at least 3 columns in
   the file and the first 3 have type H, which is the normal case, if not
   then the RESOL value is set to -1.0.

   NB: Since the calculation for the resolution is set up when the file
   is opened (LROPEN) any changes to the unit cell should be made (with
   LWCELL, where the setup is re-done) BEFORE reflections are read if it
   is wished that the new cell is used in the resolution calculation.

   There is a kluge to handle the absence flags defined by the Groningen
   BIOMOL system: If the MINDX is larger then 1000, then it is assumed
   that the subroutine is called by a BIOMOL program or another program
   that is able to interpret the BIOMOL absence flags (e.g. a value of
   -1.0E+10 indicates absent data). If MINDX is in the normal range of 1
   to 3, then the subroutine will convert values of -1.0E+10 to zero to
   allow normal processing by the CCP4 programs.

   Arguments:

   MINDX (I) INTEGER indicates which MTZ file - one index points to both
   input and output files

   RESOL (O) REAL
          resolution (4 * sin**theta/lambda**2). If the first three
          columns are not of type H, this value has no meaning and is
          -1.0.

   ADATA (O) REAL
          array of dimension at least NPLABS(MINDX) containing the
          reflection record on exit in lookup order

   EOF (O) LOGICAL
          End-of-File indicator

   LRREFF calls the following which are external to MTZLIB:

   External Subroutines: LERROR,QREAD

   Function:

   Check that there is a file open
   Everything OK, update the number of records read
   If not end of file read a record with
   CALL QREAD(RLUN(INDEX),BDATA,NCOLS(INDEX),IERR)
   and rearrange it
   Check first 3 columns are of type H and if so calculate the
   resolution. Transfer data to ADATA in LOOKUP order, if LOOKUP(?) is 0
   then presume it was an optional column and set ADATA(?) to 0.0

Subroutine LRREFL(MINDX,RESOL,ADATA,EOF)

   Read a reflection record from an MTZ file which has been opened for
   read. This returns the record in `file' order - the physical order of
   columns in the file rather than the `lookup' order, c.f. LRREFF.
   Otherwise the same as LRREFF.

   LRREFL calls the following which are external to MTZLIB:

   External Subroutines: LERROR,QREAD

   Function:

   Check that there is a file open
   Everything OK, update the number of records read
   Check first 3 columns are of type H and if so calculate the resolution
   If not end of file read a record with
   CALL QREAD(RLUN(INDEX),ADATA,NCOLS(INDEX),IERR)
   NB: End of file is no. of refs read > total no.of refs (from header)

Subroutine LRRSOL(MINDX,MINRES,MAXRES)

   Return the resolution range for the reflections in the MTZ file open
   for read on index MINDX. (Resolution is 1/d-squared). The resolution
   limits are calculated when the file is written - no `S' column is
   required in MTZ files. (See also subroutines LRREFF, LRREFL).

   Arguments:

   MINDX (I) INTEGER
          indicates which MTZ file - one index points to both input and
          output files

   MINRES (O) REAL
          minimum resolution for reflections in file (smallest number)

   MAXRES (O) REAL
          maximum resolution for reflections in file (largest number)

   LRRSOL calls the following which are external to MTZLIB:

   External Subroutines: LERROR

Subroutine LRSORT(MINDX,SORTX)

   Return sort order from header of MTZ file

   Arguments:

   MINDX (I) INTEGER
          indicates which MTZ file - one index points to both input and
          output files

   SORTX (O) INTEGER
          array of dimension (5) containing sort order of 1st 5 columns
          in MTZ file, negative numbers for descending order, 0 for not
          sorted

   LRSORT calls the following which are external to MTZLIB:

   External Subroutines: LERROR

Subroutine LRSYMI(MINDX,NSYMPX,LTYPEX,NSPGRX,SPGRNX,PGNAMX)

   Return available symmetry information (other than symmetry operations,
   for which see LRSYMM) from the MTZ header

   Arguments:

   MINDX (I) INTEGER
          indicates which MTZ file - one index points to both input and
          output files

   NSYMPX (O) INTEGER
          number of primitive symmetry operations

   LTYPEX (O) CHARACTER*1
          single character denoting the lattice type (possible values are
          P,A,B,C,I,F,R). Blank if not present in header.

   NSPGRX (O) INTEGER
          space group number, 0 if not present

   SPGRNX (O) CHARACTER*10
          space group name, blank if not present

   PGNAMX (O) CHARACTER*10
          point group name, blank if not present

   LRSYMI calls the following which are external to MTZLIB:

   External Subroutines: LERROR

Subroutine LRSYMM(MINDX,NSYMX,RSYMX)

   Return symmetry operations (if available) from the MTZ header

   Arguments:

   MINDX (I) INTEGER
          indicates which MTZ file - one index points to both input and
          output files

   NSYMX (I/O) INTEGER
          On entry, the last dimension of RSYMX; on exit the total number
          of symmetry operations or 0 if no symmetry information is
          present

   RSYMX (O) REAL
          array of dimensions (4,4,NSYM) of symmetry operations on exit
          (max. NSYM is 192)

   LRSYMM calls the following which are external to MTZLIB:

   External Subroutines : LERROR

Subroutine LRTITL(MINDX,FTITLE,LEN)

   Return the title and it's length from the header of an MTZ file.

   Arguments:

   MINDX (I) INTEGER
          indicates which MTZ file - one index points to both input and
          output files

   FTITLE (O) CHARACTER*(*)
          character string containing the title on output - maximum
          possible length 70

   LEN (O) INTEGER
          length of the title string - i.e. number of characters from
          start to last non-blank character

   LRTITL calls the following which are external to MTZLIB:

   External Subroutines: LERROR
   External Functions : INTEGER LENSTR

Subroutine LRSEEK(MINDX,REFNUM)

   Move to a specific reflection record in an MTZ file opened for read.
   Files are normally read sequentially, so this should be viewed as a
   special case. The file read pointer is positioned so that the next
   record read with a call to LRREFF or LRREFL will be the one requested.

   Arguments:

   MINDX (I) INTEGER
          indicates which MTZ file (up to MFILES possible open at once)

   REFNUM (I) INTEGER
          the reflection record number to which to move in the file

   LRSEEK calls the following which are external to MTZLIB:

   External Subroutines: LERROR, QSEEK

Subroutine LRREWD(MINDX)

   Rewind an MTZ file for re-reading of reflections. The file must
   already have been opened for read with LROPEN. The file is positioned
   at the start of the reflection records.

   Arguments:

   MINDX (I) INTEGER
          indicates which MTZ file - one index points to both input and
          output files

   LRREWD calls the following which are external to MTZLIB:

   External Subroutines: LERROR, QSEEK

Subroutine LRCLOS(MINDX)

   Close an MTZ file which has been opened for read

   Arguments:

   MINDX (I) INTEGER
          indicates which MTZ file - one index points to both input and
          output files

   LRCLOS calls the following which are external to MTZLIB:

   External Subroutines: LERROR,QCLOSE

   Function:

   Close the file with CALL QCLOSE(RLUN(INDEX))

   Mark this index as unoccupied for read

Subroutine LWOPEN(MINDX,FILNAM)

   Open MTZ file for write. This subroutine should be called after the
   corresponding input file has been opened (i.e. after LROPEN has been
   called).

   NB: Every time LROPEN is called it zeros all the header info for that
   MINDX, and then loads up the header storage with data from the file.
   Therefore if LWOPEN is called first, and if (e.g.) a title of a
   history line is added with LWTITL or LWHIST, this info will be lost if
   it is followed by a call to LROPEN (on the same MINDX). While this is
   unlikely to occur in most programs, care should be taken with programs
   which open a large number of input files in sequence and write one
   output file (and therefore have a sequence of calls like - LROPEN,
   LWOPEN, LRREFL, LWREFL, LRCLOS, LROPEN, LRREFL, LWREFL, LRCLOS ...
   LWCLOS) not to update items in the header until the last input file
   has been opened. Alternatively, if you want to retain the data from
   the first input header in the output header, you should open the first
   input file on index 1, and the output file on 1 also, and all
   subsequent input files on index 2.

   Arguments:

   MINDX (I) INTEGER
          indicates which MTZ file - one index points to both input and
          output files

   FILNAM (I) CHARACTER*(*)
          name of file to be opened

   LWOPEN calls the following which are external to MTZLIB:

   External Subroutines: LERROR,QOPEN,QMODE,QWRITE

   Function:

   Explicitly pull in the initialise block data here (EXTERNAL MTZINI)
   Check for other open files on this index - first read files If no read
   file open, then LROPEN has not been called - initialise all the MTZ
   header common blocks here - some of these not necc. if no read file,
   but do it for consistency
   Then the write files - pretty seious if already open, so stop.
   Everything OK, open the file and zero a few variables
   CALL QOPEN(IUNIN,FILNAM,'NEW')
   CALL QMODE(IUNIN,2,NITEM)
   Write a dummy first record to the file (the one which will contain the
   header offset and the machine stamp and mtz stamp)

Subroutine LWASSN(MINDX,LSPRGO,NLPRGO,CTPRGO,IAPPND)

   Setup the column labels and column types for the output MTZ file. This
   allows for the user to have specified output column assignments.

   Note that this subroutine changes the values in the header common
   block, so all information about the input file's labels and types
   should already have been extracted.

   If the program is going to allow user output labels, then the
   subroutine LKYOUT *MUST* be called to parse the output label
   assignments from the input control data, before LWASSN is called.

   Also note that the case of the user and/or program output labels is
   preserved.

   Arguments:

   MINDX (I) INTEGER
          indicates which MTZ file - one index points to both input and
          output files

   LSPRGO (I) CHARACTER*30
          array of dimension at least NLPRGO containing the program
          output labels

   NLPRGO (I) INTEGER
          number of output program labels

   CTPRGO (I) CHARACTER*1
          array of dimension at least NLPRGO containing the output column
          types

   IAPPND (I) INTEGER

   =0
          replace all existing labels and types

   =1
          append to the existing labels and types

   LWASSN calls the following which are external to MTZLIB:

   External Functions : INTEGER LENSTR
   External Subroutines: BLANK,LABPRT,LERROR,PUTLIN

   Function:

   Work out starting column
   Work out total number of columns to be written to output file. Loop
   over the new labels, and check the user assignments - if an output
   program label is the same as an input one, and there is no user output
   assignment then check the input assignments and keep the original user
   label for that column.
   Print out the output program labels and output column label, and an
   output lookup. Then check the column types are valid.

Subroutine LWCELL(MINDX,CELLP)

   Write Cell Parameters into the header common block (to be written to
   the output MTZ file). When this is called the calculation for the
   resolution is re-initialised for the new cell parameters, therefore
   this should be called before any reflections are written to the output
   file (ie before any calls to LWREFL).

   Arguments:

   MINDX (I) INTEGER
          indicates which MTZ file - one index points to both input and
          output files

   CELLP (I) REAL
          array of dimension (6) containing cell parameters to write to
          header

          LWCELL calls the following which are external to MTZLIB:

          External Subroutines: LERROR

Subroutine LWCLAB(MINDX,LSPRGO,NLPRGO,CTPRGO,IAPPND)

   Write the column labels and column types to the header of an output
   MTZ file. This is simpler than LWASSN as it doesn't look for column
   assignments and doesn't check back to the input file at all - so the
   output column labels are exactly what come into this subroutine in
   CLABS, and the case of the labels is preserved.

   Arguments:

   MINDX (I) INTEGER
          indicates which MTZ file - one index points to both input and
          output files

   LSPRGO (I) CHARACTER*30
          array of dimension at least NLPRGO containing the column labels
          on entry

   NLPRGO (I) INTEGER
          number of columns input

   CTPRGO (I) CHARACTER*1
          array of dimension at least NLPRGO containing the column types
          on entry

   IAPPND (I) INTEGER

   =0
          replace all existing labels and types

   =1
          append to the existing labels and types

   LWCLAB calls the following which are external to MTZLIB:
   External Functions : INTEGER LENSTR
   External Subroutines: LERROR

Subroutine LWHIST(MINDX,HSTRNG,NLINES)

   Write new history lines to history header. History headers have a
   maximum of NHISTL lines. We write the new NLINES of history to the
   header and then fill up any free lines with the older lines.

   Arguments:

   MINDX (I) INTEGER
          indicates which MTZ file - one index points to both input and
          output files

   HSTRNG (I) CHARACTER
          array of (NLINES) with the history lines

   NLINES (I) INTEGER
          number of history lines to be written

Subroutine LWHSTL(MINDX,EXTRA)

   Write a single line of hstory information to an MTZ file with index
   MINDX indicating that it was output from the program whose name was
   previously set with CCPVRS (/CCPRCS) at the current date and time.
   EXTRA is more information to append to the record (or blank). An
   example of the information produced might be:
    From FREERFLAG, 21/ 6/94 18:38:48 with fraction 0.050
         ^^^^^^^^^                    ^^^^^^^^^^^^^^^^^^^
         CCPVRS arg                           EXTRA

   This is just a simplified interface to LWHIST. The history line will
   be truncated to 80 characters.

   Arguments:

   MINDX (I) INTEGER
          indicates which MTZ file - one index points to both input and
          output files

   EXTRA (I) CHARACTER*(*)
          Extra information to print

   LWHIST calls the following which are external to MTZLIB:
   External Subroutines: LERROR

   Function:

   Check not too many lines input - if so take first NHISTL lines
   Copy existing history lines to scratch array
   Copy input lines to the history array in the header common blocks
   Fill up any space left with lines already in history header

Subroutine LWSORT(MINDX,SORTX)

   Write the sort order of the output file to the MTZ header.

   Arguments:

   MINDX (I) INTEGER
          indicates which MTZ file - one index points to both input and
          output files

   SORTX (I) INTEGER
          array of dimension (5) containing sort order of 1st 5 columns
          in MTZ file negative numbers for descending order 0 for not
          sorted

   LWSORT calls the following which are external to MTZLIB:

   External Subroutines: LERROR

Subroutine LWSYMM(MINDX,NSYMX,NSYMPX,RSYMX,LTYPEX,NSPGRX,SPGRNX,PGNAMX)

   Update the symmetry operations and information in the MTZ header.

   Arguments:

   MINDX (I) INTEGER
          indicates which MTZ file - one index points to both input and
          output files

   NSYMX (I) INTEGER
          total number of symmetry operations. If this is 0 then the
          symmetry operation values are not changed

   NSYMPX (I) INTEGER
          number of primitive operations

   RSYMX (I) REAL
          array of dimensions (4,4,192) of symmetry operations on entry

   LTYPEX (I) CHARACTER*1
          single character denoting the lattice type (possible values are
          P,A,B,C,I,F,R) if blank then current value not changed

   NSPGRX (I) INTEGER
          space group number, if 0 not changed

   SPGRNX (I) CHARACTER*10
          space group name, if blank not changed

   PGNAMX (I) CHARACTER*10
          point group name, if blank not changed

   LWSYMM calls the following which are external to MTZLIB:

   External Subroutines: LERROR,PUTLIN

   Function:

   First deal with symmetry operations - if NSYMX .gt. 0 ie there is
   already symmetry info there, print warning with
   CALL SYMTR3(NSYM(INDEX),RSYM(1,1,1,INDEX),SYMCHS,IPRINT) and
   CALL SYMTR3(NSYMX,RSYMX(1,1,1),SYMCHS,IPRINT)
   but copy the new ones into the header blocks anyway. Then deal with
   the other arguments.

Subroutine LWTITL(MINDX,NTITLE,FLAG)

   Update the title of an MTZ file in the header common block.

   Arguments:

   MINDX (I) INTEGER
          indicates which MTZ file - one index points to both input and
          output files

   NTITLE (I) CHARACTER*(*)
          character string containing the title - maximum possible length
          70

   FLAG (I) INTEGER

   =0
          replace old title with new one

   =1
          append new one to old, with one space

   LWTITL calls the following which are external to MTZLIB:

   External Functions : INTEGER LENSTR
   External Subroutines: LERROR

Subroutine LWREFL(MINDX,ADATA)

   Write a reflection record to an MTZ file which has been opened for
   write. Also output column labels etc. should already have been setup
   using LWASSN.

   Arguments:

   MINDX (I) INTEGER
          indicates which MTZ file - one index points to both input and
          output files

   ADATA (I) REAL
          array of dimension at least NCOLW(MINDX) containing the
          reflection record

   LWREFL calls the following which are external to MTZLIB:

   External Subroutines: LERROR,QWRITE
   External Functions : REAL LSTLSQ

   Function:

   Check that there is a file open. If everything OK, increment no. of
   reflection records written.
   Update the column ranges
   Update the resolution limits
   Write the reflection record to file with
   CALL QWRITE(WLUN(INDEX),ADATA,NCOLW(INDEX))

Subroutine LWCLOS(MINDX,IPRINT)

   Close an MTZ file which has been opened for write. The new header
   information should already have been supplied by calls to other LW*
   routines. This subroutine writes the MTZ header and its associated
   history header to the output file, writes a pointer to the headers in
   the first record of the file, and a machine stamp and closes the file.
   The headers are actually written at the end of the file.

   This is one of the most important subroutines in the library. If you
   do not call this subroutine your output file will be corrupted; it
   will have no header information and the file will be unreadable.

   Arguments:

   MINDX (I) INTEGER
          indicates which MTZ file (up to MFILES possible open at once)

   IPRINT (I) INTEGER
          print indicator: meaning:

   =0
          No MTZ info printed at all

   =1
          Brief header info printed (normal)

   =2
          Brief header plus history

   =3
          Full header dump

   LWCLOS calls the following which are external to MTZLIB:

   External Functions : INTEGER LENSTR
   External Subroutines:
   BLANK,LERROR,PUTLIN,QCLOSE,QSEEK,QWRITE,QMODE,QTYPE

   Function:

   Calculate position of start of header records, and move to it -
   =no.refls*no.cols+size of 1st record + 1
   Loop over the header lines and write them out (see LROPEN for a list
   of the possible header lines) If it is a multi-record file, and if we
   found that when we were writing the batches out to the file, the
   batches were out of order (ie serial numbers not in ascending order),
   then do an indexed sort of the array containing the batch serial
   numbers, so that they, and the batch information (title and
   orientation data), can be output serially. (NB the batch header info
   is never read at the same time as the corresponding reflection
   records, as it was in the LCF files - all batch headers are read as
   soon as the file is opened)
   Then write the history lines and then the batch info if a multi-record
   file.
   Write MTZENDOFHEADERS record (which is also end of file).
   Go back to the beginning and fill up the first record with an
   identification stamp and the offset of the headers. (ie the offset of
   the headers is the second long-word in the file)
   If IPRINT is gt 0 then call LHPRT to output header information.
   Close the file - CALL QCLOSE(WLUN(INDEX)) and mark the index available
   for write by setting WLUN(INDEX) to 0.

Subroutine LRBAT(MINDX,BATNO,RBATCH,CBATCH,IPRINT)

   Return the header info for the next batch from the multi-record MTZ
   file (or pair of files) open on index MINDX, and the information in
   the two arrays RBATCH (for numbers) and CBATCH (for characters).

   This will also optionally print out all this information in a pretty
   format.

   Note that the maximum numbers of batches currently allowed is 1000.

   Arguments:

   MINDX (I) INTEGER
          indicates which MTZ file - one index points to both input and
          output files

   BATNO (O) INTEGER
          serial number of this batch, returned as -1 if all batch
          headers have been read

   RBATCH (O) REAL(*)
          array into which integer and real batch information is stored
          by subroutine rbathd this should be equivalenced onto the
          appropriate COMMON block in the calling program. The first item
          is Nwords, i.e. how many items in the array: Nwords = 0 if no
          orientation data are present in the batch header

   CBATCH (O) CHARACTER(*)*1
          as RBATCH, but for character items - no nwords however

   IPRINT (I) INTEGER
          print indicator

   =0
          no print

   =1
          print batch title only

   =2
          print orientation block as well

   >30
          print orientation block as well BUT to IPRINT unit number

   LRBAT calls the following which are external to MTZLIB:

   External Subroutines: LERROR

Subroutine LWBAT(MINDX,BATNO,RBATCH,CBATCH)

   Write the header for batch with serial number BATNO to the MTZ file
   open for write on index MINDX, batch info stored in the two arrays
   RBATCH (for numbers) and CBATCH (for characters).

   If this routine is called at all then it must be called for every
   batch which is to be output - these batch serial numbers are stored
   and used in LWCLOS.

   If it is called with BATNO = 0 this is a flag to say that the output
   MTZ file will be a standard file, and not a multi-record one, i.e. no
   batches. After this call no batch information is available to the
   calling program, so don't call it too soon !

   Note that the maximum numbers of batches currently allowed is 1000.

   Arguments:

   MINDX (I) INTEGER
          indicates which MTZ file - one index points to both input and
          output files

   BATNO (I) INTEGER
          serial number of this batch if 0 wipe away all batch info for
          file

   RBATCH (I) REAL(*)
          array from which integer and real batch info is decoded by
          subroutine WBATHD this should be equivalenced onto the
          appropriate COMMON block in the calling program. The first item
          is NWORDS, i.e. how many items in the array. If NWORDS is 0
          then only the title is written to header

   CBATCH (I) CHARACTER(*)*1
          as RBATCH, but for character items - no nwords however; title
          is 1st 70 chars of CBATCH.

   LWBAT calls the following which are external to MTZLIB:

   External Subroutines: LERROR

   Function:

   This subroutine will check whether the number of the current batch
   which is being written is (1) already present in the output file (ie
   LWBAT has already been called with this batch number) and (2) less
   than the serial number of the last batch written (ie the serial
   numbers are out of order). If 2 batches are the same the program will
   stop, and if the serial numbers are out of order a flag is set so that
   they will be sorted by LWCLOS before being written out to the file.

Subroutine LRBSCL (MINDX,BATNO,BATSCL,NBATSC)

   Read batch scale, Bfactor and batch title for batch BATNO from batch
   headers from multi-record file open on index MINDX

   MINDX (I) INTEGER
          indicates which MTZ file - one index points to both input and
          output files

   BATNO (I) INTEGER
          batch number

   NBATSC (I) INTEGER
          maximum number of batch scales expected

   BATSCL (O) REAL
          array of dimension at least NBATSC containing batch scale,
          relative Bfactor, SD(Bscale), SD(Bfactor) if NBATSC = 4 else
          NBATSC/2 scales or B-factors + Sd's on output

   NBATSC (I/O) INTEGER
          On entry the dimension of BATSCL; on exit the number of batch
          scales found

   LRBSCL calls the following which are external to MTZLIB:
   External Subroutines: LERROR

Subroutine LRBTIT (MINDX,BATNO,TBATCH,IPRINT)

   Read batch title for batch BATNO from batch headers from multi-record
   mtz file open on index MINDX

   Arguments:

   MINDX (I) INTEGER
          indicates which MTZ file - one index points to both input and
          output files

   BATNO (I) INTEGER
          batch number

   TBATCH (O) CHARACTER
          batch title

   IPRINT (I) INTEGER
          print flag

   =0
          no print

   =1
          print title

   =2
          print title and orientation block

Subroutine LWBTIT (MINDX,BATNO,TBATCH)

   Write batch title and dummy orientation block for batch BATNO to
   multi-record file open on index MINDX

   Arguments:

   MINDX (I) INTEGER
          indicates which MTZ file - one index points to both input and
          output files

   BATNO (I) INTEGER
          batch number

   TBATCH (I) CHARACTER
          batch title

Subroutine LWBSCL(MINDX,BATNO,BATSCL,NBATSC)

   Write batch scale and Bfactor for batch BATNO to batch headers for
   multi-record file open on index MINDX

   Arguments:

   MINDX (I) INTEGER
          indicates which MTZ file - one index points to both input and
          output files

   BATNO (I) INTEGER
          batch number

   BATSCL (I) REAL
          batch scale, relative Bfactor, SD(Bscale), SD(Bfactor) if
          NBATSC = 4 else NBATSC/2 scales or B-factors + Sd's

   NBATSC (I) INTEGER
          number of batch scales (=0 to clear)

Subroutine LBPRT(IBATCH,IPRINT,RBATCH,CBATCH)

   Internal MTZ subroutine which copies the batch header information as
   it is stored in raw form on the files, into the common blocks MBTHDR
   and CBTHDR, and then calls LBPRTH to make some sense of these numbers.

   Arguments:

   IBATCH (I) INTEGER
          batch number

   IPRINT (I) INTEGER
          print indicator: meaning:

   =0
          no print

   =1
          print batch title only

   =2
          also print orientation block

   >30
          also print orientation block BUT to IPRINT unit number

   RBATCH (I) REAL(*)
          array from which integer and real batch info is decoded by
          subroutine WBATHD. This should be equivalenced onto the
          appropriate COMMON block in the calling program. The first item
          is NWORDS, i.e. how many items in the array. If NWORDS is 0
          then only the title is written to header.

   CBATCH (I) CHARACTER(*)*1
          as RBATCH, but for character items - no nwords however; title
          is 1st 70 chars of CBATCH.

          LBPRT is called by LRBAT, and it calls LBPRTH to do the actual
          printing.

SUBROUTINE EQUAL_MAGIC(MINDX,ADATA,NCOL)

   Sets an array of NCOL to VAL_MISS(2,MINDX), the appropriate value for
   the output file.

   Arguments :

   MINDX (I) INTEGER
          indicates which MTZ file - 1 index points to both input and
          output files

   ADATA (I) REAL
          array of dimension at least NCOL containing the reflection
          record with "missing" values set to VAL_MAGICA

   NCOL (I) INTEGER
          Array size of ADATA

SUBROUTINE IS_MAGIC (VAL_MAGIC,VALTST,LVALMS)

   Function to test whether a number is "magic". Returns LVALMS TRUE if
   it is - otherwise LVALMS FALSE.

   Arguments :

   VAL_MAGIC (I) REAL
          Missing value flag as "magic" for this mtz file.

   VALTST (I) REAL
          Number to test to see if it is defined as "magic" for this mtz
          file.

   LVALMS (O) LOGICAL
          Returns LVALMS TRUE if VALTST is "magic", FALSE if it is not,
          or if there is no "missing" number set.

SUBROUTINE RESET_MAGIC(MINDX,ADATA,BDATA,NCOL,VAL_MAGICA,VAL_MAGICB)

   Resets an array containing Missing value flags VAL_MAGICA to one
   containing Missing value flags VAL_MAGICB If MINDX > 0 then VAL_MAGICA
   is taken to be the value of the MNF stored in the MTZ header, for MTZ
   file MINDX. Else the passed value is taken. The MNF pertaining to the
   data need not necessarily be the same as that stored in the header.
   This allows you to list arrays containing Nan entries.

   Arguments :

   MINDX (I) INTEGER
          indicates which MTZ file - 1 index points to both input and
          output files

   ADATA (I) REAL
          array of dimension at least NCOL containing the reflection
          record with "missing" values set to VAL_MAGICA

   BDATA (O) REAL
          Array of dimension at least NCOL containing the reflection
          record with "missing" values reset to VAL_MAGIC

   NCOL (I) INTEGER
          Array size of ADATA

   VAL_MAGICA (I) REAL
          If MINDX = 0 then this value will be treated as the MNF
          pertaining to the data. Otherwise

   VAL_MAGICB (I) REAL
          "Missing value" flag to reset in BDATA to allow record to be
          printed.

SUBROUTINE SET_MAGIC(MINDX,VAL_MAGIC,SETVAL)

   Subroutine to pass the "magic" value for this mtz file either into the
   file or back to the calling program

   Arguments :

   MINDX (I) INTEGER
          indicates which MTZ file - 1 index points to both input and
          output files

   VAL_MAGIC (I) REAL
          variable giving value assigned to "missing data"; it may be
          passed to an MTZ file, or return a preset value.

   SETVAL (I) LOGICAL
          if TRUE on entry, the mtz missing flag is set to VAL_MAGIC - ie
          the value in the mtz file is OVERWRITTEN! if FALSE on entry and
          there is a "missing value" set in the input MTZ file that will
          be returned as VAL_MAGIC, and SETVAL will be returned TRUE. if
          FALSE on entry and there is NO "missing value" set in the input
          MTZ file VAL_MAGIC will be set to the default for both input
          and output SETVAL returned TRUE

SUBROUTINE LRREFM(MINDX,LOGMSS)

   Returns Logical array which flags missing data entries Array DATMSS
   set in LRREFF and LRREFL

   Arguments :

   MINDX (I) INTEGER
          indicates which MTZ file - 1 index points to both input and
          output files

   LOGMSS (O) LOGICAL
          Array of dimension at least NPLABS(MINDX) if LRREFF is being
          used, or NCOLS(MINDX) if LRREFL is being used. In practice,
          dimension MCOLS is safest. Contains the logical array LOGMSS on
          exit in order of LRREFF or LRREFL, whichever was most recently
          called. IF LOGMSS(..) is TRUE the entry is "missing". Maps onto
          DATMSS.

SUBROUTINE LRIDX(MINDX,PNAME,XNAME,DNAME,ISETS,DATCELL, DATWAVE,NDATASETS)

   Subroutine to return information for all datasets from the MTZ file
   header, including crystal names.

   Arguments :

   MINDX (I) INTEGER
          indicates which MTZ file - 1 index points to both input and
          output files

   PNAME (O) CHARACTER
          array of dimension at least NDATASETS containing the project
          name on exit

   XNAME (O) CHARACTER
          array of dimension at least NDATASETS containing the crystal
          name on exit

   DNAME (O) CHARACTER
          array of dimension at least NDATASETS containing the dataset
          name on exit

   ISETS (O) INTEGER
          array of dimension at least NDATASETS containing the dataset id
          on exit

   DATCELL (O) REAL
          array of dimension at least NDATASETS containing the dataset
          cell dimensions

   DATWAVE (O) REAL
          array of dimension at least NDATASETS containing the dataset
          wavelength

   NDATASETS (O) INTEGER
          number of datasets in MTZ header

SUBROUTINE LRIDC(MINDX,PNAME,DNAME,ISETS,DATCELL, DATWAVE,NDATASETS)

   Subroutine to return information for all datasets from the MTZ file
   header.

   Arguments :

   MINDX (I) INTEGER
          indicates which MTZ file - 1 index points to both input and
          output files

   PNAME (O) CHARACTER
          array of dimension at least NDATASETS containing the protein
          name on exit

   DNAME (O) CHARACTER
          array of dimension at least NDATASETS containing the dataset
          name on exit

   ISETS (O) INTEGER
          array of dimension at least NDATASETS containing the dataset id
          on exit

   DATCELL (O) REAL
          array of dimension at least NDATASETS containing the dataset
          cell dimensions (returns zero if not set).

   DATWAVE (O) REAL
          array of dimension at least NDATASETS containing the dataset
          wavelengths (returns zero if not set).

   NDATASETS (O) INTEGER
          number of datasets in MTZ header

SUBROUTINE LRID(MINDX,PNAME,DNAME,ISETS,NDATASETS)

   As LRIDC, but without cell and wavelength information (for backwards
   compatbility).

   Arguments :

   MINDX (I) INTEGER
          indicates which MTZ file - 1 index points to both input and
          output files

   PNAME (O) CHARACTER
          array of dimension at least NDATASETS containing the protein
          name on exit

   DNAME (O) CHARACTER
          array of dimension at least NDATASETS containing the dataset
          name on exit

   ISETS (O) INTEGER
          array of dimension at least NDATASETS containing the dataset id
          on exit

   NDATASETS (O) INTEGER
          number of datasets in MTZ header

SUBROUTINE LWIDX(MINDX,PROJECT_NAME,CRYSTAL_NAME,DATASET_NAME, DATCELL,DATWAVE)

   Subroutine to add dataset information to the output MTZ file header,
   including crystal names. Datasets identified by the
   PROJECT_NAME/DATASET_NAME pair are appended to the MTZ header one at a
   time. Checks to see if the PROJECT_NAME/DATASET_NAME pair is already
   included; if so, the dataset is updated with the cell and wavelength
   information. Redundant datasets are removed in LWCLOS.

   Arguments :

   MINDX (I) INTEGER
          indicates which MTZ file - 1 index points to both input and
          output files

   PROJECT_NAME (I) CHARACTER
          project name of dataset to be added (strings longer than 64
          will be truncated)

   CRYSTAL_NAME (I) CHARACTER
          crystal name of dataset to be added (strings longer than 64
          will be truncated)

   DATASET_NAME (I) CHARACTER
          dataset name of dataset to be added (strings longer than 64
          will be truncated)

   DATCELL (I) REAL
          cell dimensions of dataset to be added

   DATWAVE (I) REAL
          wavelength of dataset to be added

SUBROUTINE LWIDC(MINDX,PROTEIN_NAME,DATASET_NAME, DATCELL,DATWAVE)

   Subroutine to add dataset information to the output MTZ file header.
   Datasets identified by the PROJECT_NAME/DATASET_NAME pair are appended
   to the MTZ header one at a time. Checks to see if the
   PROJECT_NAME/DATASET_NAME pair is already included; if so, the dataset
   is updated with the cell and wavelength information. Redundant
   datasets are removed in LWCLOS.

   Arguments :

   MINDX (I) INTEGER
          indicates which MTZ file - 1 index points to both input and
          output files

   PROTEIN_NAME (I) CHARACTER
          protein name of dataset to be added (strings longer than 64
          will be truncated)

   DATASET_NAME (I) CHARACTER
          dataset name of dataset to be added (strings longer than 64
          will be truncated)

   DATCELL (I) REAL
          cell dimensions of dataset to be added (if zero passed, no cell
          information is added, but when the output header is written by
          LWCLOS, DATCELL defaults to overall cell).

   DATWAVE (I) REAL
          wavelength of dataset to be added (if zero passed, no
          wavelength information is added).

SUBROUTINE LWID(MINDX,PROTEIN_NAME,DATASET_NAME)

   As LWIDC, but without cell and wavelength information (for backwards
   compatbility).

   Arguments :

   MINDX (I) INTEGER
          indicates which MTZ file - 1 index points to both input and
          output files

   PROTEIN_NAME (I) CHARACTER
          protein name of dataset to be added (strings longer than 64
          will be truncated)

   DATASET_NAME (I) CHARACTER
          dataset name of dataset to be added (strings longer than 64
          will be truncated)

SUBROUTINE LRCLID(MINDX,CSETID,NCOL)

   Subroutine to return the ID of the related dataset for each column of
   the input MTZ file, as obtained from the header.

   Arguments :

   MINDX (I) INTEGER
          indicates which MTZ file - 1 index points to both input and
          output files

   CSETID (O) INTEGER
          array of dimension at least NCOL containing the dataset IDs on
          exit

   NCOL (O) INTEGER
          number of columns in the MTZ file

SUBROUTINE LWIDAS(MINDX,NLPRGO,PNAME,DNAME,IAPPND)

   Subroutine to associate dataset entry with each column for the output
   MTZ file. Note that this subroutine changes the values in the header
   common block, so all information about the input files datasets should
   already have been extracted.

   Arguments :

   MINDX (I) INTEGER
          indicates which MTZ file - 1 index points to both input and
          output files

   NLPRGO (I) INTEGER
          number of output program labels

   PNAME (I) CHARACTER
          array of dimension at least NLPRGO containing the output
          project name

   DNAME (I) CHARACTER
          array of dimension at least NLPRGO containing the output
          dataset name

   IAPPND (I) INTEGER
          =0 replace all existing column info
          =1 append to the existing column info

SUBROUTINE LRBSETID (MINDX,BATNO,BSETID)

   Subroutine to read dataset ID for batch BATNO from batch headers for
   multi-record file open on index MINDX. If LWBAT has been used, the
   batch headers in RBATW are used, else those in RBATR are used.

   Arguments :

   MINDX (I) INTEGER
          indicates which MTZ file - 1 index points to both input and
          output files

   BATNO (I) INTEGER
          batch number

   BSETID (O) INTEGER
          dataset ID for batch

SUBROUTINE LWBSETID (MINDX,BATNO,PNAME,DNAME)

   Subroutine to write dataset ID for batch BATNO to batch headers for
   multi-record file open on index MINDX. If LWBAT has been used, the
   batch headers in RBATW are used, else those in RBATR are used.

   Arguments :

   MINDX (I) INTEGER
          indicates which MTZ file - 1 index points to both input and
          output files

   BATNO (I) INTEGER
          batch number

   PNAME (I) CHARACTER
          project name of dataset

   DNAME (I) CHARACTER
          dataset name of dataset

Subroutine LKYIN(MINDX,LSPRGI,NLPRGI,NTOK,LINE,IBEG,IEND)

   Read standard input lines of the form
   LABIN <program label>=<file label> ...
   Use this to read the inputs, and then LRASSN to setup the program
   label to file label assignments.

   LKYIN also checks that each assignment set actually contains an input
   program label on one side of the = sign. This comparison is not case
   sensitive.

   If there is no ambiguity, the order in which program and file labels
   are given may be swapped.

   Arguments:

   LSPRGI (I) CHARACTER*30
          program label strings (array); L(abel) S(tring) PRG(rammme)
          I(nput)

   NLPRGI (I) INTEGER
          number of program input labels: N(umber of) L(abels) PRG(ramme)
          I(nput)

   NTOK (I) INTEGER
          from Parser, number of tokens on line

   LINE (I) CHARACTER*(*)
          the input line

   IBEG,IEND (I) INTEGER
          arrays from the parser, delimiters for each token

   LKYIN calls the following which are external to MTZLIB:

   External Subroutines: CCPUPC, PUTLIN
   External Functions : INTEGER LENSTR

Subroutine LKYSET(LSPRGI,NLPRGI,LSUSRJ,KPOINT,ITOK,NTOK,LINE,IBEG,IEND)

   Parses standard input lines of the form
   [LABIN] item1=name1 item2=name2 ...

   This subroutine returns the user input labels to the calling program
   (LKYIN does not) and the array KPOINT which indicates which of the
   program labels were assigned user input file labels

   Note that although this Subroutine looks similar to LKYIN it cannot be
   called in its place, it simply adds extra functionality. There is no
   MINDX argument to this call - it is not tied to any particular file(s)
   and the header common blocks are not affected by this subroutine.

   See the notes above (LKYIN) about the order of the assignment
   statements.

   Arguments:

   LSPRGI (I) CHARACTER*30
          program label strings (array): L(abel) S(tring) PRG(rammme)
          I(nput)

   NLPRGI (I) INTEGER
          number of program input labels: N(umber of) L(abels) PRG(ramme)
          I(nput)

   LSPRGJ (O) CHARACTER*30
          user supplied label strings (array): L(abel) S(tring)
          USR(rammme) I(nput). Copy of user input labels to return to the
          calling program

   KPOINT (O) INTEGER
          Indicator whether each program label is set: -1 if set, 0 if
          not

   ITOK (I) INTEGER
          First token to search on line - allows you to skip the LABIN
          token

   NTOK (I) INTEGER
          from Parser, number of tokens on line

   LINE (I) CHARACTER*(*)
          the input line

   IBEG,IEND (I) INTEGER
          arrays from the parser, delimiters for each token

   LKSET calls the following which are external to MTZLIB:

   External Subroutines: CCPUPC, PUTLIN
   External Functions : INTEGER LENSTR

Subroutine LKYOUT(MINDX,LSPRGO,NLPRGO,NTOK,LINE,IBEG,IEND)

   Read standard input lines of the form
   LABOUT LabelFC=userFC LabelPHCAL=userPHCAL ...
   Use this to read the inputs, and then LWASSN to setup the program
   label to (new) file label assignments.

   LKYOUT also checks that each assignment set actually contains an
   output program label on one side of the = sign. This comparison is not
   case sensitive.

   If there is no ambiguity, the order in which program and file labels
   are given may be swapped.

   Note that the case of the user output labels is preserved.

   Arguments:

   LSPRGO (I) CHARACTER*30
          program label strings (array): L(abel) S(tring) PRG(rammme)
          O(utput)

   NLPRGO (I) INTEGER
          number of program output labels: N(umber of) L(abels)
          PRG(ramme) O(utput)

   NTOK (I) INTEGER
          from Parser, number of tokens on line

   LINE (I) CHARACTER*(*)
          the input line

   IBEG,IEND (I) INTEGER
          arrays from the parser, delimiters for each token

   LKYOUT calls the following which are external to MTZLIB:

   External Subroutines: CCPUPC, PUTLIN
   External Functions : INTEGER LENSTR

Subroutine LKYASN(MINDX,NLPRGI,LSPRGI,CTPRGI,LOOKUP)

   Do column assignments, bypassing the need for keyworded input. This is
   useful in writing little mtz programs, without using Parser in the
   main program.

   Read column assignments and make them, for input MTZ file open for
   read on index MINDX

   It expects to read from stream 5 a line of the form
   LABIN program_label=file_label program_label=file_label . . .
   This routine is useful for simple jiffy programs that don't want full
   keyworded input

   See the LKYIN section above for the notes on case, and order of input
   assignments.

   Arguments:

   MINDX (I) INTEGER
          file index number for opened MTZ input file

   NLPRGI (I) INTEGER
          number of input program labels

   LSPRGI (I) CHARACTER*30
          array of dimension at least NLPRGI containing the program label
          strings

   CTPRGI (I) CHARACTER*1
          array of column types for each column: these will be checked to
          see that they match the actual column types in the file. If you
          don't want to check column types, provide blank types here
          (dimension at least NLPRGI)

   LOOKUP (O) INTEGER
          array of dimension at least NLPRGI containing column numbers
          for each assigned label

   LKYASN calls the following which are external to MTZLIB:

   External Subroutines: PARSER, LERROR

Subroutine LHPRT(MINDX,IPRINT)

   Print out the header information from the MTZ COMMON blocks for the
   MTZ file open on index MINDX.

   Arguments:

   MINDX (I) INTEGER
          indicates which MTZ file - 1 index points to both input and
          output files

   IPRINT (I) INTEGER
          print indicator: meaning:

   =1
          Brief header info printed (default)

   =2
          As above plus history info

   =3
          Full header dump, symmetry, alles!

   =4
          As 1 plus full symmetry

   any other value, nothing happens

   LHPRT calls the following which are external to MTZLIB:

   External Functions : INTEGER LENSTR
   External Subroutines: BLANK,LERROR,PUTLIN,SYMTR3

Subroutine LPHIST(MINDX)

   Output the history information from the MTZ file header. This text can
   be anything the programmer chooses, (but probably program stamps at
   least).

   Arguments:

   MINDX (I) INTEGER
          indicates which MTZ file - 1 index points to both input and
          output files

   LPHIST calls the following which are external to MTZLIB:
   External Functions : INTEGER LENSTR
   External Subroutines: BLANK,LERROR,PUTLIN

Subroutine RBATHD(ILUN,BATCH,RBATCH,CBATCH)

   MTZLIB internal subroutine to read next batch header from multi-record
   MTZ file open on unit ILUN, and return it's batch number, plus real
   and character arrays.


Arguments:

ILUN    (I)  INTEGER         LUN on which the file is open

BATCH   (O)  INTEGER         serial number of this batch

RBATCH  (O)  REAL(*)         array into which integer and real batch
                             info is decoded by subroutine
                             this should be equivalenced onto the
                             appropriate COMMON block in the calling
                             program. The first item is nwords,ie how
                             many items in the array, if nword is 0
                             then only the title is present

CBATCH  (O)  CHARACTER(*)*1  as RBATCH, but for character items - no
                             nwords however; title is 1st 70 chars of
                             CBATCH.

   RBATHD is call by LROPEN.

   RBATHD calls the following which are external to MTZLIB:

   External Subroutines: LERROR,QMODE,QREAD

Subroutine WBATHD(ILUN,BATCH,RBATCH,CBATCH)

   MTZLIB internal subroutine to write batch header to Multi-record MTZ
   file open for write on ILUN, with batch number BATCH, and data in
   RBATCH and CBATCH


Arguments:

ILUN    (I)  INTEGER         LUN on which the file is open

BATCH   (I)  INTEGER         serial number of this batch

RBATCH  (I)  REAL(*)         array from which integer and real batch
                             info is encoded by subroutine
                             this should be equivalenced onto the
                             appropriate COMMON block in the calling
                             program. The first item is nwords,ie how
                             many items in the array, if nword is 0
                             then only the title is written

CBATCH  (I)  CHARACTER(*)*1  as RBATCH, but for character items - no
                             nwords however; title is 1st 70 chars of
                             CBATCH.

   WBATHD is called by LWCLOS.

   WBATHD calls the following which are external to MTZLIB:

   External Subroutines: QMODE,QWRITE

Subroutine LRHDRL(ILUN,LINE)

   MTZLIB internal subroutine to read one header record from an MTZ file
   open for read on unit ILUN, and place the result in the character
   string LINE. All the header lines are 80 characters long and written
   to the file in 20A4 format, so have to decode from integers to chars
   QMODE = 0 for the header record (ie bytes)


Arguments:

ILUN    (I)  INTEGER         LUN on which the file is open,
                             for each MTZ file open this is stored
                             in the RLUN array in MTZWRK

LINE    (O)  CHARACTER*(*)   character string containing one header
                             record from the MTZ file

   LRHDRL calls the following which are external to MTZLIB:
   External Subroutines: QREAD,LERROR

Subroutine LBPRTH(IBATCH,IPRINT)

   Internal subroutine to print out the batch header information from the
   MTZ COMMON blocks /MBTHDR/ and /CBTHDR/ (info already there)


Arguments:

IBATCH  (I)  INTEGER    batch number

IPRINT  (I)  INTEGER    print indicator: meaning:
                        =0 no print
                        =1 print batch title only
                        =2 also print orientation block
                        .GT. 30 also print orientation block
                        TO UNIT NUMBER IPRINT

   LBPRTH is called by LBPRT.

   LBPRTH calls the following which are external to MTZLIB:

   External Subroutines: BLANK,PUTLIN

Subroutine LABPRT(LABELS,NLABS)

   Internal subroutine for MTZ routines to output an array of character
   strings across the page nicely eg labels or types.
   Uses subroutine PUTLIN to output to window CURWIN.


Arguments:

LABELS  (I)  CHARACTER*(*)   array of dimension (NLABS) containing
                             the character strings to be output

NLABS   (I)  INTEGER         number of labels to be output


   LABPRT calls th following which are external to MTZLIB:

   External Functions : INTEGER LENSTR
   External Subroutines: PUTLIN

Subroutine SORTUP(N,A,IN)

   Internal subroutine to return order of A in IN - Index Sort, for
   integer array. Lifted from STILLS program (MOSCO suite).
   Ref: Comm. ACM VOL.12 #3 MARCH 1969, R.C.SINGLETON


Arguments:

N       (I)  INTEGER    dimension of arrays A and IN

A   (I)  INTEGER    array to be sorted

IN  (O)  INTEGER    index array for A

Subroutine ADDLIN(NEWLIN,LINES,MAXLIN)

   Internal subroutine to add new lines from NEWLIN to array LINES


Arguments:

NEWLIN(MAXLIN)  (I/O)   character array
   this is cleared on output

LINES(MAXLIN)  (O)   character array

INTEGER Function NEXTLN(LINES,MAXLIN)

   Internal integer function to find the next empty line in a character
   array


Arguments:

LINES(MAXLIN) (I)   character array

NEXTLN        (O)   INTEGER number of next blank line (= -1 if full)


Subroutine LSTRSL(MINDX,A,B,C,ALPHA,BETA,GAMMA)

   Internal subroutine to calculate coefficients for
   (sin(theta)/lambda)**2 from h,k,l for general axes.

   First calculate the components of input axes in an orthonormal basis,
   then calculate components of reciprocal axes in same basis

   Input angles are in degrees

   This is exactly the same as the subroutine SETRSL in SYMLIB, except
   that it stores its variables in the internal MTZ COMMON blocks, and
   will work if more than one file is open at once.


MINDX  (I)  INTEGER      indicates which MTZ file - one index
                         points to both input and output files

A,B,C,ALPHA,BETA,GAMMA
       (I)  REAL         cell parameters

REAL FUNCTION LSTLSQ(MINDX,IH,IK,IL)

   Internal real function to calculate (sin(theta)/lambda)**2 from h,k,l;
   coef's set by call to LSTRSL, for the file open on index MINDX

   This is exactly the same as the function STHLSQ in SYMLIB, except that
   it stores it's variables in the internal MTZ COMMON blocks, and will
   work if more than one file is open at once.


MINDX     (I)  INTEGER    indicates which MTZ file - one index
                          points to both input and output files

IH,IK,IL  (I)  INTEGER    Miller indices for the reflection

MTZ INTERNAL COMMON BLOCKS The following common blocks used by MTZLIB are
listed here for completeness: MTZCHR, MTZHDR, MTZWRC, MTZWRK, MBTHDR, CBTHDR,
MTZHAR



C
C - Parameters, COMMON blocks, and declarations for MTZ subroutines
C
C     .. Parameters ..
      INTEGER MFILES,MCOLS,MBATCH
      PARAMETER (MFILES=4,MCOLS=500,MBATCH=5000)
      INTEGER MINCOL
      PARAMETER (MINCOL=3)
      INTEGER NTYP,LTYP
      PARAMETER (NTYP=16,LTYP=9)
      INTEGER MBLENG,CBLENG
      PARAMETER (MBLENG=185,CBLENG=70+3*8)
      INTEGER NHISLM
      PARAMETER (NHISLM=30)
C     ..
C     .. Arrays in Common ..
      REAL CELL,CRANGE,SRANGE,RBATR,RBATW,RSYM,WRANGE,WSRNGE
      INTEGER BATNUM,HDRST,ISORT,NBATCH,NBATR,NBATW,NCOLS,NCOLW,NHISTL,
     +        NPLABS,NREFR,NREFS,NREFW,NSPGRP,NSYM,NSYMP,RLUN,RPOINT,
     +        WLUN,WOMBAT,NSETW,SET_ID,CSET_ID,IDEFSET
      LOGICAL SORTB
      CHARACTER CBATR*1,CBATW*1,CTYPE*1,LTYPE*1,PGNAM*10,SPGNAM*10,
     +          CLABEL*30,PLABS*30,TITLE*70,HSCR*80,ENTRY_ID*64,
     +          DIFFRN_ID*64
C     ..
C     .. Local Arrays ..
      CHARACTER CTYPES(NTYP)*1,LTYPES(LTYP)*1
C     ..
C     .. Common blocks ..
      COMMON /MTZCHR/TITLE(MFILES),CLABEL(MCOLS,MFILES),
     +       CTYPE(MCOLS,MFILES),SPGNAM(MFILES),LTYPE(MFILES),
     +       CBATR(CBLENG,MBATCH,MFILES),PGNAM(MFILES)
      COMMON /MTZHDR/CELL(6,MFILES),NSYM(MFILES),NSYMP(MFILES),
     +       RSYM(4,4,192,MFILES),NCOLS(MFILES),NREFS(MFILES),
     +       NBATCH(MFILES),BATNUM(MBATCH,MFILES),ISORT(5,MFILES),
     +       CRANGE(2,MCOLS,MFILES),NSPGRP(MFILES),
     +       RBATR(MBLENG,MBATCH,MFILES),SRANGE(2,MFILES)
      COMMON /MTZWRC/PLABS(MCOLS,MFILES),HSCR(NHISLM,MFILES),
     +       CBATW(CBLENG,MBATCH,MFILES)
      COMMON /MTZWRK/NCOLW(MFILES),RLUN(MFILES),WLUN(MFILES),
     +       RPOINT(MCOLS,MFILES),WRANGE(2,MCOLS,MFILES),NREFW(MFILES),
     +       NREFR(MFILES),NPLABS(MFILES),NBATW(MFILES),NBATR(MFILES),
     +       WOMBAT(MBATCH,MFILES),HDRST(MFILES),SORTB(MFILES),
     +       NHISTL(MFILES),RBATW(MBLENG,MBATCH,MFILES),WSRNGE(2,MFILES)
      COMMON /MTZHAR/NSETW(MFILES),SET_ID(MSETS,MFILES),
     +       ENTRY_ID(MSETS,MFILES),DIFFRN_ID(MSETS,MFILES),
     +       CSET_ID(MCOLS,MFILES),IDEFSET(MFILES)
C     ..
C     .. Data statements ..
      DATA CTYPES/'H','J','F','D','Q','P','W','A','B','Y','I','R',
     +            'G','K','L','M'/
      DATA LTYPES/'P','A','B','C','I','F','R','H','?'/


   Common blocks used by multi-record MTZ routines:

   These subroutines pass the batch header information (title and
   orientation blocks) as arguments packed into a REAL(185) and a
   CHARACTER(94) array. In the real array, the first 156 words are REAL
   numbers and the remaining 29 are INTEGER*4. The subroutine which
   produces formatted output of the batch headers, LBPRT, decodes these
   arrays into separate items by copying these arrays into common blocks
   (one for real and one for characters), and calling a subroutine
   (LBPRTH) which has these common blocks as


      COMMON /MBTHDR/ NWORDS,NINTGR,NREALS,IORTYP,LBCELL(6),MISFLG,
     +     JUMPAX,NCRYST,LCRFLG,LDTYPE,JSCAXS,NBSCAL,NGONAX,LBMFLG,
     +     NDET,LBSETID,INTPAD(8),
     +     CELL(6),UMAT(3,3),PHIXYZ(3,2),CRYDAT(12),DATUM(3),
     +     PHISTT,PHIEND,SCANAX(3),TIME1,TIME2,
     +     BSCALE,BBFAC,SDBSCL,SDBFAC,PHIRANGE,BATPAD(11),
     +     E1(3),E2(3),E3(3),
     +     GONPAD(12),SOURCE(3),S0(3),BEMDAT(25),
     +     DX1,THETA1,DETLM1(2,2),DX2,THETA2,DETLM2(2,2),DETPAD(33)


      INTEGER NWORDS,NINTGR,NREALS,IORTYP,LBCELL,MISFLG,
     +     JUMPAX,NCRYST,LCRFLG,LDTYPE,JSCAXS,NBSCAL,NGONAX,LBMFLG,
     +     NDET,LBSETID,INTPAD


      REAL   CELL,UMAT,PHIXYZ,CRYDAT,ETAD,DATUM,
     +     PHISTT,PHIEND,PHIRANGE,SCANAX,TIME1,TIME2,
     +     BSCALE,BBFAC,SDBSCL,SDBFAC,BATPAD,E1,E2,E3,GONPAD,
     +     SOURCE,S0,BEMDAT,ALAMBD,DELAMB,DELCOR,DIVHD,DIVVD,
     +     DX1,THETA1,DETLM1,DX2,THETA2,DETLM2,DETPAD,ETADH,ETADV


         COMMON /CBTHDR/ BTITLE,GONLAB(3)

         CHARACTER BTITLE*70, GONLAB*8

   An explanation of the format of the common blocks:

   Orientation block data

   This contains slots for all information that seems to be essential at
   present. Each group of parameters is padded at the end for future
   expansion.

   Data in the orientation block are referred to the Cambridge laboratory
   axis frame: x along the (idealized) X-ray beam, z along usual rotation
   axis E1 (omega on 3-axis system). The matrix Q converts a vector in
   the Madnes frame to the Cambridge frame. Note that the laboratory
   frame is essentially defined by the vectors e1,e2,e3 and source. It
   doesn't really seem necessary to carry through a whole lot of crystal
   and beam tensors, particularly as we have integrated intensities at
   this stage, but maybe someone will want to, using the allocated
   padding
   The general orientation equation is


x  =   R M U B h

where x    position in laboratory frame
R    goniostat matrix
M    missetting angle matrix (if relevant, see MISFLG)
            PhiZ PhiY PhiX (PHIXYZ)
U    crystal orientation matrix UMAT
B    cell orthogonalization matrix, derived from cell dimensions
h    reflection indices


Note that the description below is NOT is the same order as in the
common block, in which all the integers come before all the reals
(flagged as I or R in the description below)

I    NWORDS       number of words in orientation block
I    NINTGR       number of integers (first part of block includes
                  these counts)
I    NREALS       number of reals
I    IORTYP       type of orientation block (for possible future
                  use, now = 0)
I    INTPAD(8)    padding for future use (integers)

--- Information for this crystal

R    CELL(6)      cell dimensions  (A and degrees)
I    LBCELL(6)    refinement flags for cell dimensions
R    UMAT(3,3)    orientation matrix U. If MISFLG .gt. 0, U is the
                   standard setting when PhiXYZ ==0
I    MISFLG       status of missetting angles PHIXYZ
                   = 0  PHIXYZ not used, all orientation in UMAT
                   = 1  1 set of missetting angles (PHIXYZ(I,1))
                   = 2  2 sets PHIXYZ(I,J), J=1,2
R    PHIXYZ(3,2)  missetting angles at beginning and end of rotation
I    JUMPAX       reciprocal axis closest to principle goniostat axis E1
                       (only used for printing)
I    NCRYST       crystal number: a crystal may contain several batches
I    LBSETID      dataset number (this indexes a list of datasets in the
                  file header)
I    LCRFLG       type of crystal mosaicity information
                  (=0 for isotropic, =1 anisotropic)
     *** CRYDAT(12) equivalenced to following ***
R    ETAD         reflection width (full width) (degrees) (if LCRFLG=0)
      or
R    ETADH,ETADV  horizontal and vertical reflection width  (if LCRFLG=1)
R    rest of CRYDAT: padding for crystal information
                     (eg more complicated mosaicity model)

--- Information for this batch

I    LDTYPE       type of data
                   = 1    oscillation data   (2D spots)
                   = 2    area detector data (3D spots)
                   = 3    Laue data
R    DATUM(3)     datum values of goniostat axes, from which
                  Phi is measured (degrees)
R    PHISTT,PHIEND start and stop values of Phi (degrees)
                   relative to datum
R    PHIRANGE     range of Phi values: typically this will be PHIEND-PHISTT,
                    but storing this explicitly allows a distinction
                    eg between a rotation of +160 degrees from a rotation
                    of -200 degrees
I    JSCAXS       goniostat scan axis number (=1,2,3, or =0
                  for multiple axis scan
R    SCANAX(3)    rotation axis in laboratory frame
                  (not yet implemented: only relevant if JSCAXS=0)
R    TIME1, TIME2 start and stop times in minutes
I    NBSCAL       number of batch scales and Bfactors plus SD's
                   (4 at present, BSCALE, BBFAC and sd's)
                  set = 0 if batch scales unset
R    BSCALE       batch scale
R    BBFAC        batch temperature factor.
                   corresponding scale is
                   exp(-2 B (sin theta/lambda)**2)
R    SDBSCL       sd (Bscale)
R    SDBFAC       sd (BBfac)
R    BATPAD(11)   padding for batch information

--- Crystal goniostat information

I    NGONAX       number of goniostat axes (normally 1 or 3)
I    E1(3),E2(3),E3(3) vectors (in Cambridge laboratory frame,
                        see below) defining the NGONAX goniostat axes
C    GONLAB(3)  names of the three goniostat axes
R    GONPAD(12) padding for goniostat information


--- Beam information

R    SOURCE(3)    Idealized (ie excluding tilts) source vector
                   (antiparallel to beam), in Cambridge
                   laboratory frame
R    S0(3)        Source vector (antiparallel ! to beam), in
                   Cambridge laboratory frame, including tilts
I    LBMFLG       flag for type of beam information following
                   = 0 for ALAMBD, DELAMB only (laboratory source)
                   = 1     ALAMBD,DELAMB,DELCOR,DIVHD,DIVVD
                           (synchrotron)
                           (other options could include white beam)
*** BEMDAT(25) equivalenced to following ***
R    ALAMBD       Wavelength in Angstroms
R    DELAMB       dispersion Deltalambda / lambda.
R    DELCOR       Correlated component of wavelength dispersion.
R    DIVHD        Horizontal beam divergence in degrees.
R    DIVVD        Vertical beam divergence (may be 0.0 for
                   isotropic beam divergence.
R    rest of BEMDAT: padding for beam information

--- Detector information

I    NDET         number of detectors (current maximum 2)
     -- for each detector
R    DXn          crystal to detector distance (mm)
R    THETAn       detector tilt angle (=Madnes:tau2) (degrees)
R    DETLMn(2,2)  minimum and maximum values of detector
                  coordinates (pixels)
                     (i,j): i = 1 minimum, = 2 maximum
                            j = 1 Ydet,    = 2 Zdet
R    DETPAD(34)     padding for detector information


If you want to see an example of this, look at the subroutines
LBPRT and LBPRTH.

C INTERFACE Jan Pieter Abrahams has written a C interface to MTZLIB which is
incorporated into the solomon program.

   A new C-language library, which includes functions for reading and
   writing MTZ files, is under development, see the new library page.

EXAMPLE PROGRAM USING AN MTZ FILE (See also the program templates available on
the CCP4 developer's pages.)


      PROGRAM example_MTZ
C     ===================
C
C---- An example of a program reading and writing MTZ files.C
C
C     .. Parameters ..
      INTEGER MCOLS, NPAR, NLOC
      PARAMETER (MCOLS=500, NPAR=200, NLOC=50)
C     ..
C     .. Scalars for Parser ..
      INTEGER NTOK
      LOGICAL LEND
      CHARACTER KEY*4,LINE*400
C     ..
C     .. Arrays for Parser ..
      REAL FVALUE(NPAR)
      INTEGER IBEG(NPAR),IDEC(NPAR),IEND(NPAR),ITYP(NPAR)
      CHARACTER CVALUE(NPAR)*4
C     ..
C     .. Local Scalars ..
      REAL EPS,F1,F2,FLAGIP,FLAGOP,RSOL
      INTEGER ALLSYM,I,IC,ICALL,ICEN,IERR,IFIL,II,ILEN,IPRINT,ISYSAB,
     +        JDO10,JDO30,JDO40,JQ,NCEN,NCHK,NCOL,NEPS,NLPRGI,NLPRGO,
     +        NREF,NSYM,NSYSAB,NLUSRI,NLURSO
      CHARACTER DUMMY*10,TITNEW*70
      LOGICAL EOF
C     ..
C     .. Local Arrays ..
      REAL ADATA(MCOLS),DUM(2,MCOLS),RSYM(4,4,192)
      INTEGER IH(3),JPOINT(NLOC),LOOKUP(NLOC)
      CHARACTER OUTTYP(NLOC)*1,LSPRGI(NLOC)*30,LSPRGO(NLOC)*30,
     +          HISNEW(20)*80,CTPRGI(NLOC)*1
C     ..
C     .. External Subroutines ..
      EXTERNAL CCPUPC,CENTR,EPSLON,LRASSN,LRINFO,LROPEN,LRREFF,
     +         LRSYMM,LRTITL,LWASSN,LWCLOS,LWHIST,LWOPEN,LWREFL,LWTITL,
     +         PARSER,SYMTRN,LKYIN,LKYOUT
C     ..
C     .. Data statements ..
C---- NLPRGI  =  number of input labels
      DATA NLPRGI,LSPRGI/7,'H','K','L','F1','SIG1','DELF1',
     +     'SIGDELF1',43*' '/
C---- NLPRGO  =  number of output labels
      DATA NLPRGO,LSPRGO/9,'H','K','L','FP','F1','SIG1','SIGFP',
     +     'FN','SIGFN',41*' '/
C---- This code signs which input columns are essential (LOOKUP)
      DATA CTPRGI/'H','H','H','F','Q','F','Q',43*' '/
      DATA OUTTYP/'H','H','H','F','Q','F','Q','F','Q',41*' '/
      DATA LOOKUP/-1,-1,-1,-1,-1,-1,0,43*0/
C---- Clear character arrays  TITNEW, HISNEW, JPOINT
      DATA HISNEW/20*' '/, JPOINT/50*0/
C     ..
      CALL CCPFYP
      CALL MTZINI
      NTOK = NPAR
      IFIL = 1
      IPRINT = 3
C---- Open input file for Read
      CALL LROPEN(IFIL,'HKLIN',IPRINT,IERR)
C---- Open output file
      CALL LWOPEN(IFIL,'HKLOUT')
C---- Default is to copy input title to output
C---- Do you want to change title??
      TITNEW = 'A test case for reading and writing MTZ files'
      CALL LWTITL(IFIL,TITNEW,0)
C---- Some history to append to output file
C      Only last 30 lines will be kept
      HISNEW(1) = ' Calculating F(+) F(-) - MTZRW_NEW'
      HISNEW(2) = ' Some more info...'
      CALL LWHIST(IFIL,HISNEW,2)
C---- Find out how many columns and reflections in input file
      CALL LRINFO(IFIL,DUMMY,NCOL,NREF,DUM)
C---- We want to set up centric and epsilon tests
      ALLSYM = 0
      CALL LRSYMM(IFIL,NSYM,RSYM)
      CALL SYMTRN(NSYM,RSYM)
      CALL CENTRIC(NSYM,ISYM,0)
C---- Read Program labels here if you like or
C     use those assigned in data stt above...
C
C    Eg as in FFT  F1 SIG1 F2 SIG2 PHI ....
C
C    LKYIN will read string F1=FNAT89 PHI=Acalc  ...
C    LRASSN  will set LOOKUP(i) (i=1-nlabs) equal
C                column number in input file.
C    LOOKUP(i)=0 if label not matched...
      NLUSRI = 0
      NLUSRO = 0
   20 CONTINUE
      LINE = ' '
      KEY = ' '
      NTOK = NPAR
      CALL PARSER(KEY,LINE,IBEG,IEND,ITYP,FVALUE,CVALUE,IDEC,NTOK,LEND,
     +            .FALSE.)
      IF (.NOT.LEND) THEN
        IF (KEY.EQ.'LABI') THEN
          CALL LKYIN (IFIL,LSPRGI,NLPRGI,NTOK,LINE,IBEG,IEND)
          CALL LRASSN(IFIL,LSPRGI,NLPRGI,LOOKUP,CTPRGI)
        ELSE IF (KEY.EQ.'LABO') THEN
          CALL LKYOUT(IFIL,LSPRGO,NLPRGO,NTOK,LINE,IBEG,IEND)
          CALL LWASSN(IFIL,LSPRGO,NLPRGO,OUTTYP,0)
        END IF
        GO TO 20
      END IF
C---- Now read data (`lookup' order)
      WRITE (6,FMT=*) '  NREF= ',NREF
      DO 40 JDO40 = 1,NREF
        CALL LRREFF(IFIL,RSOL,ADATA,EOF)
        IH(1) = ADATA(1)
        IH(2) = ADATA(2)
        IH(3) = ADATA(3)
C       centricity check
        CALL CENTR(IH,ICEN)
        IF (ICEN.EQ.1) THEN
          NCEN = NCEN + 1
          IF (NCEN.LT.21) WRITE (6,FMT='(A,3I4,F8.2)') ' CENTRIC ',IH
        END IF
C---- EPS = multiplicity of reflection. ISYSAB = 1 - systematic absence
        CALL EPSLON(IH,EPS,ISYSAB)
        IF (EPS.GT.1.0) THEN
          NEPS = NEPS + 1
          WRITE (6,FMT='(/,A,3I4,F8.2)') '  EPS GT 1 ',IH,EPS
          IF (ISYSAB.EQ.1) THEN
            NSYSAB = NSYSAB + 1
            WRITE (6,FMT='(/,A,3I4,F8.2)') ' SYS ABS  ',IH
          END IF
        END IF
        NCHK = MOD(JDO40,500)
        IF (NCHK.EQ.1) THEN
          IH(1) = ADATA(1)
          IH(2) = ADATA(2)
          IH(3) = ADATA(3)
          WRITE (6,FMT=6004) JDO40,IERR,IH, (ADATA(II),II=4,NCOL)
        END IF
C---- Do something .....
        F1 = (ADATA(4)+ADATA(6))/2
        F2 = (ADATA(4)-ADATA(6))/2
        ADATA(6) = F1
        ADATA(7) = ADATA(5)
        ADATA(8) = F2
        ADATA(9) = ADATA(5)
C---- New write routine
        IF (NCHK.EQ.1) WRITE (6,FMT=6006) JDO40,
     +      (ADATA(II),II=1,NLPRGO)
        IERR = -1
        ICALL = ICALL + 1
        CALL LWREFL(IFIL,ADATA)
   40 CONTINUE
      WRITE (6,FMT=6008) NCEN,NEPS,NSYSAB
C---- Close output file  - This call actually writes the header
      CALL LWCLOS(IFIL,2)
      CALL CCPERR(0, 'Normal termination')
C---- Format statements
 6000 FORMAT (' No assignment using default of ',A)
 6002 FORMAT (' index for MLABSO = ',I4,' prog lab ',A,' user label ',A)
 6004 FORMAT (' NREF IEND - IP DATA ',I8,I3,/1X,3I4,10F8.1,
     +       10 (/13X,10F8.1))
 6006 FORMAT (' NREF OP DATA ',I8,/1X,3F6.2,10F8.1,10 (/13X,10F8.1))
 6008 FORMAT (' END OF FILE - NUMBER OF CENTRIC REFLNS',I5,/' NUMBER O',
     +       'F EPS GT 1 ',I5,/' NUMBER OF SYS ABS ',I5)
      END

AUTHORS AND HISTORY Sandra McLaughlin and Howard Terry (EMBLHH) November 1989
Header handling revised: SMM November 1990
Multi-record routines: SMM Feb 1990
Symmetry handling routines: Eleanor Dodson (York)
First limited release to an unsuspecting public May 1991

Missing Number Flag routines: 1996-ish

Dataset handling: Martyn Winn 1998-2002