NCSMASK (CCP4: Supported Program)
                                       
NAME

   ncsmask - averaging mask manipulation program
   
SYNOPSIS

   ncsmask [ MSKIN foo.msk / XYZIN foo.pdb ] MSKOUT bar.msk
   [Keyworded input]
   
DESCRIPTION

   This program performs operations on non-crystallographic symmetry
   masks. It is ideal as a precursor to `dm', since it contains a more
   sophisticated treatment of mask overlap, and may avoid some problems
   commonly caused by poorly defined masks.
   
   Input can be from a PDB file, in which case a mask is generated from
   spheres around all atoms. A crude 'sphere mask' can be constructed by
   making a PDB file with only a few atoms and specifying a large radius.
   
   Alternatively input can be from a CCP4 format map/mask file.
   
   The mask may then be modified by expanding or contracting, smoothing
   the boundary, reducing from a multimer to a monomer (in some cases),
   removing crystallographic- or non-crystallographic symmetry overlap
   and altering the mask box size.
   
   This program should not normally be used for generating solvent masks,
   since it does not impose crystallographic symmetry or unit cell
   repeat. See mapmask for further details. However, these masks can be
   used in DM 1.7.1 or later.
   
INPUT/OUTPUT FILES

   XYZIN
          is the input PDB file
          
   MSKIN
          is the input mask file
          
   MSKOUT
          is the output mask file
          
KEYWORDED INPUT

   The GRID and SYMMETRY cards are useful if input is from a .pdb file,
   otherwise the information is taken from the input mask header.
   Available keywords are:
   
     AVERAGE, AXIS, EXPAND, GRID, MONOMER, NOTRIM, OVERLAP, PEAK,
     RADIUS, SMOOTH, SYMMETRY, XYZLIM
     
  GRID <nx> <ny> <nz> | SPACING <x> [ <y> <z> ]
  
   Set the sampling grid over the unit cell to <nx>*<ny>*<nz>. The
   default is 1.0 Angstrom spacing.
   Alternatively, the SPACING subkeyword allows you to set the grid
   spacing; if only x is specified then this gives x Angstrom spacing
   along all axes, otherwise x, y and z are the spacings along each axis.
   
   The GRID keyword is ignored if a mask is input.
   
  SYMMETRY <spacegroup name/number>
  
   Set the spacegroup symmetry for the mask. The default is taken from
   the input mask if a mask is input, or P1 if a .pdb file is input.
   
  AXIS <x> <y> <z>
  
   Change the default output axis order. The first axis specified will
   vary fastest.
   
  XYZLIM <x1> <x2> <y1> <y2> <z1> <z2>
  
   Changes the default mask extent. <x1>-<z2> are either in grid units or
   fractional coordinates. If the new extent is smaller than the input
   mask extent, the input will be truncated, if the new extent is larger
   the mask will be padded with zeros. The default is either the extent
   of the input mask or the extent of the input .pdb file + sphere radius
   + 3.0 Angstrom. See however the NOTRIM card.
   
  RADIUS <rad>
  
   Set the sphere radius for building a mask out of atoms. Default=3.0
   Angstrom. A much larger value could be used to build a mask around
   C-alpha or sulphur coordinates, for example.
   
  PEAK <num>
  
   Pick the <num> largest connected regions of the mask, and delete all
   others. `PEAK 1' is particularly useful for tidying up a correlation
   mask (see maprot).
   
  EXPAND <rad>
  
   Expand/contract the mask. This function expands the mask by <rad>
   Angstrom in all directions. The mask will not be expanded beyond the
   current mask extent, if this is required the XYZLIM card should be
   used to increase the mask extent. A negative value will contract the
   mask.
   
  SMOOTH <rad>
  
   Smooth the mask using a sphere of radius <rad>. This will eliminate
   features smaller than <rad> from the surface of the mask. Maximum
   radius ~5 grid points.
   
  AVERAGE <nncs>
  
   Enter NC-symmetry elements for overlap removal. (Note that this card
   has the same format as the `dm' `AVERAGE' card). This card is followed
   by <nncs> rotation/translation matrices on subsequent lines in either
   CCP4 or O/RAVE format.
   
   CCP4 Formats (see also lsqkab):
          

ROTATE EULER <alpha> <beta> <gamma>     (Euler angles)
TRANSLATE <t1> <t2> <t3>

   or
          

ROTATE POLAR <omega> <phi> <kappa>      (Polar angles)
TRANSLATE <t1> <t2> <t3>

   or
          

ROTATE MATRIX <r11> <r12> <r13> <r21> <r22> <r23> <r31> <r32> <r33>
TRANSLATE <t1> <t2> <t3>

   O/RAVE Format
          OMAT
          <r11> <r21> <r31>
          <r12> <r22> <r32>
          <r13> <r23> <r33>
          <t1> <t2> <t3>
          where
          x' = <r11>x + <r12>y + <r13>z + <t1>
          y' = <r21>x + <r22>y + <r23>z + <t2>
          z' = <r31>x + <r32>y + <r33>z + <t3>
          (note that the rotation matrix is transposed with respect to
          CCP4 matrix format.)
          
   These are the operations which map the density in the region covered
   by the input mask onto the other equivalent regions. The first
   operator must be the identity matrix. The mask is input in CCP4 mask
   format on the input file label MSKIN, and should cover just one
   monomer or averaging domain, NOT the whole unit cell.
   
  MONOMER
  
   Reduce a multimer mask to cover only a monomer. This option will
   generate a mask covering an arbitrarily chosen monomer from a multimer
   in the case where the NCS consists ONLY of a SINGLE PROPER ROTATION
   AXIS of any order. An arbitrary segment covering an angle of
   2*pi/<nncs> is selected and the rest of the mask is removed.
   
  OVERLAP [ <ncycle> ]
  
   Perform overlap removal. Overlap removal will be performed by removing
   pixels from the surface of the mask. The mask is overlapped with its
   crystallographic- and non-crystallographic symmetry related partners
   (see SYMMETRY and AVER cards). The overlap removal calculation may not
   remove all overlap on the first cycle, if <ncycle> is specified,
   overlap removal will be repeated this number of times.
   
  NOTRIM
  
   Disable mask trimming. The default is to reduce the mask extent to
   obtain the minimum box which will contain the final output mask. With
   NOTRIM, the mask extent will be the same as the input mask or the
   values on the XYZLIM card if it is present.
   
NOTES

   The calculations are performed in the following order:
    1. Mask input/generation
    2. Peak picking
    3. Expansion/Contraction
    4. Smoothing
    5. Monomer generation
    6. Overlap removal
    7. Extent trimming
       
   If you want to do them in a different order, run the program several
   times.
   
   Read your output. When removing overlap, check that the input and
   output masks fill a sensible volume of the unit cell. Don't complain
   until you have done this.
   
EXAMPLES

   To remove the overlap from a mask for input to `dm':
#
ncsmask mskin ins.msk mskout ins1.msk << eof
AVERAGE 2
OMAT
 1.000  0.000  0.000
 0.000  1.000  0.000
 0.000  0.000  1.000
 0.000  0.000  0.000
OMAT
 -0.88284    -0.46960    -0.00849
 -0.46899     0.88238    -0.03808
  0.02537    -0.02964    -0.99924
 82.80000     0.10000   -34.10000
OVERLAP
END
eof

   To make a mask from pdb file and remove overlap (note that `dm'
   doesn't care about the grid on which input masks are calculated):
   
#
ncsmask xyzin ins.pdb mskout ins1.msk << eof
SYMMETRY R3
RADIUS 3.0
AVERAGE 2
ROTATE EULER 0.0 0.0 0.0
TRANSLATE 0.0 0.0 0.0
ROTATE EULER -29.6  180.0    0.0
TRANSLATE 0.3  0.1 -0.1
OVERLAP
END
eof

SEE ALSO

   dm, lsqkab, mapmask, maprot, bones2pdb.