POSTREF (CCP4: Unsupported Program)

NAME

   postref - Post-refinement of reflection data

SYNOPSIS

   postref hklin foo_in.mtz hklout foo_out.mtz
   [Key-worded input file]

DESCRIPTION

   This program refines orientation and cell parameters for one or more
   rotation film packs, by comparing the intensities of partial
   reflections with a reference intensity.

KEY WORDED INPUT

   Most cards are optional (except BATCH), and all are free format, with
   fields separated by 'space'. Cards may be in any order, except for
   BATCH and END. Any keyword may be abbreviated to 4 letters, and they
   are case-insensitive. Data for any card may be continued if necessary
   on the next line, by the character '-' or '&' at the end of the line.

   The following keywords are available

       TITLE       ROCK          BEAM         MOSAICITY     SDFAC
       REFINE      CONSTRAINT    FIX          FREE          DELAY
       REJECT      RESOLUTION    PRINT        DEBUG         REFMEAN
       REFSUM      REFALL        WAVELENGTH   CELL          MISSET
       SCALE       OUTPUT        INSCALE      BATCH         CRYSTAL
       END

  TITLE title

   Title to write to printer output.

  ROCK keyword(s)

   Rocking curve keywords are STEP, COSINE (default) or TANH for square
   profile, cosine profile, or hyperbolic tangent profile respectively,
   and ISOTROPIC (default) or ANISOTROPIC for isotropic or anisotropic
   divergence refinement. If present, STEP, COSINE or TANH must precede
   ISOTROPIC or ANISOTROPIC.

   ISOTROPIC is equivalent to
     FREE ET
     FIX  DH DV DL CD

   ANISOTROPIC is equivalent to
 
     FREE DH DV
     FIX  ET DL CD

   For the tanh profile, the TANH keyword may be followed by the keyword
   WTANH (alias LIMIT) and a value for the truncation limit WTANH ( = w
   in section following expression (c) above) which is used to make the
   tanh function into a bounded curve; and the keyword QTANH (alias
   SCALE) may be followed by a scale factor for the argument of the tanh
   function ( = q in expression (c) above): the refined value of the
   reflection width or divergence will be dependent on the value of w/q,
   since as w is increased, more of the tail of the profile is included
   in the reflection width. The default value of w = WTANH = 2.7 (
   tanh(2.7) = 0.991 ), which means that the curve is truncated at Pcal =
   0.0045 and Pcal = 0.9955. The default value of q = QTANH = 2.0

  MOSAICITY <eta>

   Specify crystal mosacity eta (degrees) to override value in file

  BEAM [FILE] | [<DH> <DV> <DL> <CD>]

   Define beam parameters to override values in file.

   If the keyword FILE is given, the beam parameters and mosaicity will
   be picked up from the input file (from OSCGEN and ABSCALE) (this the
   default).

   DH
          horizontal beam divergence (degrees)

   DV
          vertical beam divergence (degrees)

   DL
          delta(lambda)/lambda = dispersion

   CD
          correlated component of the spectral dispersion

  FIX or FREE followed by labels

   Specifies which parameters are to be refined. The 2-character
   parameter labels are:
          A*, B*, C*   cell edges
 
          AA, BA, GA   cell angles
 
          WL           wavelength
 
          ZM, ZD       mean and difference of epsilon-z
 
          YM, YD       mean and difference of epsilon-y
 
          ET           mosaicity (eta)
 
          DH, DV       horizontal, vertical beam divergence

          DL           dispersion, delta lambda/lambda (leave fixed)

          CD           correlated dispersion (leave fixed)

   The keywords FIX or FREE may be mixed with parameter labels to specify
   the status of subsequent parameters given on the card.

   Defaults: cell parameters normally default to the flags given in the
   orientation block, but if any cell parameter label is given here, all
   the cell parameters will default to free. The cell flags in the file
   also indicate constraints tying cell edges together (eg a* = b* ):
   these constraints are not affected by FIX or FREE cards. Other
   parameters are by default fixed except for ZM, YM and ET (or DH & DV
   if the divergence is anisotropic: a ROCK ... ANISOTROPIC card sets DH
   & DV free and fixes ET). If WL is free, the cell edges A*, B* and C*
   are automatically fixed. You would be ill-advised (probably) to refine
   beam parameters other than ET or DH+DV.

  DELAY label delay ....

   This card takes a series of pairs of parameter-label, 'LABEL', (see
   FIX card) and a number DELAY, which makes that parameter fixed for the
   first DELAY cycles, after which it reverts to its staus as defined by
   FIX and FREE cards. All delays default to zero.

  CONSTRAINT icon(1) ... icon(6)

   Set cell constraint flags to override those derived from the input
   file. If ICON(I) = J, the I'th cell dimension is constrained to equal
   the J'th: normal values are 1 2 3 4 5 6 .

  REFINE ncyc convrg fltlim fltstt fltdec

   NCYC is the number of cycles (defaults to 8).

   CONVRG is a convergence limit (default = 0.02); the refinement has
   converged if the change of SIG = Sqrt ( Sum ( w del**2 ) ) / (Nobs -
   Npar) is less than CONVRG.

   FLTLIM, FLTSTT, FLTDEC. The filter-level is the amount added to all
   eigenvalues to speed convergence: it has the effect of damping shifts
   in the directions corresponding to small eigenvalues. The filter level
   starts at FLTSTT, and is decremented by FLTDEC until it reaches FLTLIM
   (defaults 0.0,0.05,0.02)

  REJECT fincr rejfac(1) rejfac(2) cutoff rejang frlow frdec rejsd frclim

   Reflection rejection limits etc.

   FINCR
          Intensity increment for analysis against intensity (default =
          1000). Used only when PRINT is set to ANALYSIS or FULL. Max.
          no. of bins fixed at 12.

   REJFAC(1)
          reject reflections with Iobs < REJFAC(1) * sd(Iobs) (default =
          0) The refinement seems to converge best with all data
          included.

   REJFAC(2)
          reject reflections with Iref < REJFAC(2) * sd(Iref) (default =
          0)

   CUTOFF
          reject reflections with sd(fraction obs) > CUTOFF (default=0.5)

   REJANG
          reject reflection closer than REJANG degrees to the rotation
          axis on the film (default = 3 degrees)

   FRLOW,FRDEC
          define which non-fractional reflections are used. In each
          cycle, reflections are used with calculated fraction Pcal such
          that

         -FRL < Pcal < 1 + FRL

          FRL starts at FRLOW on the first cycle, and is decremented by
          FRDEC on each cycle until FRL = 0.0. This allows reflections
          which are just outside the fractional range to be used in the
          early cycles, in case they are really fractional. These
          reflections are weighted by

 
      (1 - exp( - (delta I)**2/2(sd(I))**2 ) )

          to weight down those reflections which are really
          non-fractional. (Defaults 0.0, 0.0)

   REJSD
          reject reflections for which Pobs - Pcal > REJSD * sd(Pobs)
          (default = 10.0)

   FRCLIM
          omit reflections altogether from calculation if the calculated
          fraction in the input file FRACTIONCALC is greater than FRCLIM.
          If this fraction is reliable, leaving out the safe fully
          recorded reflections speeds up the calculation considerably.

  REFMEAN

   Use mean of safe fully recorded reflections (IMEAN) as reference
   intensity (default, cards REFSUM and REFALL are alternatives).

  REFSUM

   Use summed partials (ISUM) as reference intensity.

  REFALL

   Use summed partials (ISUM) as reference intensity if present,
   otherwise IMEAN

  RESOLUTION res1 [res2]

   RES1,RES2. Set resolution limits in Angstrom, either order. If only
   one number given, use as high resolution limit. Default, use all data.

  SDFAC sdfac sdadd

   Read modification factors for standard deviation of Iobs, as for
   ROTAVATA and AGROVATA.

   Variance(Iobs):= SDFAC**2 ( Var(Iobs) + (SDADD * Iobs)**2 )

   (Default 1.0, 0.0 ie no change)

  CELL a b c [alpha beta gamma]

   Read real cell dimensions (Angstrom and degrees) to override those on
   the file. Angles default to 90. This needs to be repeated for each
   CRYSTAL card.

  WAVELENGTH wavelength

   WAVELENGTH is the wavelength in Angstrom to override value in file. If
   this card is present but no value is given, the wavelength is set to
   1.54182 (Cu Kalpha). This needs to be repeated for each CRYSTAL card.

  MISSET phix phiy phiz [phix2 phiy2 phiz2]

   Read mis-setting angles (degrees) to override those in the file. Two
   different sets of three angles may be specified, corresponding to the
   start and finish of the rotation range (phi1 and phi2). By default,
   the two sets are equal (ie no crystal slippage). This needs to be
   repeated for each CRYSTAL card.

  SCALE scale bfac

   Read scale and temperature factor for the next batch, to override the
   values in the file. If this card is present, the next BATCH card must
   specify one batch only.

  OUTPUT [keyword]

   The keyword OFF switches off output of reflections to the output MTZ
   file. The keyword ALL makes the program copy all batches to the output
   file, even if they are not refined. An OUTPUT card with no keyword
   resets the default option, to write to the output file only those
   batches which are refined.

  INSCALE [keyword]

   By default, a scale correction is applied if a column SCALE is present
   in the file. The INSCALE card switches the application of this scale
   off or on again. Keywords OFF or ON may be present, otherwise the card
   switches to the opposite state

  PRINT keyword

   Set amount of analysis etc printed. The optional keywords are:

   BRIEF
          (default) minimal output, prints only the analysis against
          fraction

   SHIFTS
          (or PRINT with no keyword) prints also the shifts on EACH cycle
          and the orientation data from the header records for each
          batch.

   ANALYSIS
          additional extensive analysis after the last cycle (this is
          worth doing for at least a few films).

   FULL
          is equivalent to both SHIFTS and ANALYSIS

   REFLECTIONS
          in addition to the FULL analysis, all reflections are printed
          on the last cycle.

   VECTORS
          prints eigenvectors of normal matrix on last cycle, as well as
          eigenvalues.

  DEBUG ibug

   Set debug flag to give extensive (!) output for debugging.

  BATCH [ batch-specification ]

   This card is an alternative to the CRYSTAL card, specifies which
   batches are to be refined as independent films, and refines them. Note
   that unlike other cards which specify parameters or flags, the BATCH
   card tells the program to refine the specified batches, after which
   further cards are read to change parameters and refine more batches if
   required. Batches must always be specified in the order they occur in
   the file, ie in ascending order of batch number.

   Specification of batches

   (a)
          ALL all batches (default if no keyword on BATCH card)

   (b)
          list of batches n1 n2 n3 etc

   (c)
          range of batches n1 TO n2

   (d)
          EXCLUDE with list n1 n2 n3 etc This may follow ALL or a range.

  CRYSTAL [keywords] batch-specification

   This card is an alternative to BATCH, and specifies a group of films
   to be refined together (up to 50). The batch specifications are the
   same as for the BATCH card. By default, mis-setting angles and rocking
   curve parameters are refined independently for each film. The keyword
   ONEMISSET causes the same set of mis-setting angles to be refined for
   all files, and the keyword ONEROCK the same set of rocking curve
   parameters. Both keywords may be present. Note that the ONEMISSET
   option will not work well with a set of films covering a large
   rotation angle, since the refinement of misseting within each cycle is
   done in the camera frame rather than the crystal frame.

  END

   This terminates the program. Alternatively, the program ends on
   end-of-file on stream 5. If OUTPUT ALL was specified, any remaining
   unrefined batches in the file are copied to the output file.

INPUT AND OUTPUT FILES

   Input Files

     The control data file

     HKLIN The input reflection data file. This is a multi-record MTZ
     file (See section PROGRAM FUNCTION for details)

   Output Files

     HKLOUT The output reflection data file. This is a multi-record MTZ
     file (See section PROGRAM FUNCTION for details)

PRINTER OUTPUT

   Comments on the printer output

   Definitions of statistics:
Avdel = 1/n Sum  delta I
 
Avsd  = 1/n Sum sqrt(1/weight)
 
rmsdel= sqrt( 1/n Sum(delta I **2) )
 
rmsesd= sqrt( 1/n Sum(1/weight) )
 
      = sqrt( 1/n Sum( Var(Iobs)) )
 
RDEL    = Rfactor = Sum  Icorr - Iref  / Sum  Iref
 
RSIG    = fractional mean sd(Icorr-Iref)
 
        = Sum{sqrt[Var(Iobs)/(Pcal**2) + Var(Iref)]} / Sum Iref
 
RDEL and RSIG exclude reflections with Pcal < 0.1
 
DPER    = weighted mean delta(fraction)
 
        = Sum[(Pobs - Pcal)/Var(Pobs)] / Sum[1/Var(Pobs)]
 
ADPER   = weighted mean  delta(fraction)
 
        = Sum[ Pobs - Pcal /Var(Pobs)] / Sum[1/Var(Pobs)]
 
ESD     = rms sd(fraction) = sqrt[Sum Var(Pobs)/n]
 
RMS     = rms delta(fraction) = sqrt[Sum(Pobs-Pcal)**2/n]
 
Q = S/NR = mean delta(fraction)**2/variance
 
         = 1/n Sum[(Pobs-Pcal)**2 / Var(Pobs)]
 
For all statistics, Pcal = 1 for a fully recorded reflection,
 
                         = 0 for a non-recorded one.

ERROR MESSAGES

   Data control card errors
!!!! Keyword KEY not recognised !!!!
 
!!!! Syntax error on card !!!!
 
!!!!!! Unrecognised parameter label: LABEL         (FIX/FREE/DELAY)
 
!!!! Scale card is only valid with one batch specified on card !!!!
 
Errors in opening units
 
STOP **UNABLE TO OPEN UNIT 5 OR 6**
 
STOP **UNABLE TO OPEN UNIT 9**
 
Too many parameters
 
!!!!! Too many free parameters, maximum is N
 
Problems with the Batch Handling
 
!!!! Too many batches in list: N
 
!!!!! No orientation data found for batch N
 
!!!!! Too many films for this crystal, maximum = N
 
NB batch N has no reflections contributing to refinement !!!!
 
**** Batch number not found in file ****
 
!!! Error in batch titles in NEWFIL !!!
 
Point Group dictionary
 
Point group PG not found in library !!!!
 
!!!!!!! Warning: point group name was previously set to PG !!!!!!!!
 
Matrix handling
 
!!!!!! Symmetry matrix is singular !!!!!!
 
MTZ file errors
 
!!!!! First five columns of input file are out of order Nq1 N2 N3 N4 N5
 
Error on reading MTZ file: Error no. N

   Error messages may also be produced by the MTZ file handling routines.
   These start with the message **MTZ ERROR** and are documented
   elsewhere.

PROGRAM FUNCTION

   This program is based on the post-refinement program by Winkler and
   Schutt (ref. 1). It refines orientation and cell parameters for one or
   more rotation film packs, by comparing the intensities of partial
   reflections with a reference intensity. The reference intensity is
   typically the mean of safe fully recorded reflections from the same or
   different films, or the sum of the spot with its other half. The
   reference intensity and the appropriate scale factor may be provided
   by the program ROTAVATA.

   The residual minimized is

           Sum w ( Iobs - Pcal Iref )**2

   where the calculated fraction Pcal is a function of the following
   parameters:

     Cell dimensions

     Wavelength (as an alternative to cell edges)

     Misorientation angles phi-z, phi-y, phi-x (optionally different at
     the two ends of the rotation range). Within each cycle the program
     refines the mis-setting angles in the camera frame epsilon-z and
     epsilon-y (ZM and YM), and optionally their difference ZD and YD,
     then rotates the epsilon shifts into the reference frame (phi-z,
     phi-y, phi-x ) after each cycle.

     Rocking curve parameters (divergence and dispersion)

   The program may refine each film pack (batch) seperately, or a group
   of films (up to 50) may be refined together with the same cell
   dimensions, with the same or different mis-setting angles and rocking
   curve parameters (see CRYSTAL card).

   The program allows three alternative forms of rocking curve to relate
   the angular fraction to the intensity fraction: both have a finite
   angular width 2g, such that the intensity fraction

          Pcal = 1/2 ( 1 +- f(b) )

   where b is the angular fraction (ie fraction of g) = delta beta / g

      (a) square profile   f(b) = b
 
      (b) cosine profile   f(b) = sin ( b * pi/2 )
 
      (c) hyperbolic tangent profile f(b) = tanh ( q * b )
 
          where q = QTANH is a scale for the tanh function (see ROCK card).
 

   Note that function (b) is defined only for -1 < b < 1 and (c) for b <
   (w/q): otherwise function (a) is used. The tanh function (c) is
   equivalent to a peak with tails compared to the cosine function. For
   the tanh profile, b = (w/q)*(delta beta / g ), and b is truncated at b
   = w/q : w = WTANH is the truncation limit (see ROCK card). This
   scaling ( parameters w and q ) makes the divergence for the tanh
   function more comparable with that for the cosine curve.

   The reflection width g includes a dispersion term, and may be
   anisotropic.
 
   g = 1/2 * ( sqrt( (2  TANtheta  *  CD  +  DH  COSalpha)**2  +  (DV  *
       SINalpha)**2) + ET + DL * TANtheta )

   see Greenhough & Helliwell (ref. 2) and Greenhough (ref. 3) (see BEAM
   card) where alpha = (tan)**-1 y/z , the azimuthal angle on the film.
   Note that g is the half-width of the reflection, but the rocking-curve
   parameters ET, DH & DV refer to the full-width of the reflection.

  A note on convergence

   If the program is refining parameters for one film at a time, some
   parameters are poorly determined. This may not be too serious, since
   we are not interested in the parameters themselves, but only in the
   fractionality calculated for each reflection from the parameters. In
   particular, the mis-setting angle about the rotation axis phi-z
   (epsilon-z) is correlated with the cell dimensions perpendicular to
   the rotation axis. Cell angles are even more correlated, and it is
   doubtful whether cell angles can be refined sensibly with only one
   film. The program has three facilities which may assist convergence.

   a)
          Eigenvalue filtering (see REFINE card)
          A number (filter) may be added to all eigenvalues of the normal
          matrix during the calculation of shifts. This is equivalent to
          adding the filter value to all diagonal elements of the normal
          matrix (Marquardt method), and has the effect of damping shifts
          in the direction corresponding to the smallest eigenvalues. The
          filtering seems useful on the first few cycles, to allow the
          most sensitive parameters to refine first, but it is best
          decremented to zero after 3 or 4 cycles (as is done in the
          default settings).

   b)
          Parameter delay (see DELAY card)
          Any parameter may be fixed for the first few cycles. This may
          be useful for the parameters ZD and YD, which define the
          difference of orientation at the beginning and end of the
          rotation range.

   c)
          Inclusion of reflections which are not partial, but are nearly
          so. (parameters FRLOW and FRDEC on REJECT card)
          It is possible to include reflections bordering on the partial
          in the early cycles, since they may become partial as the
          parameters change. This seems not to be helpful, but may be in
          some cases

  Details of input reflection file

   The input MTZ file may be prepared by ROTAVATA and SORTMTZ. It
   contains a series of films (batches) which are processed sequentially,
   although individual batches may be selected for inclusion or
   exclusion. The file must be sorted with BATCH as the most significant
   key. The file is expected to contain columns
H K L M/ISYM BATCH I SIGI FRACTIONCALC IMEAN SIGIMEAN ISUM SIGISUM

   where IMEAN and ISUM are alternative reference intensities,
   respectively the mean of the safe fully recorded reflections, and the
   sum of the two adjacent partials.

   The file should also a batch header and orientation block for each
   batch. The orientation block contains starting values of the
   orientation parameters, constraint flags for cell parameters, and the
   relative scale and temperature factor (from ROTAVATA) to put this
   batch on the same scale as the reference intensity. The orientation
   blocks are put into the file by ABSCALE. The orientation parameters in
   the file may be overridden by control data (see above).

   Orientation data (see also libmtz.doc)

       1.  6 cell dimensions (Angstrom and degrees,  real  numbers).  These
           cell dimensions define an orthogonalization matrix B to  convert
           indices hkl to Cartesian crystal axes xyz
 
           x  =  B  h
 
           B = (a*        b* cos gamma*    c* cos beta*            )
               (0         b* sin gamma*   -c* sin beta* cos alpha  )
               (0               0             lambda / c           )

                                               (Busing & Levy 1967)
 
           This gives x parallel to a*, and y in the a* b* plane.
 
       2.  6 cell dimension flags (integer) defining which parameters may
           be varied.
 
               Flag = -1       parameter is freely variable
 
                    =  0       parameter is fixed (ie cell angle  =  90  or
                               120)
 
                    = I(.gt.0) parameter is constrained to  have  the  same
                                value as parameter number I .
 
       3.  Orthonormal matrix U (9 real numbers in order U11, U12, U13, U21
           etc) to rotate the crystal Cartesian coordinates to  the  camera
           Cartesian coordinates. The IDXREF matrix is A = U B . The matrix
           U defines a standard orientation,  and  is  a  function  of  the
           mounting axis and the axis defined as phi = 0 , but  it  is  not
           dependent on the misorientation angles. Typically, U will  be  a
           permutation matrix.
 
       4.  JUMPAX, the 'mounting' axis, as defined for  OSCGEN  (1,2,3  for
           h,k,l) (not used)
 
       5.  6 misorientation angles, rotation  axis  mis-setting  (6
           real numbers):
 
                 PHIX1 , PHIY1 , PHIZ1 , PHIX2 , PHIY2 , PHIZ2 
 
           The first three refer to the orientation at the beginning of the
           rotation range (at phistart), the second three  phi  angles  (if
           present) refer to to the end of the rotation range (at  phiend).
           The second set should be set  equal  to  the  first  set  if  no
           crystal slippage is assumed.
 
       6.  Start and stop rotation angles.  (  2  real  numbers)  phistart,
           phiend
 
       7.  crystal mosaicity in degrees 
 
       8.  lambda, delta lambda/lambda, correlated dispersion
 
       9.  Scale , Temperature factors for this batch ( from Rotavata etc).
           The correction to be applied is
 
                 SC * exp ( -2 * B * (sin theta/lambda)**2 )
 

  Details of output reflection file

   The output MTZ file is similar in structure to the input file. The
   refined orientation parameters are placed in the orientation block.
   For each reflection, the calculated fraction and its standard
   deviation are placed in columns labelled FRACTIONCALC and
   SIGFRACTCALC, and the partial flag M is updated (in column M/ISYM).
   Valid values of M are:

                   M = 0  fully recorded
 
                     = 1  partial ( 0  =< P < 1.0 )
 
                     = 2  not recorded ( P < 0 )
 
                     = 3  partial at both ends of the range
 
                     = 4  too near axis (see REJANG above on REJECT) card

   Reflections with M > 1 will be rejected in AGROVATA.

REFERENCES

    1. Winkler F.K., Schutt C.E. & Harrison S.C., Acta Cryst., (1979),
       A35, 901 - 911.
    2. Greenhough T.J. & Helliwell J.R., J. Appl. Cryst., (1982), 15, 493
       - 508
    3. Greenhough T.J., CCP4 Information Quarterly for Protein
       Crystallography, Feb. 1983, Daresbury Laboratory.

AUTHORS

   Originator : Winkler and Schutt
   Availability : Fortran77/vms/unix
   Contact : Phil Evans, MRC Cambridge

EXAMPLES

   Example 1.

!
! Sort output file from Rotavata for postrefinement
!
$SORTMTZ HKLIN RPFKPRF2 HKLOUT RPFKPRF2S BATCH H K L M/ISYM
!
! Now postrefine
!
$POSTREF HKLIN RPFKPRF2S HKLOUT RPFKPRFT6
TITLE PFK R-native, 2nd postrefine rescaled, averaged cell, tanh 2.3
POINTGROUP PG222
FREE WL
FIX A* B* C* AA BA GA
REFINE 20 0.01 0.0 0.05 0.02
ROCK TANH LIMIT 2.3
REJECT 1000 0 0 0.5 10 
CELL 122.17 84.30 61.26
BATCH 200 TO 299
CELL 122.84 84.39 61.60
BATCH 300 TO 399
CELL 122.67 84.39 61.53
BATCH 400 TO 499
CELL 122.67 84.20 61.59
BATCH 500 TO 599
CELL 122.77 84.10 61.86
BATCH 600 TO 699
CELL 122.70 84.64 61.52
BATCH 700 TO 799
!
! Resort data ready for Agrovata or Rotavata
!
$SORT: SORTMTZ HKLIN RPFKPRFT6 HKLOUT RPFKPFTS6 H K L M/ISYM BATCH

   Example 2.

$SORTMTZ HKLIN ROTSTR3 HKLOUT ROTSORT BATCH H K L M/ISYM
$POSTREF HKLIN ROTSORT HKLOUT PREFSTR2
TITLE STR-ATP C* POSTREF
POINTGROUP PG222
ROCK TANH LIMIT 2.5
CRYSTAL ONEROCK 1391 TO 1394
CRYSTAL ONEROCK 1501 TO 1504
CRYSTAL ONEROCK 1521 TO 1524
CRYSTAL ONEROCK 1531 TO 1535
CRYSTAL ONEROCK 1541 TO 1543
CRYSTAL ONEROCK 1545 TO 1548
CRYSTAL ONEROCK 1551 TO 1555
CRYSTAL ONEROCK 1561 TO 1564
CRYSTAL ONEROCK 1567 TO 1569
END
.

   Example 3.

#!/bin/csh -f
#
#  Recycle Rotavata & Postref
#
# Number of cycles controlled by parameters in next few lines
#   To do final merge, set cycle = maxcycle
#
cd $scr0
set dataset = bst
set cycle = 3
set nextcycle = $cycle           # For final merging only: else reset below
set maxcycle = 3
set saved = /ss1/pre/pfk/bst

# Following line to do final merge
if ($cycle == $maxcycle && $cycle != 1) then
 goto agro
endif


#  Skip initial Rotavata if restarting after cycle 1

if ($cycle == 1) then

rotavata  hklin  ${saved}/${dataset}_sort  
   hklout ${dataset}_save_${cycle}  
          scales  ${dataset}_${cycle}.scales << end_rota
title BST PFK T9 + T10
batches 100
bins    10
brefine on
cycles  5
scale unity
output  postref
resolution 20 2.6
rejlim 4
width  1500
intensities  profile
process  full  partial
sdinflate  sdfac = 1 sdadd = 0.04
anomalous off
records  truncate
end_rota

endif

########### Return here for next cycle
cycle:
echo =============================================================
echo 
echo    Postrefinement cycle $cycle 
echo 
echo =============================================================

@ nextcycle = $cycle + 1

#  Sort for Postref on BATCH
#
sortmtz hklin  ${dataset}_save_${cycle} 
        hklout ${dataset}_prfrs_${cycle} << eof-sort
BATCH H K L M/ISYM
eof-sort

postref:
postref hklin  ${dataset}_prfrs_${cycle} 
        hklout ${dataset}_savep_${cycle} 
 summary ${saved}/${dataset}_${cycle}.prfsum << eof-prf
Title  PFK B.st T-state crystals  T9 & T10 cycle ${cycle}
rock tanh limit 2.3 isotropic
crystal 900 to 944
crystal 1000 to 1042
eof-prf

# Resort for Rotavata
#
sortmtz hklin  ${dataset}_savep_${cycle} 
        hklout ${dataset}_prfs_${cycle} << eof-s1
H K L M/ISYM BATCH
eof-s1

rota:
rotavata  hklin  ${dataset}_prfs_${cycle}  
   hklout ${dataset}_save_${nextcycle}  
          scales  ${saved}/${dataset}_${cycle}.scales << end_rota
title BST PFK T9 + T10
batches 100
bins    10
brefine on
cycles  5
scale postref
output  postref
resolution 20 2.6
rejlim 4
width  1500
intensities  profile
process  full  partial
sdinflate  sdfac = 1 sdadd = 0.04
anomalous off
records  truncate
end_rota

end_cycle:
# Clean up unwanted files
 /bin/rm ${dataset}_prf*

# Recycle if required

if ($cycle < $maxcycle) then
 @ cycle = $cycle + 1
 goto cycle
endif


time

##exit


##############################################################
#
#  Final merging
#

agro:

agrovata  hklin ${dataset}_save_${nextcycle}  
                hklout ${saved}/${dataset}_merge <<end-agro
@${saved}/${dataset}_${cycle}.scales
intensities profile
process full partial all
frmin 0.7
end-agro
#
exit

time

trunc:
truncate  hklin  ${saved}/${dataset}_merge 
          hklout ${saved}/${dataset}_F <<EOF-trunc
title BST PFK T9 + T10
wilson
#resolution  
nresidue   1280
labout  F=FT SIGF=SIGFT
EOF-trunc


time

   Example 4:

#!/bin/csh -f
#
#  Postrefinement
#
#
#  First resort data on batch
sortmtz hklin $scr0/cx88_scl1 hklout $scr0/bc93_s << eof-1
BATCH  H K L M/ISYM
eof-1

# now for Postref
postref hklin $scr0/bc93_s hklout $scr0/bc93_p << eof-2
Title  Postrefinement B.st. PFK C2

rock   tanh  isotropic
!beam 0.03 0.01
refine 6
refall
sdfac  0.8 0.08
crystal  61   to  699
crystal  701  to  799
crystal  811  to  899
crystal  911  to  999
crystal 1111  to 1199
crystal onemisset 1311  to 1319
crystal 1321  to 1399
crystat 2011  to 2099
crystal 2111  to 2199
eof-2
#

#
# exit
#

# sort back for Rotavata
sortmtz hklin $scr0/bc93_p hklout $scr0/bc93_post << eof-3
H K L M/ISYM BATCH
eof-3