NAME
       ribbon  -  Stereo Cartoons of Protein Structures



SYNOPSIS
       ribbon

	    This document describes  a	procedure  for	producing
       stereo  Jane Richardson-type  cartoon  drawings	of   pro-
       tein   structures.   These can either be	rendered as black
       and white plots suitable	for publication	  or  as   "back-
       ground"	 pictures   on	an  Evans  and	Sutherland  PS300
       series graphics display system  with  the  program  FRODO.
       Such  a	picture	 can then be easily photographed directly
       from the	screen for making color	slides.	 The  first  fol-
       lowing  reference  is suggested	for  familiarizing  your-
       self with these types of	cartoons in general.  The  second
       reference describes the programs	in this	suite more fully.

       Jane S. Richardson (1985) Methods Enzymol. 115 359-380.

       John P. Priestle	(1988) J. Appl.	Cryst. 21 572-576.

	    The	procedure consists of five to seven  steps  which
       are  described briefly below and	in detail further on:

	    1) Executing a program called RIBBON.  For this  pro-
       gram  you  will need  a	set  of	 coordinates  in  Protein
       Data  Bank format.  Only	C-alphas are used.  You	also need
       the first and last residues  of	the  secondary structural
       elements	  (alpha-helices,  beta-sheets and reverse turns)
       as well as any breaks in	the structure, e.g. if more  than
       one   subunit   is  present  or for a protein-protein com-
       plex.  From these, RIBBON creates a set of coordinates for
       a preliminary Jane Richardson-type drawing.

	    2)	Executing  the	program	RIBROT which rotates  the
       ribbon  drawing and writes out a	preliminary plotfile.

	    3) Executing  a  program  called  POSTPLOT	with  the
       RIBROT plotfile	as input.   This program adds perspective
       to the random coil regions of the structure (if	desired),
       removes	"hidden"  lines	 and   creates	two  output plot-
       files,  one  each  for  the right and  left  stereo  views
       (or only	one mono-plot if so desired).

	    4) Executing a program called SPLITD (optional) which
       divides	the  plot   file   according  to  sequence  (e.g.
       domains or subunits) rather than	by secondary structure.

	    5)	Executing PLTOUT, which	creates	either a file  to
       plot  on	 the terminal,	background  ("MOL")   files   for
       FRODO, or a file	for a paper plotter.

	    6)	Displaying  the	 picture   on	the  terminal,	a
       graphics	 display system	 with  FRODO  or,  plotting   the
       file  out onto paper.  The FRODO	option was created by Dr.
       Geoffry Ford (Sheffield Univ.) and  was	later expanded by
       the author.
	    7)	If the picture is plotted  for	publication  pur-
       poses,  it  will	probably be necessary to add  some  final
       touches by hand.



PROGRAM-FLOW
       ribbon

	Program	|Input |Output | Other	    | Main Function
		| File | File  | Parameters |
		|      |       |	    |
		|      |       |	    |
		|      |       |	    |
	RIBBON	|X.PDB |X.RIB  |Secondary   |Makes preliminary
		|      |       | structure  |picture
		|      |       |	    |
	RIBROT	|X.RIB |X.ROT  |View matrix |Rotates picture
		|      |       |  (angles)  |
		|      |       |	    |
	POSTPLOT|X.ROT |X.PST  |No. of	    |Completes picture
		|      |  or   | shade lines|Removes hidden lines
		|      |XR.PST |	    |Adds shade	lines
		|      |XL.PST |	    |Makes stereo pair
		|      |       |	    |
		|      |       |	    |
	SPLITD	|X.PST |X.SPL  |Splits	    |Splits protein
		|      |       |	    |  by domain, not
		|      |       |	    |	secondary  struc-
       ture
		|      |       |	    |
	PLTOUT	|X.PST |X.SCR  |Outpt device|Prepares output
		| or   |X.COLxx|  type	    | file for FRODO
		|X.SPL |X.HPL  |	    | or plotting
		|      |X.POS  |	    |
		|      |X.PIP  |	    |
		|      |X.FIG  |	    |


DESCRIPTION
       ribbon

	    RIBBON  reads  in  the raw C-alpha coordinates of the
       protein and  the	regions	  of   secondary   structure  and
       creates	a  set	of coordinates for a Jane Richardson-type
       cartoon drawing.	 Since	the  final  product  is	 a quali-
       tative  representation  of the protein structure, the pro-
       gram takes considerable artistic	freedom	with your coordi-
       nates to	produce	a smooth, visually pleasing illustration.
       This is carried out in three steps:

	    1) IDEALIZATION (optional) -  All  1-2  distances  as
       well  as	 1-3,  1-4 and 1-5 distances of	alpha-helices and
       1-3  distances  of  beta-strands	  are	regularized    by
       restraining   them   to	 ideal	values.	  This	procedure
       continues  until	 the  R.M.S. shift is 0.20A or	less  (or
       twenty  cycles).	  Random  coils	are smoothed, so that the
       old zig-zag line	 connecting   the  C-alphas   becomes	a
       graceful	  looping arc.	Sharp turns (e.g., reverse turns)
       tend to be shortened  by	  the	procedure,   hence,   the
       OUTERMOST  residues   (2	  for	a   beta-turn,	 1  for	a
       gamma-turn) can be flagged as reverse turns.  This  simply
       "freezes" their positions.

	    2)	TWO  STRANDS  are created from	the  single  line
       connecting  the C-alphas.   The	 distance   between   the
       strands	 (the  ribbon  edges)  for alpha-helices  can  be
       set  by	the  user.   Beta-sheet	   strands    are  trans-
       formed	into   arrows,	the  width and thickness of which
       again can be set	by the user.  Random coils are this stage
       are also	two-stranded, but with a separation of zero.

	    3)	ROUNDING  of the strands by interpolation to give
       smooth  curves.	The  number  of	 interpolations	 is,   of
       course, under user control with three cycles (7 interpola-
       tion points) sufficient to give the  appearance of  smooth
       curves  in almost all cases.  Larger structures often look
       fine with only two interpolation	passes.	 The two  strands
       are   then   written out	 in  Protein  Data  Bank  format.
       This pseudo-protein is made up of pseudo-alanines with  10
       atoms/residue  named  CA,  CB, CC, CD, CE, CF,  CG, CH, CI
       and CJ.


INPUT:
       ribbon

	       Keyworded.  Read	from a prepared	file.


	   ribbon RIBLP	  ../testout/ribbon.lp
		  RIBDAT  ../example/ribbon.dat
		  XYZIN	  ../example/dhfr.pdb
		  RIBOUT  ../testout/dhfr.rib

	    Each input	line  consists	of  a  KEYWORD	(first	6
       places),	followed by data.   Most  are  optional,  as rea-
       sonable defaults	are predefined,	and  should  be	 included
       only   if   the	 default   values   are	 to  be	 changed.
       Obligatory  are	lines describing the secondary	structure
       of  your	 protein  (ALPHA,  BETA,  REVTRN,  BREAK, GROUP1,
       GROUP2).	  The  order  of the input is unimportant.

	    The	 following  input  lines  define  the	secondary
       structure   of  your protein.   After  the  KEYWORD,  give
       the first and last residue numbers defining that	secondary
       structural  element.   Two  residues sequences  are ALWAYS
       necessary (may be the same residue twice).

	    ALPHA   -  Defines	an  alpha-helix.   Minimum  of	5
       residues.
	    BETA     -	Defines	 a  beta-strand.   Minimum  of	4
       residues.
	    REVTRN - Defines the outtermost residues of	a reverse
       turn.
	    BREAK   -  Defines a break in the chain (e.g. between
       subunits).


	    The	following input	lines allow  special  groups   of
       atoms   to  be carried  along.	See  NOTES  for	 problems
       which may arise.	 After	the  KEYWORD,  give  the  residue
       number  of  that	 special  group.   Only	 ONE residue  per
       GROUP1(2) line, although	up to twenty residues (maximum of
       200  atoms)  can	 belong	 to  a	 group.	  For  black  and
       white  plots,  the assignemnt to	GROUP1 or GROUP2 is unim-
       portant.

		 GROUP1	- Residue belongs to group 1.
		 GROUP2	- Residue belongs to group 2.

	    The	  following   input  lines  control  the  picture
       characteristics.	 All are optional:

	    KEY	WORD	    Allowed Values	  Default Values
	    IDEAL		No data		  Don't	Idealize
	    PASSES		 1 - 4			3
	    SMOOTH		 0 - 4			2
	    ALFWID	       0.0 - 3.5	       2.0
	    BETWID	       0.1 - 4.5	       2.5
	    BETTHK	       0.1 - 3.0	       0.75

       IDEAL

	Flag to	first idealize the C-alpha  structure.	 No  data
       necessary.   If	 this	line   is  missing,  idealization
       will NOT	be preformed, however, a summary of the	 analysis
       of  the input structure	verses ideal  distances	 will  be
       printed	to  help  locate  incorrectly  flagged	secondary
       structure.

       PASSES

	Number of interpolation	passes done during  the	 rounding
       phase.  The  total   number   of	 interpolation	points	=
       (2**MAXPAS)-1.  The arrays are limited to 5000 'atoms' per
       strand,	so  the	 maximum number	 of  passes depends  upon
       the  size  of  your protein.  If	you ask	for more than the
       program can handle, it will reduce it.

       SMOOTH

	Number of cycles for smoothing out  random  coil.   Fewer
       cycles  are more	 realistic,  but  hard	to  follow,  more
       cycles are easy to follow, but may lose desired detail.

       ALFWID

	Width of alpha helical ribbons in Angstroms.

       BETWID

	Width of beta-strand arrows in Angstroms.

       BETTHK

	Thickness of beta-strand arrows	in Angstroms.

	    Reverse turns usually do NOT need to be  flagged,  as
       they are	simply treated as random coil in any case.  Flag-
       ging them as reverse turns only freezes their positions so
       that   they  are	 not  shortened	 during	 the smoothing of
       random coil.

	    No residue	should	be  flagged   as   belonging   to
       more   than   one secondary  structural	element.  If this
       occurs, the program assigns the secondary structural type:

			  beta-sheet > alpha-helix > reverse turn

	    For	reasons	that I haven't fully figured out yet, the
       carboxy	end TWO	residues cannot	be beta-strand.

	    An output file named "RIBBON.LP" of	the terminal out-
       put is  created for a hard copy of the program run.



OUTPUT
	    RIBBON is the only program with a significant  amount
       of  output  that	 should	be examined.  The first	output is
       simply a	summary	of the input.

	    If	the  structure	is  to	be  idealized,	then  the
       results	  of  idealization   are   given.   If	any  dis-
       tances  deviate by more	than  1.0  Angstroms  from  their
       ideal  values,  they are	listed out.   This  list  is also
       given  if  idealization is not requested.   Deviations  of
       more  than  2.0	Angstroms usually indicate that	the  sec-
       ondary  structure  has  been incorrectly	 assigned.   This
       should  be  corrected  and  RIBBON  run again.  For  every
       cycle   of    idealization     some     statistics     are
       listed.	 Idealization	 continues   until   the   R.M.S.
       shift  is  less	than  0.20 Angstroms or	until  a  maximum
       of twenty cycles	are performed.

	    Cycles  of	smoothing  of  the  random coils are per-
       formed.	Listed	out is	 the   average	 deviation   from
       linearity  of  the  random coil regions.	 After two passes
       (default), the deviation	is  typically	less   than   0.5
       Angstrom.

	    The	 angles	made entering and exiting the beta-strand
       arrows (if any are  present) are	then listed  out.   Sharp
       angles  (less  than  110	 degrees) are flagged.	The beta-
       strand should be	shortened by one  residue  in	the  sec-
       ondary	structure   list   and	 RIBBON	 run again to fix
       this.  Remember that a beta-strand must be composed of  at
       least four residues.

	    Lastly,  the  results  of interpolation are	given for
       each of the  two	strands.  The  average	angle  for  every
       three  consecutive points is listed out.	  As  the  struc-
       ture  becomes  smoother,	 these	 should	   approach  lin-
       earity.	  The	starting   average   is	  usually  around
       110-130 degrees.	 After three passes of interpolation  the
       average angle should  be	 around	170  degrees  and  should
       be  roughly  the	same (+/- 1 degree) for	both strands.


NOTES
	    The	 default  values  give	 drawings    that    most
       closely	approximate those of Richardson.  You may want to
       play around some	if you think that they can  be	improved,
       or  if you want something different.  If	 you  give values
       which  are  outside  of	the  accepted  range,	it   will
       be  set appropriately to	the maximum or minimum acceptable
       value.

	    From the input PDB file only C-alphas are used.  Only
       NUMBERS	 are  possible	 in   the  sequence number field.
       Sequences need not  be  numbered	 sequentially,	but  must
       always  increase.   Hence,  a second  chains  cannot start
       with  1	again,	but  must  have, e.g., 500 added  to  its
       sequence	 numbers.   If this is not done, when the program
       encounters  a  sequence number  SMALLER	than  the  previ-
       ous  one,  it  will add the next	100 to following sequence
       numbers	 automatically.	   E.g.	   a   proteinase    plus
       inhibitor,  the	enzyme	is numbered 8 to 316, followed by
       the inhibitor numbered 1	to  58.	  Upon	encountering  the
       inhibitor,  it  will  add  400 (next hundred after 316) to
       it, hence the inhibitor will be numbered	401  to	 458  and
       THESE   numbers	 must	be  used  in  defining	its  sec-
       ondary structure	in RIBBON.DAT.
	    Problems  may  arise  if  special  atom  groups   are
       desired.	  Two  sets (to	 be  colored  differently  later)
       of up to	20 residues and	 200  atoms  each  are	possible.
       These  will  typically be cofactors such	as heme,  but may
       also  be	special	amino  acids,  e.g.   cystein  disulphide
       bridges.	 If special amino acids	are selected, only the C-
       alpha and side chain  atoms are taken.	This  also  means
       that  any special groups	with atom names	'C', selected, in
       the PDB file its	sequence  number  should  continue   from
       the  end	  of   the  protein  (i.e.  not	be 1).	E.g.  for
       the hemoglobin alpha subunit, the protein is numbered from
       1  to 142, the  heme  group  should then	have the sequence
       number 143 (or higher).

	    There is  another  problem	associated   with   amino
       acids   which  are selected  as	special	 groups.  Because
       of smoothing,  the  RIBBON  drawing  may	 no  longer  pass
       exactly	through	 their	original  C-alpha  positions  and
       their side chains will appear to	float  in  space,  uncon-
       nected  to  the main chain.  For	residues in alpha-helices
       this is no problem, as the  helical  ribbon   still   goes
       through	the original C-alpha positions.	 For loops, these
       residues	will be	automatically flagged as "reverse  turns"
       (REVTRN)	 and   have   their  positions frozen so that the
       ribbon  also  passes  through   them.	For   beta-strand
       residues,  this	is  still  a problem  as  the  arrow runs
       smoothly	 through  the  middle  of the old zig-zag and the
       C-alpha	positions  will	be about  an  Angstrom	from  its
       surface.	  Hence,  any selected	 beta-stand   side  chain
       will  not  be connected to it.  Note that idealization can
       also change the original	C-alpha	 positions,  depending on
       how unideal your	structure is.



FRODO
	    FRODO  is	a   molecular  manipulation  program  for
       an  interactive graphics	display	system like the	Evans and
       Sutherland  PS-300  series.   It	 was written by	Dr. Alwyn
       Jones (Methods  Enzymol.	(1985)	115   157-171).	  It   is
       not  included  in  this	program	suite but can be obtained
       from many places.  Some of the various versions	may   not
       accept  the  vectorized background files.

	    It	is  assumed  that  you	are  familiar	with  the
       PS-300  system  and FRODO.
	    Once in FRODO, get in MOL and put the  eight  vector-
       ized   backgrounds  into	 the  eight  different background
       buffers by doing	the following eight times:

       English (Cambridge) version:
	       NAME MOLN (where	N is 1-6)
	       VEC X.COLxxx
	(where X.COLxxx	is one of the output files from	VECTOR
		    option of PLTOUT) American (Rice) version:
	       NAME MOLN (where	N is 1-6)
	       FILE
	       X.COLxxx
	(where -.COLxxx	is one of the output files from	the DSN1
		    option of PLTOUT)

	    The	colors of the  eight  backgrounds  can	 now   be
       varied	with  the dials	 until you're happy.  Simply pho-
       tograph this (Ektachrome	400, f2.8 with 1 second	 exposure
       gives  good  results on our  system).   For  stereo pairs,
       of course, the whole procedure has to be	done twice.
	    The	files are set up so that the standard view  (hit-
       ting  "Z" on  the keyboard)  and	 a center (ACON	(Rice) or
       CENTER (Cambridge)) of 0.,0.,0.	gives  the  proper  view.
       Because	of  the	 hidden	 lines,	 this  is  the	ONLY view
       possible	 (although  rotations  around	Z  are	possible,
       except for stereo pairs which MUST have Y vertical).
	    One	problem	with using the graphics	display	system is
       that  it	 is not	 possible to make final	hand corrections.
       Since  the  idea	 is  to	 make  slides	which	will  not
       undergo	 close	 scrutiny   (rule   of	 thumb	  2  min-
       utes/slide   for	 a  seminar), this is usually not a prob-
       lem.  If	some horrible flaw is present, either  try   cor-
       recting	it  in	the  POSTPLOT output (usually not practi-
       cal as there are	typically some 10,000 vectors  there)  or
       try a slightly different	orientation.


FINAL TOUCHES
	    At	this  point you	should have a stereo picture that
       allows the easy visualization  and  comprehension  of  the
       overall	folding	 and secondary structure of your protein.
       Almost certainly, however, there	 will	also  be   a  few
       minor  imperfections,  especially regarding "hidden" lines
       (both those that	should be and aren't and those	that  are
       and  shouldn't  be).  There  are	surely many ways of deal-
       ing with	these, assuming	one wants  to  take  the  effort.
       Described  below	 is  one  step-by-step procedure that has
       proven successful in the	past.

	    1) Photocopy the original plot , expanding to A3 (16"
       x 11.5").
	    2)	Using  a straightedge and a black pen  (or  felt-
       tip),  carefully	connect	 up  those   lines   which   have
       been  falsely  removed.	 It's often necessary to periodi-
       cally check under a stereo viewer to make sure	that  the
       right  connections  are made.  Lines that have thinned out
       during the photocopying or  elsewhere  can  also	 be  made
       thicker and/or darker at	this point.
	    3)	Careful	 application  of "Tipp-Ex" (also known as
       "White-Out")  to	those	lines	that  should  be  hidden.
       Another	approach to this procedure which allows	for finer
       work is to photocopy the	drawing	(after	step	2  above)
       onto   a	 transparency.	 The  Xeroxing	can be easily and
       finely scratched	away with the  point  of  an  (UNFILLED!)
       fountain	 pen.	 Checking  under a stereo viewer periodi-
       cally is	useful and probably necessary.
	    4) Direct photography of the corrected  transparency,
       with  a	white background underneath.
	    5)	If a mono-slide	(or transparency) is to	be  made,
       coloring	 the picture  can  vastly improve the clarity  of
       the  structure.	 For  example,	beta-strands  and  alpha-
       helices can  be	colored	 differently,  or,  even  better,
       the   inside   and   outside  of	 the alpha-helices can be
       colored slightly	differently as well  as	 the   "surfaces"
       and  "sides"  of	 the beta-strand arrows.



ADVANCED TOPICS
	       Discussed  below	are a few embellishments that can
       be added.

	  LABELS:

	    Adding  labels  to	monoview   drawings   is   easily
       accomplished    with   press-on	 letters.    It	 is  also
       possible	to do this with	stereo	pictures  by  adding  the
       label to	one picture near part of the structure that it is
       identifying.   On  a  lightbox,	align the second  picture
       with  the first such that that part of the structure over-
       laps  (others  parts   will   not  necessarily	overlap).
       Place   the   label to the second picture exactly over the
       label on	the first.  This will cause the	label  to  appear
       at the same depth as the	structure identified.


	    The	 picture on the	graphics display has been rotated
       and translated to  present  the optimal view along  Z  and
       to  be  centered	at 0.,0.,0.  If	you wish to add	labels to
       side chains, disulphide	bridges,  inhibitors, etc.,  they
       must   first   be   brought  into  the same orientation as
       the picture.  The original coordinates  can   be	  rotated
       and   translated	  to  superimpose   on the RIBBON picture
       with the	program	PDBROT.	 The program is	 interactive  and
       needs  only the original	PDB file, the rotation matrix (or
       angles)	used in	RIBROT and the "center of pseudo-protein"
       given at	the end	of RIBBON.LP.  The output is again a nor-
       mal PDB file  which  can	be  read  into FRODO.  The  atoms
       can  then  be  "clicked"	to get labels and the atoms them-
       selves then toggled off.

	  COLORED PLOTS

	    The	 plotfile  X.HPL  from	the  HPPLOT   option   of
       PLTOUT	for   a	Hewlett-Packard	 plotter  currently  uses
       only  the  pen in position 1.  However, whenever	a  change
       occurs  (analogous  to  the  X.COLxx files of the DSN1  or
       VECTOR options),	it is possible to change the  pen  selec-
       tion in the X.HPL file itself with the editor.  Search for
       'SP1;' (Select  Pen  1)	and  change  appropriately  (e.g.
       'SP2;').	  For  plot  files from	X.PST there will be 9 pen
       changes:

	    1.	- edges	of the RIBBON picture
	    2.	- shade	lines for outside of helices.
	    3.	- shade	lines for inside of helices.
	    4.	- shade	lines for random coil regions.
	    5.	- shade	lines for faces	of beta	strands.
	    6.	- shade	lines for sides	of beta	strands.
	    7.	- edge	line  of  helices  and	corners	 of  beta
       strands
	    8.	- special group1 atoms.
	    9.	- special group2 atoms.

	    The	 colors	for 1 and 7 should be the same.	 The last
       'SP0;' returns the pen and should not be	changed.  If  the
       input  file  to PLTOUT was from SPLITD, then there will be
       as many pen changes as pieces and can also  be  similarily
       changed.	  Likewise,  the  output file X.FIG from the FIG-
       URE option of PLTOUT is marked with  ".!	   colxxx   peice
       xx"   where  the	changes	occur and a '.NC2' (for	New Color
       2, or 3,	etc.) can be inserted before running FIGURE.


PROGRAM	SPEEDS
	    Below are  some  comparison	 CPU  times  for  running
       the   various  programs.	   The	test protein was papain	c
       (212 C-alphas) without special groups, the computer was	a
       VAX 8600.

	 RIBBON	(3 interpolation passes).................16.0sec.
	 RIBROT..........................................17.3sec.
	 POSTPLOT
	   No hidden line removal, no shade lines, mono..17.3sec.
	   No hidden line removal, shade lines,	mono.....26.0sec.
	   Hidden line removal,	shade lines, mono.......240.2sec.
	   Hidden line removal,	shade lines, stereo.....472.3sec.
	 SPLITD..........................................40.1sec.
	 PLTOUT	(HPPLOT	option)..........................13.9sec.
		(REGIS option)...........................14.5sec.
		(DSN1 option)............................24.9sec.



AVEAT EMPTOR!
	    No	guarantee  can be given	concerning  the	 results.
       The  programs have  been	 extensively tested, both by  the
       author  and others, and every effort has	been made to make
       the input  straightforward,  but	 there	are   a	 lot   of
       options	 and  possibilities for	mistakes.  Do not combine
       these programs with any older version of	the RIBBON   pro-
       grams  because  subtle changes  have  been made (esp. with
       regard to residue  labels)  which  will	cause  unexpected
       errors  to  occur.   Check carefully that your drawings or
       slides  are  a  true  representation  of	 your  structure.
       Any   problems,	questions,  comments,  suggestions,  etc.
       should be addressed to:


AUTHOR
		      Dr. John P. Priestle
		      K-681.3.43
		      Ciba-Geigy, Ltd.
		      CH-4002 BASEL
		      Switzerland

		      E-mail address: PRIESTLE@FMI.CH



REFERENCES
       Jane S. Richardson (1985) Methods Enzymol. 115 359-380.

       John P. Priestle	(1988) J. Appl.	Cryst. 21 572-576.


SEE ALSO
       ribrot, postplot, pltout, splitd