SFCHECK (CCP4: Supported Program)

NAME

   sfcheck - A program for assessing the agreement between the atomic
   model and X-ray data.

SYNOPSIS

   sfcheck [HKLIN in.mtz] [XYZIN in.pdb] [HKLOUT out.mtz] [MAPOUT
   map.ccp4]
   [PATH_OUT path_out] [PATH_SCR path_scr]
   [Keyworded input]

DESCRIPTION

Version 6.0.3 (26.02.2002) - Features

   A program for assessing the agreement between the atomic model and
   X-ray data. The program requires one or two input files, with the
   coordinates of the model (in PDB format) and structure factors ( MTZ
   or CIF format), and runs completely automatically, gives information
   about R-factor, correlation, Luzzati plot, Wilson plot,
   Boverall,pseudo-translation, twinning test ..., local error estimation
   by residues. Sfcheck can compute omit phases and use these instead of
   phases of model. For output Sfcheck generates a PostScript file.
   Sfcheck can also create a new MTZ output file with omit phases or with
   detwinned data.
     _________________________________________________________________

CONTENTS

     * Reference
     * Output information produced by SFCHECK
     * Local error esimationt
     * Omit procedure
     * Partional information
     * Twinning test
     * Input output files
     *
     * Keywords
     * Command file examples
     _________________________________________________________________

Reference

   Authors:      A.A.Vagin, J.Richelle, S.J.Wodak.
                email: alexei@ysbl.york.ac.uk
    A.A.Vaguine, J.Richelle, S.J.Wodak. SFCHECK: a unified set of
    procedure for evaluating the quality of macromolecular stracture-factor
    data and their agreement with atomic model.
    Acta Cryst.(1999). D55, 191-205

Output information produced by SFCHECK

    1. Data deposited in PDB file:

      1.1 Crystal:
          cell parameters and space group

      1.2 Model:
          number of atoms
          number of water molecules
          solvent content
          <B> for model
          Matthews coefficient and corresponding solvent %
          reported resolution
          reported R-factor

      1.3 Refinement:
          refinement program
          resolution range for refinement
          reported sigma cut-off for refinement
          reported R-factor
          reported Rfree

    2. Data computed by Sfcheck:

      2.1 Structure factors:
          number of reflections
          number of reflections with I > sigma
          number of reflections with I > 3sigma
          resolution range
          completeness
          R-standard computed by Sfcheck (sum(sigma)/sum(F))
          Wilson plot (amplitudes vs. resolution)
          overall B-factor by Patterson origin peak and by Wilson plot
          optical resolution
          expected minimal error in coordinates
          Anisotropic distribution of Structure Factors -ratio of Eigen values

      2.2 Model vs. structure factors:
          R-factor
          Correlation coefficient
          R-factor for reported resolution range and sigma cut-off
          Rfree
          Luzzati plot (R-factor vs. resolution)
          coordinate error from Luzzati plot
          expected maximal error in coordinates
          diffraction-data precision indicator (DPI)
          Patterson scaling    - scale , Badd
          Anisothermal scaling - betas: b11,b22,b33,b12,b13,b23
          Solvent correction - Ks,Bs

    Optical resolution

      Optical resolution is defined as the expected minimum distance
      between two resolved peaks in the electron density map. It is
      computed as (del_patt*2)/sqrt(2), where del_patt is the width of
      the Patterson origin peak.
      The "expected optical resolution for the complete data set" is
      calculated as above but using all reflections, with values for
      missing reflections assumed to be the average value in
      the corresponding resolution shell.
      Plot of Optical resolution for an atom with B=0 demonstrates
      behavior of the part of Optical resolution corresponded on the
      series termination.

    Patterson scaling

      Scaling in SFCHECK is based on the Patterson origin peak which is
      approximated as a gaussian. Compared to the conventional scaling
      by the Wilson plot, this method is particularly advantageous when
      only low resolution data are available.
      The program gives overall B-factors estimated by both methods.

    Low resolution cut-off

      Disordered solvent contributes to diffraction at low resolution.
      However, removal of low resolution data from calculations results
      in a series termination effect which is noticeable in the electron
      density at the surface of the molecule. To reduce the influence of
      low resolution terms, SFCHECK applies a "soft" low resolution
      cut-off to structure factors according to the formula:

        Fnew = Fold (1-exp(-Boff*s2)) , where Boff = 4dmax2

      Sfcheck uses Boff = 256. This corresponds to the low resolution
      cut-off at 8 A.

    Scaling

      Sfcheck scales Fobs and Fcalc by the Patterson origin peak using all
      data applying Boff.
      First, it computes Boveralls for observed and calculed amplitudes.
      Second, it makes the width of the calculated peak equal to the
      observed, i.e. computes an additional thermal factor Badd:

            Badd = Boverall_obs - Boverall_calc

      Third, Sfcheck computes the scale factor for Fcalc:

                                  sum(Fobs2*(1-exp(-Boff*s2)))
            scale = sqrt ( --------------------------------------------- )
                           sum(Fcalc^2*exp(-Badd*s2)*(1-exp(-Boff*s2)))

      Finally we have:

            Fcalc_scaled = Fcalc * scale * exp(-Badd*s2)

      Sfcheck computes the R-factor and Correlation coefficient for all
      data applying the soft low resolution cut-off as described above.
      Sfcheck computes the R-factor and Correlation coefficient for
      the reported resolution range and reported sigma cut-off without
      applying Boff. If the Fobs file contains reflections marked with
      the Rfree flag, the program computes Rfree.

    Completeness

      Missing data are restored by using the average values of
      intensities for the corresponding resolution shell.
      The program produces a plot of completeness vs. resolution and
      a plot of the average radial completeness in polar coordinates
      theta and phi.

    Expected minimal error

      The minimal coordinate error is estimated using the experimental
      sigmas(F). The standard deviation of an atomic coordinate is
      given by:

         sig_min(r) = sqrt(3)*sigma(slope)/curvature

              where  sigma(slope) is the slope of then electron density in the
                                  x direction (along A).
                     curvature is an average curvature of the electron
                                  density at the atomic peak centre.

      and computed as:

       sigma(slope) = (2pi*sqrt(sum(h2*(sigF)2)))/(VOL*A)

                     VOL - volume of cell
                     A   - cell parameter
                     h   - Miller index
                     summation over all reflections

                    ( Cruickshank,D.W.J. (1949) Acta.Cryst 2, 65.)

       curvature  = (2pi2*sum(h2*F))/(VOL*A^2)

                    ( Murshudov et al., (1997) Acta.Cryst D532, 240.)

      If there is no experimental sigma Sfcheck
      uses  sigma = Fobs * 0.04 for all reflections.

    Expected maximal error

      The expected maximal error in coordinates is estimated
      by the difference between !Fobs! and !Fcalc!:

       sig_max(r) = sqrt(3)*sigma(slope)/curvature

       sigma(slope) = (2pi*sqrt(sum(h2*(Fobs-Fcalc)2)))/(VOL*A)

       curvature  = (2pi2*sum(h2*F))/(VOL*A^2)

      For missing reflections the program uses the average value of
      sigma(Fobs) for the corresponding resolution shell instead
      of (Fobs-Fcalc).

    DPI - diffraction-data precision indicator

      The Cruickshank method of estimation of coordinate error.
                   (Acta Cryst.(1999), D55, pp 583-601)

        sig(x) = sqr(Natoms/(Nobs-4Natoms)) C-1/3 dmin Rfact

                where  C     - fractional completeness.
                       Rfact - convential crystallographic R-factor
                       Nobs  - number of reflections
                       Dmin  - maximal resolution

       If Rfree flags are specified, the program uses the Murshudov approach
       to calculate DPI:
                   (Newsletter on protein crystallography., Daresbury
                    Laboratory, (1997) 33, pp 25-30.)

        sig(x) = sqr(Natoms/Nobs) C-1/3 dmin Rfree

    Luzzati plot (R-factor vs. resolution)

       Program computes the average radial error <delta> in coordinates
       by Luzzati plot.
                          <delta(r)> = 1.6 sig(x)

    Solvent content

       The solvent content is the fraction of the unit cell volume not occupied
       by the model. The model consists of ALL atoms present in the coordinate
       file including ordered solvent.


    Residual factor Rmerge

                            sum_i (sum_j |Ij - <I>|)
                Rmerge(I) = --------------------------
                                 sum_i (sum_j (<I>))

                Ij  = the intensity of the jth observation of reflection i
                <I> = the mean of the intensities of all observations of
                       reflection i

                sum_i is taken over all reflections
                sum_j is taken over all observations of each reflection

Local error estimation

    Local error estimation (plotted for each residue, for the backbone
    and for the side chain):
       1. Amplitude of displacement of atoms from electron density
       2. Density correlation coefficient
       3. Density index
       4. B-factor
       5. Index of connectivity

    Displacement

      Displacement of atoms from electron density is estimated from the
      difference (Fobs - Fcal) map. The displacement vector is the ratio of
      the gradient of difference density to the curvature. The amplitude of
      the displacement vector is an indicator of the positional error.

    Correlation coefficient

      The density correlation coefficient is calculated for each residue
      from the atomic densities of (2Fobs-Fcalc) map - "Robs" and the model
      map (Fcalc) - "Rcalc" :

      D_corr =  <Robs><Rcalc>/sqrt(<Robs2><Rcalc^2>)

          where <Robs> is the mean of "observed" densities of atoms
                of the residue (backbone or side chain).

                <Rcalc> is the mean of "calculated" densities of atoms
                of the residue.

          The value of density for an atom from the map R(x) is given by:

                   sum_i ( R(xi) * Ratom(xi - xa) )
          Dens =  ----------------------------------
                       sum_i ( Ratom(xi - xa) )

            where  Ratom(x): the atomic electron density for x-th point of grid
.
                   xa      : vector of the centre of atom.
                   xi      : vector of the i-th point of grid.

            Sum is taken over all grid points which have distance
            from the centre of atom less than Radius_limit.
            For all atoms Radius_limit = 2.5 A.

    Index of density and index of connectivity

      The index of connectivity is the product of the (2Fobs-Fcal) electron
      density values for the backbone atoms N, CA and C, i.e. the geometric
      mean value for these atoms. Low values of this index indicate breaks
      in the backbone electron density which may be due to flexibility of
      the chain or incorrect tracing.  The index of density is a similar
      indicator which is calculated for all atoms of a given residue.

Omit procedure


      An omit map procedure is a means of reducing the model bias in
      the electron density calculated with model phases. SFCHECK produces
      the so called total omit map by an automatic procedure. First, the
      initial (Fobs, PHImodel) map is divided into N boxes. For each
      box, the electron density in it is set to zero and new phases are
      calculated from this modified map. A new map is calculated using
      these phases and Fobs. This map contains the omit map for the
      given box which is stored until the procedure is repeated for
      all boxes. At the end, all the boxes with omit maps are used
      to assemble complete omit map. Phases calculated from this complete
      omit map are combined with the initial phases. The whole procedure may
      be repeated (keyword NOMIT). Note: it is time consuming!
      Sfcheck can optionly create an output file with omit phases
      (see HKLOUT)

Partional information


      Sfcheck can use only one input file of either coordinates or structure
      factors. In such cases Sfcheck can of course produce limited analysis of
      the coordinates or the data.

Twinning test


     Sfcheck checks for merohedral twinning.
     (only if the program uses one input MTZ file of structure factors)

     Perfect twinning test: <I2>/<I>2

     Sfcheck will compute a Partial Twinning test:

          H = !I(h1)-I(h2)!/(I(h1)+I(h2))

     for the following space groups:

                           P3 P31 P32 R3
                           P4 P41 P42 P43 I4 I41
                           P6 P61 P62 P63 P64 P65
                           P312 P321 R32
                           P23 F23 I23 P213 I213

     Alpha (twinning fraction) = 1/2 - <H>

     If  0.05 <Alpha< 0.45 Sfcheck can create an output MTZ file
     with detwinned data (see HKLOUT)

     For details see: Yeates,T.O. (1997) Methods in Enzymology 276, 344-358.

Input output files

   HKLIN
          Input MTZ file with the reflected data.
          See the LABIN keyword for details.
          Also CIFile of structure factors is acceptable.

   XYZIN
          Input PDB file with the coordinates.
          Must contain a CRYST1 card with the unit cell and the space
          group name. Sfcheck can use the information from HEADER, SCALE,
          MTRIX and REMARK cards.

  Output files

   Information is output to a PostScript file:

   sfcheck_<identifier>.ps

   Sfcheck can create:

   HKLOUT
          Only required if output MTZ file is needed. output new MTZ file
          with the reflected data(F,sigF) or with OMIT Phases
          (Fobs,Ph,FOM) or with detwinned Fobs (F,sigF).

   MAPOUT
          Only required if output file with map is needed. output CCP4
          file with the extract density (around model) map.

   PATH_SCR
          You can use this variable to redirect all scratch files to
          special directory.
          Default is value of TEMP1 or CCP4_SRC variables.
          If 'PATH_SCR .' all scratch files will be in current directory.

   PATH_OUT
          This variable will redirect output PostScript file to the
          defined directory.

Keywords

   The available keywords are:

     LABIN, NOMIT

  LABIN <program label>=<file label>...

   Specify input column labels. Only needed if a MTZ file is input.

   Sfcheck labels defined are: F, SIGF, F(-), SIGF(-), I, SIGI, I(-),
   SIGI(-), FREE

   F       label of F or F(+)
   SIGF    label of sigma F or sigma F(+)
   F(-)    label of F(-)
   SIGF(-) label of sigma F(-)
   FREE    label of flag of Rfree factor
   I       Structure Intensity of hkl
   SIGI    Standard deviation of the above
   I(-)    Structure Intensity of -h -k -l
   SIGI(-) Standard deviation of the above

  NOMIT <nmon>

   Only required if omit procedure is needed

   <nomit> is the number of cycles of omit procedure. Default is 0, i.e
   no omit procedure. The <nmon>=2 is recommended value.

Command file examples

  Example of usual command file :

  There are two input files: MTZ and PDB.
  Sfcheck will assess the agreement between the atomic
  model and X-ray data.

# --------------------------------
sfcheck HKLIN test.mtz XYZIN 2sar.pdb << eor
# --------------------------------
LABIN F=F SIGF=SIGF FREE=FreeR_flag
eor

  Example for omit procedure :

  There are two input files: MTZ and PDB.
  For assessing Sfcheck will use the phases after the omit procedure.
  New MTZ file with OMIT Phases will be created. As variable PATH_OUT
  is used  the output PostScript file will be placed in directory:
  /y/people/alexei/

# --------------------------------
sfcheck HKLIN test.mtz XYZIN 2sar.pdb \
HKLOUT new.mtz PATH_OUT /y/people/alexei/ \
 << eor
# --------------------------------
LABIN F=F SIGF=SIGF FREE=FreeR_flag
NOMIT 2
eor
     _________________________________________________________________