SURFACE (CCP4: Supported Program)
                                       
NAME

   surface - surface accessibility program and for preparing input file
   to program volume.
   
SYNOPSIS

   surface xyzin1 foo_in1.pdb [xyzin2 foo_in2.pdb] xyzout foo_out3.rad
   [Keyworded input]
   
DESCRIPTION

   For each atom in a list, the accessibility program is designed to find
   the surface area in square Angstroms that is accessible to a probe
   sphere of a radius specified by the user. The program requires atom
   identification data and crystallographic coordinates from an input
   file. This will normally be in Brookhaven PDB format, but the program
   will also accept the output file from the Konnert-Hendrickson
   refinement program, or a file produced internally during operation of
   this program (see FORMAT). The program can be easily modified to
   accept other formats.
   
   Atom types are identified through residue and atom names. Van der
   Waals radii are assigned to each atom on the basis of atom type. The
   values are listed in the subroutines RADASNCHC and RADASNRICH (see
   VDWR). The data statements in that program can easily be changed by
   the user if a different set of standard values is wanted. Any atoms
   that cannot be identified by this subroutine are assigned a default
   radius of 1.80 Angstroms. The radius of the spherical probe may be
   assigned any value in the range 0.0 to 9.9 (see PROBE). Adjustments to
   the source program must be made to accomodate values outside of this
   range. A water molecule is commonly assumed to have a radius of 1.40
   Angstroms. A flag system can be used to include or exclude atoms from
   the accessibility calculation.
   
   The output of the program is a file containing all of the input data
   for each atom, the assigned Van der Waals radii, certain internal
   flags indicating the atoms included in the calculation, the accessible
   area, the contact area, and the fractional area (not yet implemented).
   The accessible area is the area in square Angstroms units of the locus
   of the center of the probe. The contact area is the area in square
   angstroms on the Van der Waals surface of an atom that can be
   contacted by a sphere of the given probe radius. The algorithm of Lee
   and Richards (1971) is used to calculate the accessible area.
   
   [NOTE: The initial part of this program may be used to prepare an
   output file to be used as input into the VOLUME program.]
   
INPUT AND OUTPUT FILES

  Input files
  
   XYZIN1, XYZIN2
          Input files of atom and coordinate data. These would normally
          be in PDB format ('PDB'), although 'WAH', 'RAD' and 'CHA' are
          also possible (see FORMAT). Normally only XYZIN1 is used; use
          the NFILES keyword to specify two input files.
          
     * PDB FORMATTED FILES - Header information is typed on the screen
       record by record until a line begining with the word "ATOM  " or
       "HETATM" is found. When the program assigns Van der Waals radii to
       the atoms an intermediate file is first created, containing only
       those lines that have the "ATOM  " or "HETATM" keyword in the
       first six columns. The program then reads the intermediate file
       line by line assigning Van der Waals radii according to atom name
       and residue type.
     * WAH FORMATTED FILES - The format is the same as the standard
       output file from KONNERT - HENDRICKSON refinement. It is assummed
       that no header information or remarks are included in these files.
     * RAD FORMATTED FILES - These files are the standard output files of
       this program. It is generally recommended that when you work on a
       given molecular structure that the accessibility calculation first
       be performed on the entire structure. This way you will have an
       output file that can be used as a reference file when different
       subsets are calculated. You can also use this standard output file
       as the input file for future accessibility calculations on any
       SUBSET specified by the flags. Since the Van der Waals radii have
       already been assigned and are included in the file time can be
       save by skipping over the radius assignment section. Also no
       intermediate file is needed as in the case of PDB files. The time
       expended creating and reading from this file is then eliminated.
       It is also useful as a reference when subsets are calculated. You
       can then compare subset accessibility to the reference (entire
       molecule) accessibility. A further advantage is that if you want
       to assign special values to atoms or define a subset that can not
       be created easily within the program you can edit this reference
       file. An example might be that you want to change the Van der
       Waals radii of a few individual atoms of a given atom name and
       residue type while leaving all the rest at the value assigned in
       the program. This would have to be done by editing or creating a
       file of the "RAD" format with all the particular values you
       desire. When this file in "RAD" FORMAT is read the Van der Waals
       radius indicated for each atom is accepted without regard to atom
       name or residue type. This is particularly useful when only a few
       atoms have been assigned default radii because the radius
       asignment program wasn't prepared for the particular residue type
       or atom name.
       
  Output file
  
   XYZOUT
          This is a formatted ASCII file
          (1X,I2,1X,I5,1X,I2,1X,I2,1X,2A4,1X,I3,3F8.3,2F5.2,2F6.1,1X,F4.2
          ) with the following columns:
          
     KEY(I)     = flag for accessibility calculation.
     I          = integer counter
     NUMCHN(I)  = chain number if more than one peptide.
     NUMFIL(I)  = file number if more than one protein is listed.
     ATM(I)     = atom designation. Up to 4 characters (uses PDB convention).
     RES3(I)    = residue designation (three letter code).
     SEQNUM(I)  = sequence number of residue.
     X(I)       = X coordinate of atom.
     Y(I)       = Y coordinate of atom.
     Z(I)       = Z coordinate of atom.
     RVDW(I)    = Van der Waals radius of atom.
     RCOV(I)    = covalent radius of atom.
     AAREA      = accessible area of atom.
     CAREA      = contact area of atom.
     FRCACC     = fractional accessibility of atom (not yet implemented).

          This is a 'RAD' format file that can be used as input to this
          program. It can also be used as input to the VOLUME program.
          
KEYWORDED INPUT

   Available keywords are:
   
     ALLATM, ATOM, CALCULATE, CHAIN, DONE, FILE, FORMAT, INCLUDE, NEXT,
     NFILES, OMIT, PRESET, PROBE, RERUN, RESET, RESIDUE, RUN, SERIAL,
     SKIP, STOP, SUBSET, VDWR, ZONE, ZSTEP.
     
   The order of the keywords is important. It is advisable to read the
   whole of this document first.
   
   Except within the first set, keywords must be entered in the order
   described in this section. The first set of keywords is:
   
  NFILES <nfiles>
  
   Number of input files (default=1, maximum=2).
   
  FORMAT <file> <format>
  
   Specify format of input file number <file>. Possible values of
   <format> are PDB, WAH, CHA or RAD. The default is for all input files
   to have the Brookhaven PDB format, <format> = PDB.
   
  PROBE <probe>
  
   <probe> between 0.0 and 9.9 (default 1.40). The PROBE RADIUS is the
   radius of the sphere for which the Van der Waals surface of each atom
   flagged 0 will be tested. It is ordinarily assumed that you will be
   testing for accessibility to water. We use a standard radius of 1.40
   Angstroms for water so this is the default value. If you want to
   change the probe radius because you are testing accessibility to
   something other than water or have a different value for water this is
   where to make the change.
   
  ZSTEP <zstep>
  
   <zstep> between 0.1 and 1.0 (default 0.25). The ZSTEP value will
   determine the accuracy of the accessibility calculation. The program
   finds a given atom for which the accessibility is to be calcuated.
   Then it finds all the neighboring atoms (rejecting or including
   according to FLAG value), and sequentially slices through the
   effective spheres of the set of atoms along the z axis. The circle of
   intersection of the atom for which the accessibility is being
   calculated is analyzed to see what arc length of this circle is
   overlapped by the intersecting circles of neighboring atoms. The arc
   distance that remains is then considered to be accessible to the
   PROBE. The total accessibility is calculated by simply summing the arc
   distances for all the slices through the particular atom of interest
   and multiplying by the distance between the slices. This distance is
   designated by the variable ZSTEP. The smaller the ZSTEP the more
   slices and the greater the accuracy (also the more computer time).
   Since the smallest Van der Waals radii are of the order of 1.10
   Angstroms and the probe will usually be 1.40 Angstroms the diameter of
   the smallest effective sphere = 2.0 x (1.40 + 1.10) = 5.0 Angstroms.
   With a ZSTEP of 0.25 this would give 20 slices through the sphere.
   This is acceptable for most of the conditions for which this program
   will be utilized. We recommend that the ZSTEP value be no less than
   0.10 and no greater than 0.50 for the reasons of program time and
   diminished accuracy respectively.
   
  VDWR CHC | RICH
  
   Sets USECHC or USERIC (default USECHC = .TRUE. and USERIC = .FALSE.).
   Assign van der Waals radii to atoms based on atom name and residue
   name. iflag(i,4) is set to negative if atom is not found or residue is
   not found. If the residue type is not found and the atom is a main
   chain atom: "C   ", "N   ", "O   ", "CA  ", the radius will be
   assigned to either the original code values (RICH) or the Cyrus values
   (CHC) (see reference [2]).
   
  SKIP
  
   Toggles DOCALC off (default DOCALC = .TRUE.). The output file will
   have the same format either way but one contains area data and the
   other only dummy entries in those columns. If areas are not needed,
   then that calculation can be avoided. Unlike the area output file,
   which lists information for only those atoms for which the area was
   calculated, the output file when DOCALC = .FALSE. is entered contains
   all the atoms read from the input file(s). The flags indicating OMIT,
   INCLUDE or CALCULATE remain intact if you want to specify subsets of
   atoms for the VOLUME calculation.
   
   This first set of keywords should be terminated with one of the
   following three keywords:
   
  RUN
  
   Do a calculation. The program reads the input file(s), stores all the
   data into arrays and assigns the Van der Waals radii. The number of
   atoms that have been read into the arrays will be printed. If any
   atoms have not been found in the radius assignment subroutine, the
   data associated with that atom will be displayed with an annotation as
   to whether the RESIDUE NAME or ATOM NAME was not found. If you are
   concerned because atoms have been assigned default radii you should
   determine why the atom names or the residue names were not found and
   try to correct the problem. This may mean editing the subroutine
   responsible for assigning radii to include a new RESIDUE TYPE or ATOM
   NAME. It may also mean that the format of your input file was not
   aligned with the expected format.
   
  RERUN
  
   It is assumed that the input files have been read on a previous run,
   and van der Waals radii assigned. A new calculation on this data is
   started.
   
  STOP
  
   Stop and finish.
   
   If everything is satisfactory, then the program moves to a second set
   of keywords.
   To allow flexibility and to reduce and eliminate unneccessary
   repetition of calculations a flag system is utilized. Every atom is
   assigned an integer FLAG value of -1, 0, or 1 with the following
   meanings:
   
   -1
          the atom is completely ignored during the accessibility
          calculation. This would be the same as omitting the particular
          atom from the input coordinate file.
          
   0
          the area is to be calculated for this atom. The surrounding
          consists of all other atoms flagged either "0" or "+1".
          
   1
          the atom is considered part of the protein environment but no
          area calculations will be performed on this atom.
          
   The program will loop through the atoms until an atom has a flag value
   0. The program then finds all those atoms with a value of 0 or 1 that
   fall within the 'touching' distance of the atom for which the
   calculation is being performed. This distance will vary with the Van
   der Waals radii and probe radius chosen.
   
   There are three keywords for assigning flags:
   
  ALLATM
  
   Calculate the accessible surface of all atoms read into the data
   arrays.
   
  PRESET
  
   Only available if the input file(s) were of 'RAD' format. This will
   take the flag values from the first column of this file and create the
   indicated subsets based on the standard flag values.
   
  SUBSET
  
   Define a subset of atoms. If you have an interest in a particular
   group of atoms, they can be specified rather than producing lengthy
   output files and taking up unnecessary program run time. FLAGS can be
   used for finding changes in the accessibility of the protein upon the
   removal of substrate(s) or upon deletion of a section of the protein.
   They may also be used if you only have an interest in the
   accessibility of certain RESIDUE types or ATOM types and do not wish
   to waste time doing the calculation for all atoms in the coordinate
   list. This option is designed to handle a few of the most logical flag
   assignments. If you have something that cannot be handled by the
   SUBSET flag setting subroutine, you can create your own file and set
   the flags as you wish. The file should then be in the 'RAD' format and
   you should use the PRESET keyword.
   
   If you choose the SUBSET option, then the following keywords can be
   used.
   First define the flag value to be assigned with one of:
   
   OMIT Assign flag of -1
   
   INCL Assign flag of 1
   
   CALC Assign flag of 0
   
   DONE No more flag assignments, proceed to next step in program.
   
   If one of the first three options is entered you can choose one of six
   different ways to specify what atoms are to be assigned that
   particular flag:
   
   FILE Assign flag if atom came from one of two input files. This is not
   available if only one input file was read.
   
   CHAI(N) Assign flag to an atom if it has the chain number specified.
   Many times a molecule will consist of two separate chains that are
   identified in the coordinate list. Two monomers in an asymmetric unit
   or two subunits in a dimer are usually identified separately.
   
   ZONE Assign flag based on a range of the sequence number. Any atom
   that has a sequence number greater than or equal to the starting value
   entered or less than or equal to the ending value specified will be
   assigned the designated flag. Repeat this operation for as many
   sequence pairs as required. Entering the same number twice will result
   in the flag assignment to the single residue specified.
   
   RESI(DUE) Assign flag to an atom if the residue name is the same as
   the one specified. For instance in a protein you may only be
   interested in calculating the accessibility of histidine residues. If
   you enter the standard three letter notation "HIS" all histidines will
   be assigned the flag value.
   
   ATOM Assign flag to an atom if the atom name is the same as the one
   specified. This is the same as the "RESI" option, except that atom
   types are identified.
   
   SERI(AL) Assign flag based on a range of serial numbers of atoms in
   the coordinate list. An atom of serial number equal to or greater than
   the starting value entered or less than or equal to the ending value
   entered will be assigned the designated flag. Repeat through as many
   serial number pairs as required. Entering the same number twice will
   result in the flag assignment to the single atom specified.
   
   If you have more than one input file you will be asked for the file
   number for which flags are to be set.
   
   The ORDER OF OPERATION in setting FLAGS is very important. Any
   operation that is performed will overwrite the previouse flag value
   assigned to an atom. For example if a zone from 1 to 20 is assigned a
   FLAG of -1 by using the "OMIT" flag and the "ZONE" operation, and then
   the "CALC" flag is set to a ZONE from 5 to 10. The end result would be
   that the ZONE from 1 to 4 is OMITTED, the ZONE from 5 to 10 is
   CALCULATED and the ZONE from 11 to 20 is OMITTED. If "CALC" was first
   called for the ZONE from 5 to 10 and the "OMIT" was called for ZONE 1
   to 10 all the atoms associated with residues 1 to 10 would be OMITTED.
   
   Having set the flags, one of the following two keywords should be
   entered:
   
  RESET
  
   Reset the flags with one of the above three keywords (for interactive
   use).
   
  NEXT
  
   Do calculation, and then return to the first set of keywords. >From
   there, you can RERUN the calculation, or STOP.
   
EXAMPLES

  Unix examples script found in $CEXAM/unix/runnable/
  
     * surface.exam - example of accessible surface area calculation.
     * surface_rnase.exam - example with two accessible area calculations
       in a single run.
     * surface-volume-calc - example of preparing input to program
       VOLUME.
       
SEE ALSO

   volume, areaimol
   
REFERENCES

    1. B.Lee and F.M.Richards, J.Mol.Biol., 55, 379 - 400 (1971)
    2. Chothia (1975), "Structural Invariants in Protein Folding", Nature
       254: 304-308
       
AUTHORS

   Author: Mark D. Handschumacher and F.M. Richards.
   Original and earlier versions produced by: B. Lee, F.M. Richards, T.J.
   Richmond and J.B. Matthew.
   This CCP4 version (partially keyworded) is from Kim Henrick.