TRUNCATE (CCP4: Supported Program)
                                       
NAME

   truncate - obtain structure factor amplitudes using Truncate procedure
   and/or generate useful intensity statistics
   
SYNOPSIS

   truncate hklin foo_in.mtz hklout foo_out.mtz [ plot foo.plt ]
   [Keyworded input]
   
DESCRIPTION

   The standard use of the program is to read a file of averaged
   intensities (output from SCALA, SCALEPACK2MTZ or DTREK2MTZ) and write
   a file containing mean amplitudes and the original intensities. If
   anomalous data is present then F(+), F(-), with the anomalous
   difference, plus I(+) and I(-) are also written out. The amplitudes
   are put on an approximate absolute scale using the scale factor taken
   from a Wilson plot.
   
   There are two ways in TRUNCATE to calculate the amplitudes from the
   intensities. The simplest is just to take the square root of the
   intensities, setting any negative ones to zero (keyword TRUNCATE NO).
   Alternatively, the "truncate" procedure (keyword TRUNCATE YES, the
   default) calculates a best estimate of F from I, sd(I), and the
   distribution of intensities in resolution shells (see below). This has
   the effect of forcing all negative observations to be positive, and
   inflating the weakest reflections (less than about 3 sd), because an
   observation significantly smaller than the average intensity is likely
   to be underestimated. See reference below.
   
   This program can be used even if the "truncate" procedure is not
   desired, since it produces some useful statistics on intensity
   distributions. These can indicate problems with the data; for instance
   if the data is extremely anisotropic (see the FALLOFF keyword) or if
   it is likely to be twinned. See Cumulative distribution plot, which
   for a perfect twinning becomes sigmoidal, and the moments of I (or E
   or z) which are different for twinned data than for untwinned.
   
   If the input specified on the LABIN line includes an assignment for F,
   then no output will be generated. It is most undesirable to TRUNCATE a
   set of data where the intensities have already been modified to
   generate amplitudes.
   
   The general formula for expected moments <I^k> /<I>^k for untwinned
   acentric data is:
Table of moments:

  k-th moment is Gamma(k+1)  = k!  if k is an integer
  k-th moment                = sqrt(PI) k!  if k equals integer+0.5
  ie the (2k+1)th moment of E = sqrt(PI) 2k * 2k-2 * ... *2

  In general Gamma(k+1) = k Gamma(k)

               Acentric                        Centric
         Untwinned data Perfect twin.   Untwinned data Perfect twin.
  <E>         0.866         0.94             0.798       ?
  <E^3>       1.339         1.175            1.596       ?
  <I^2>       2.0           1.5              3.0         ?
  <I^3>       6.0           3.0             15.0         ?
  <I^4>      24.0           7.5            105.0         ?

   The scale factor estimated from the Wilson plot is applied to the data
   and allows the data to be put on a (very approximate) absolute scale.
   This at least gives amplitudes of a sensible magnitude for further
   calculations. The calculation relies on the number of residues/atoms
   given by the keywords NRESIDUE/CONTENTS being roughly correct. The
   program does not, however, apply any temperature factor.
   
KEYWORDED INPUT

   The various data control lines are identified by keywords Only the
   first 4 letters of each keyword are necessary. Most keywords are
   optional.
   
     ANOMALOUS, CELL, CONTENTS, FALLOFF, HEADER, HISTORY, LABIN, LABOUT,
     NRESIDUE, PLOT, RANGES, RESOLUTION, RSCALE, SCALE, SYMMETRY, TITLE,
     TRUNCATE, VPAT
     
   In addition, the following optional keywords control the data
   harvesting functionality:
   
     DNAME, NOHARVEST, PNAME, PRIVATE, RSIZE, USECWD
     
DESCRIPTION OF KEYWORDS

  TITLE <title>
  
   (default TITLE='From Truncate') [OPTIONAL INPUT]
   
   Title to write to output reflection file
   
  RANGES <nrange> | <range>
  
   (Default <nrange>=60) [OPTIONAL INPUT]
   
   <nrange> is the number of resolution bins over the resolution range
   for the Wilson Plot. <range> is the width of the bins on 4sin**2
   theta/lambda**2 and is an alterative to <nrange>. The resolution range
   used for the Wilson Plot is taken from the input data file, or set
   with the RESOLUTION keyword. A subset of these bins, covering a
   resolution range defined with the RSCALE keyword, is used to estimate
   the scale and B-factor.
   The use of this card is discouraged, as the choice of the number of
   bins is important. Too few bins and the scale and overall B will be
   less accurate. Too few reflections per bin could mean a large
   scattering of points from the straight line. This would mean a large
   uncertainity in the values for scale and B.
   If this card is omitted, the program divides the resolution range into
   60 bins, then checks that there are not less than 40 reflections in
   any one bin and if necessary reduces the number of bins until the
   above condition is satisfied. In all cases, the program will stop if
   the width of ranges is greater than 0.03 or the number of bins is
   greater than 60.
   
  RESOLUTION <Dmin> <Dmax>
  
   [OPTIONAL INPUT]
   
   Resolution limits - either 4(sin theta/lambda)**2 or d in Angstroms
   (either order). Reflections outside these limits will be excluded from
   all analysis and omitted on output. Defaults are taken from the range
   of data in the input file (i.e. all data included).
   
  RSCALE <Dmin> <Dmax>
  
   [OPTIONAL INPUT]
   
   Resolution limits for scaling (either 4(sin theta/lambda)**2 or d).
   This option allows you to exclude low resolution reflections from the
   calculation of the scale and B factor. However, all points in the
   range defined by RESO are plotted on the Wilson plot. It is probably a
   good idea to include only high resolution data (beyond 3A, if you have
   any data there) in the Wilson plot. This is because the assumptions
   behind Wilson statistics are invalid for low resolution data. The
   default high resolution limit is the same as RESOLUTION. The low
   resolution limit is, by default, set to 4.0A if the high res. limit is
   greater than 3.5A.
   
  SCALE <scale>
  
   [OPTIONAL INPUT]
   
   The default is to apply a scale factor from the Wilson plot. If a
   scale factor is given here, then that is applied instead. This option
   is useful if relative scaling is already done in SCALA.
   
   If amplitudes rather than intensities are specified on the LABIN line,
   then the Wilson scale is not applied, and a default scale of 100 is
   used.
   
  FALLOFF YES | NO [ CONE <cone> ] [ PLTX | PLTY ]
  
   [OPTIONAL INPUT]
   
   The first argument of the FALLOFF keyword should be "YES" or "NO",
   followed optionally by subkeywords controlling the detailed behaviour.
   The default is "YES", which triggers an analysis of the anisotropy of
   the data according to the "falloff" procedure contributed by Yorgo
   Modis. This calculates the falloff of mean F and mean F/sigma values
   as a function of (sinth/lab)**2 in 3 orthogonal directions. An overall
   falloff of all reflections is also calculated. The 3 mutually
   perpendicular directions are:


        DIRECTION 2 = B*-AXIS
        DIRECTION 3 = PERPENDICULAR TO A* AND B*
        DIRECTION 1 = PERPENDICULAR TO B* AND DIRECTION 3.

   If either of the subkeywords PLTX or PLTY are specified, then an
   output plot file (PLOT) is produced, in which Direction 1 is plotted
   as a thick line, Direction 2 is plotted as a hollow line with boxes at
   regular intervals of resolution, and Direction 3 is plotted as a thin
   line. The resolution range and number of resolution bins used in the
   calculation can be set by the keywords RESOLUTION and RANGES
   respectively.
   
   Subkeywords:
   
   CONE <cone>
          The falloff of mean F-values along each orthogonal direction is
          calculated using reflections falling within a cone orientated
          along that direction. <cone> is the angle the surface of the
          cone makes with the associated direction. Reflections which are
          located at a greater angle than <cone> from the closest
          direction will not be included in the falloff calculations.
          Default: 30.0 degrees.
          
   PLTX | PLTY
          Produce an output plot file (PLOT) and orientate it
          horizontally or vertically.
          Default is horizontally (PLTX).
          
  LABIN <program label>=<file label>...
  
   Specify input column lables. [OPTIONAL INPUT]
   
   Truncate takes output from SCALA, SCALEPACK2MTZ or DTREK2MTZ which
   generate standard labels. This is the most common usage of the
   program, in which case LABIN records are not required. If F is
   assigned,there will be no reflections output. You must assing either
   IMEAN/SIGIMEAN or F/SIGF.
   
   The program labels defined are: IMEAN SIGIMEAN I(+) SIGI(+) I(-)
   SIGI(-) F SIGF F(+) SIGF(+) F(-) SIGF(-).
   
   IMEAN
          Original average Structure Intensity
          
   SIGIMEAN
          Standard deviation of the above
          
   I(+)
          Structure Intensity of hkl
          
   SIGI(+)
          Standard deviation of the above
          
   I(-)
          Structure Intensity of -h -k -l
          
   SIGI(-)
          Standard deviation of the above
          
   F
          Original average Structure Amplitude
          
   SIGF
          Standard deviation of the above
          
   F(+)
          Structure Amplitude of hkl
          
   SIGF(+)
          Standard deviation of the above
          
   F(-)
          Structure Amplitude of -h -k -l
          
   SIGF(-)
          Standard deviation of the above
          
  LABOUT <program label>=<file label>...
  
   Specify output column labels. [OPTIONAL INPUT]
   
   The labels allowed are F SIGF DANO SIGDANO F(+) SIGF(+) F(-) SIGF(-)
   IMEAN SIGIMEAN I(+) SIGI(+) I(-) SIGI(-) ISYM. The output labels will
   default to these unless they are changed by assigning a program label
   to a user label.
   
   F
          Structure Amplitude
          
   SIGF
          Standard deviation of the above
          
   DANO
          Anomalous difference
          
   SIGDANO
          Standard deviation of the above
          
   F(+)
          Structure Amplitude for hkl
          
   SIGF(+)
          Standard deviation of the above
          
   F(-)
          Structure Amplitude for -h -k -l
          
   SIGF(-)
          Standard deviation of the above
          
   IMEAN
          Original average Structure Intensity
          
   SIGIMEAN
          Standard deviation of the above
          
   I(+)
          Structure Intensity of hkl
          
   SIGI(+)
          Standard deviation of the above
          
   I(-)
          Structure Intensity of -h -k -l
          
   SIGI(-)
          Standard deviation of the above
          
   ISYM
          Symmetry number for F: normally=0 but 1 or 2 if the F column
          arises entirely from F+ or F- reflections respectively
          
   If there is no anomalous data present then only the appropriate
   columns (F, SIGF, IMEAN and SIGIMEAN) are output. Values may be given
   in any order and as either Proglabel=Userlabel or Userlabel=Proglabel.
   
  CONTENTS <symbol> <n> ...
  
   [ALTERNATIVE COMPULSORY INPUT]
   
   followed by number of atoms in asymmetric unit, including hydrogens
   
   A maximum of 20 atom (element) types is allowed, each followed by a
   number, e.g.
  CONTENTS  H 746 C  454  N 115    O 139   S 12  ! Must include hydrogens

   The average scattering power is calculated from a table of form
   factors. By default the file $CLIBD/atomsf.lib contains this table of
   form factors. You can change the table used by assigning 'ATOMSF' to
   your preferred file. [NOTE the program RWCONTENTS provides the
   information for this keyword; how many Carbons etc., from a PDB file.
   Also, it gives an estimate of the number of hydrogens there would be.]
   
  NRESIDUE <Nres>
  
   [ALTERNATIVE COMPULSORY INPUT]
   
   <Nres> is the number of residues expected in the asymmetric unit
   
   A very approximate atom composition is calculated:
    mean mass of an amino acid = 110
    add on one ordered water per amino acid = ca. 128

   This is then taken as 5 C + 1.35 N + 1.5 O + 8 H /residue as number of
   atoms in asymmetric unit.
   
  VPAT <vpat>
  
   [OPTIONAL INPUT]
   
   volume per atom - default = 10
   
  PLOT [ ON | OFF ]
  
   PLOT or PLOT ON produces extra ascii plots in the log output. The
   default is PLOT OFF.
   
   [OPTIONAL INPUT]
   
  HEADER [ NONE | BRIEF | HISTORY | ALL ] [ NOBATCH | BATCH | ORIENTATION ]
  
   [OPTIONAL INPUT]
   
   Controls printout from reading file and batch headers
    a. file header printing:
       
        NONE
                no header printed
                
        BRIEF
                brief header (default)
                
        HISTORY
                brief + history
                
        ALL
                full header printed
                
    b. batch header printing:
       
        NOBATCH
                no batch header printed
                
        BATCH
                batch titles printed (default)
                
        ORIENTATION
                batch orientation data also printed
                
  HISTORY string
  
   [OPTIONAL INPUT]
   
   History strings to be added to history records in output file
   
  ANOMALOUS YES | NO
  
   [OPTIONAL INPUT]
   
   Controls whether anomalous differences are output. Defaults YES if
   anomalous information is present on input file, otherwise NO
   
  TRUNCATE YES | NO
  
   [OPTIONAL INPUT]
   
   If YES (default) the data will be truncated according to the procedure
   of French and Wilson. If NO the data are not truncated but the
   structure amplitudes are calculated simply by taking the square root
   of the intensities. Negative intensities are set to zero.
   
  SYMMETRY <space_group> | <number>
  
   [OPTIONAL INPUT]
   
   Default is to use symmetry in input HKLIN file. (Normally OMIT this
   command.)
   
  CELL <a> <b> <c> [ <alpha> <beta> <gamma> ]
  
   [OPTIONAL INPUT]
   
   The cell dimensions in Angstroms and degrees. The angles default to 90
   degrees. If this key is omitted then the cell dimensions are taken
   from the input file (normally OMIT this command)
   
Data Harvesting keywords

   Provided a Project Name and a Dataset Name are specified (either
   explicitly or from the MTZ file) and provided the NOHARVEST keyword is
   not given, the program will automatically produce a data harvesting
   file. This file will be written to
   
   $HARVESTHOME/DepositFiles/<projectname>/<datasetname>.truncate
   
   The environment variable $HARVESTHOME defaults to the user's home
   directory, but could be changed, for example, to a group project
   directory.
   
  PNAME<project_name>
  
   Project Name. In most cases, this will be inherited from the MTZ file.
   A dataset, as listed in the MTZ header, is specified by a
   project-name/dataset-name pair. The project-name specifies a
   particular structure solution project, while the dataset-name
   specifies a particular dataset contributing to the structure solution.
   An entry in the PNAME keyword should therefore be accompanied by a
   corresponding entry in the DNAME keyword.
   
  DNAME <dataset_name>
  
   Dataset Name. In most cases, this will be inherited from the MTZ file.
   A dataset, as listed in the MTZ header, is specified by a
   project-name/dataset-name pair. The project-name specifies a
   particular structure solution project, while the dataset-name
   specifies a particular dataset contributing to the structure solution.
   An entry in the DNAME keyword should therefore be accompanied by a
   corresponding entry in the PNAME keyword.
   
  PRIVATE
  
   Set the directory permissions to '700', i.e. read/write/execute for
   the user only (default '755').
   
  USECWD
  
   Write the deposit file to the current directory, rather than a
   subdirectory of $HARVESTHOME. This can be used to send deposit files
   from speculative runs to the local directory rather than the official
   project directory, or can be used when the program is being run on a
   machine without access to the directory $HARVESTHOME.
   
  RSIZE <row_length>
  
   Maximum width of a row in the deposit file (default 80). <row_length>
   should be between 80 and 132 characters.
   
  NOHARVEST
  
   Do not write out a deposit file; default is to do so provided Project
   and Dataset names are available.
   
INPUT AND OUTPUT FILES

   The input files are:
    a. Control data file.
    b. HKLIN - Input reflection data file in MTZ format.
       
     This will contain one record per reflection with the following
     items:
     SCALA (with or without anomalous)
        H K L IMEAN SIGIMEAN I(+) SIGI(+) I(-) SIGI(-)

     SCALEPACK2MTZ or DTREK2MTZ (with anomalous)
        H K L IMEAN SIGIMEAN I(+) SIGI(+) I(-) SIGI(-)

  Any set of amplitudes in mtz format for which you wish to analyse statistics.
        H K L F SIGF F(+) SIGF(+) F(-) SIGF(-)

     where I+ and I- are used for the anomalous differences
       
   The output files are:
    c. HKLOUT - Output reflection data file. Not generated if F assigned
       as input column.
       
     The output file is a reflection data file in standard MTZ format
     (i.e. one record/reflection) containing 7 or 18 items per
     reflection as follows (see above for labels used)
   H K L  F SDF [DANOM SD(DANOM) F(+) SDF(+) F(-) SDF(-)]
          Imean SDImean [I(+) SDI(+) I(-) SDI(-) ISYM]

     The Fs are multiplied by the Wilson scale and the Is are multiplied
     by the square of the Wilson scale / 100.0.
    d. PLOT - plot file showing fall-off of mean F in 3 perpendicular
       directions.
       
     Produced if either of the subkeywords PLTX or PLTY of the FALLOFF
     keyword are specified. This can be viewed with XPLOT84DRIVER, or
     converted to postscript with PLTDEV.
       
PRINTER OUTPUT

   The printer output starts with details of the control data and details
   of the input MTZ reflection data file. Analyses of the data against
   resolution are then given and include intensity distributions for
   comparison with Wilson's theoretical distributions. The following
   graphs are output (which can be viewed via XLOGGRAPH or LOGGRAPH):
     * Wilson plot.
     * Moments of the intensity for acentric and centric data. These
       plots may indicate twinning, see above.
     * Cumulative intensity distribution for both acentric and centric
       data compared to theoretical predictions. If twinning is present,
       these curves become sigmasoidal (and will therefore be shifted to
       the right of the theoretical curves for some or all of the plot),
       although anisotropic diffraction can confuse this picture.
     * Plots of mean amplitude (F) and mean amplitude/standard deviation
       (F/sd) calculated for the data in resolution shells, and plotted
       against resolution.
     * Mean F, mean F/sd and number of reflections calculated for data
       lying in the region of 3 orthogonal directions d1, d2, d3 (see the
       FALLOFF keyword). Differences in the falloff rate in the 3
       directions indicates anisotropy of the data.
       
PROGRAM FUNCTION

   The program TRUNCATE reads a reflection data file of averaged
   intensities (SCALA, SCALEPACK2MTZ or DTREK2MTZ output) and outputs an
   MTZ reflection data file containing F and DeltaFanom values. The input
   intensities are assumed to follow a normal distribution with the
   standard deviations, i.e. negative observations must have been
   preserved. The truncation procedure used was devised by French and
   Wilson and is based on Bayesian statistics. The F's are calculated
   using the prior knowledge of Wilson's distributions for acentric or
   centric data (calculated in shells of reciprocal space in a first pass
   through the data) and the mean intensity and standard deviation
   values. The F's output are all positive and follow Wilson's
   distribution. The truncation procedure has little effect on
   reflections larger than 3 standard deviations but should give
   significantly better values for the weak data than those obtained by
   merely taking the square root of the intensities and setting negative
   intensities to zero. Reflections of less than minus four standard
   deviations are rejected.
   
   The following warnings should be heeded:
    a. Do not truncate data more than once, e.g. do not merge truncated
       data with untruncated data and then truncate again.
    b. The standard deviations are crucial to the procedure and the
       standard deviation analysis from SCALA should be checked.
    c. The procedure should not be used on data which has been forced to
       be positive e.g. from ordinate analysis measurements on a
       diffractometer or where negative observations have been set to
       zero.
       
    WILSON plot
    
   The Wilson plot part of the program attempts to calculate an absolute
   scale and temperature factor for a set of observed intensities, using
   the theory of A C Wilson. This says that IF the atoms are randomly
   distributed through the asymmetric unit THEN
   
   <f**2> should equal scale*<Fobs**2> * exp(-2B sin**2/lambda**2)
   
   By fitting a least squares line through ln(<f**2>/<Fobs**2>) v
   2sin**sq/lambda**2 the program derives the scale and B value.
   
   For real structures the assumption that the atoms are randomly
   distributed is obviously incorrect. The effect of this is most obvious
   in the low resolution reflections. The Wilson plot will deviate from a
   straight line from about 3.0A - 4.0A downwards. Although all the
   points on the Wilson plot are plotted, the scale and B are only
   determined from a limited resolution range determined by the user (see
   keyword RSCALE).
   
   There may be a problem in evaluating <Fobs**2> if all the weak data
   have been systematically omitted (this should NOT be the case for data
   measured in any proper manner: note that if this IS the case, the
   Truncate procedure will also fail). If this is the case then you need
   to use TRUNCATE NO. The program estimates the expected number of
   reflections in each resolution shell and then calculates <Fobs**2> by
   dividing by the number of predicted reflections.
   
SEE ALSO

   scala, scalepack2mtz, dtrek2mtz, rwcontents, Data Harvesting
   
REFERENCES

    1. French G.S. and Wilson K.S. Acta. Cryst. (1978), A34 , 517.
       
AUTHORS

   K.S. Wilson and S. French
   
   "falloff" program contributed by Yorgo MODIS, European Molecular
   Biology Lab (original program: W.G.J. HOL/SINEKE BREEN (part of the
   Groningen BIOMOL package). Incorporated into TRUNCATE by Martyn Winn.
   
EXAMPLES

  unix example scripts found in $CEXAM/unix/runnable/
  
     * truncate.exam
     * scala.exam
     * scalepack2mtz.exam
       
  VMS versions found in $CEXAM/vms/
  
     * truncate.com
     * scala.com
       
  ....and non runnable examples in $CEXAM/unix/non-runnable/
  
     * rotaprep.exam
     * texan-proc.exam