VOLUME (CCP4: Supported Program)
                                       
NAME

   volume - polyhedral volume around selected atoms
   
SYNOPSIS

   volume xyzin surface.out xyzoutvolume.out3 erroutvolume.error
   shellfilewater.shell
   [Key-worded input]
   
DESCRIPTION

   In its present version the VOLUME program determines the volume of a
   polyhedron surrounding the selected atom or atoms when the polyhedral
   faces are determined by one of three procedures based on the Voronoi
   construction. A general description of these procedures, the
   differences between them and which one is likely to be of use in a
   particular situation are described below.
   
   NB: On some systems (e.g. some Digital/Compaq machines) there may be a
   system program also called volume, and this name clash may lead to
   problems trying to run the CCP4 version of VOLUME (depending on the
   value of your PATH environment variable). If you encounter this
   problem then try using the full path e.g. $CBIN/volume to specify the
   correct version.
   
INPUT AND OUTPUT FILES

  Input file
  
   The program requires a formatted file as input - logical name XYZIN .
   It is written to accept the output file from the SURFACE program
   directly. This wll be the normal input because of the KEY selection
   procedure described below. The file will be processed as follows:
   
   All header material will be disregarded. The program searches each
   line for the starting characters 'BEGIN '. If found, the program then
   reads into the appropriate arrays the atom data starting on the
   following lines in the format:
   
   (1X,I2,7X,I2,1X,I2,1X,2A4,1X,I3,3F8.3,2F5.2,2F6.1,F5.2)
   
   The arrays filled are:
 KEY(I)     = atom processing flag. see below
 NUMCHN(I)  = chain number if more than one
       peptide in input file (not used
       in this program)
 NUMFIL(I)  = file number if more than one
       protein is listed in input file
       (not used in this program)
 ATM(I)     = atom designation. 1 to 4
       characters (use BNL system)
 RES3(I)    = residue designation (three letter
       code)
 SEQNUM(I)  = sequence number of residue
 X(I)       = X coordinate of atom
 Y(I)       = Y coordinate of atom
 Z(I)       = Z coordinate of atom
 RVDW(I)    = vanderWaals radius of atom
 RCOV(I)    = covalent radius of atom
 AAREA      = accessible area of atom in
       file from ACCESS.
 CAREA      = contact area of atom in
       file from ACCESS.
 FRCACC     = fractional accessibility of
       atom in file from ACCESS.
       (These dummy variables are
       not used in this program.
       Kept in list as reminder)

   Note that the maximum value for I is the number of atoms in the input
   list. (These may be protein atoms,'heteroatoms',and/or water molecules
   depending on the file used.) You must ensure that the array dimensions
   in the VOLUME program are large enough no only to accomodate this list
   but also to hold the output of SHELL (see below). The relevant arrays
   are dimensioned through the parameter MAXATM which appears in the file
   VOL.CMN. Check this value and edit as required.
   
  Output files
  
   The output of the program is provided in two files. The successful
   calculations are put into a file designated as local name XYZOUT. The
   format of this file is:
 SUMMARY INFORMATION
BEGIN
 (followed by data records in the following format)
       (2I5,2I3,2A6,I5,3F8.3,2F5.2,F8.3,I5)

 NCALC     = Number of atom in this output list
 I         = Serial number of atom in full coordinate
   list
 NUMCHN(I) = Chain number (see INPUT)
 NUMFIL(I) = File number  (see INPUT)
 ATM(I)    = Atom designation - 1 to 4 characters
 RES3(I)   = Residue designation - 3 letter code
 SEQNUM(I) = Residue sequence number
 X(I)      = X coordinate of atom
 Y(I)      = Y coordinate of atom
 Z(I)      = Z coordinate of atom
 RVDW(I)   = vanderWaal's radius of atom
 RCOV(I)   = Covalent radius of atom
 VOLUME    = Volume of atom as calculated by 
   specified method
 NS        = Number of solvent shell positions used
   in defining the limiting polyhedron

   The second file, local name ERROUT, contains any error messages that
   may have been generated during the operation of the program. If
   serious errors are encountered the calculation for that atom is
   aborted (VOLUME and NS are both set equal to 1000),error messages
   listed, and the calculations continued with the next atom in the list.
   Occasionally less serious errors are found, the messages are listed,
   but the calculation is continued. The decision on whether or not to
   keep the result is made by the investigator. Normally, the cause of
   the problem can be identified, corrected and the calculation rerun.
   
KEYWORDED INPUT

  EDGE <edge>
  
   Length of the edge of the shell (default=2.80).
   
  SRAD <srad>
  
   Search radius (default=6.50).
   
  METHOD VORO | RICH | RADI
  
   Method. VORO is Standard Voronoi Procedure (default), RICH is Richards
   Method B, and RADI is Radical Plane Procedure.
   
  OUTER <outer>
  
   For Surface Volume Adjustment (default=0.0).
   
  SHELL | NOSHELL
  
   (default = NOSHELL).
   
  CALC | NOCALC
  
   (default = CALC).
   
  VERB | NOVERB
  
   Don't activate this unless you want a very big .error file (default =
   NOVERBOSE).
   
  WATER | NOWATER
  
   Use this if you want to add the extra shell of water from the file
   SHELLFILE.
   
  RUN | END
  
   End input.
   
PROGRAM FUNCTION

   After reading the input file, the next step is to surround the protein
   with a hypothetical 'solvent' shell which serves to define the volume
   of the surface atoms on the protein. The positions assigned to these
   'molecules' are loaded onto the end of the protein atom file. They are
   used to define the limiting polyhedron, but, except in the case of
   cavity calculations, they are not used as centers for volume
   calculatons themselves. This layer is set up by the subroutine SHELL.
   
   The program then cycles through each atom in turn whose volume is to
   be calculated (as designated by the KEY array).
   
   a) The Subroutine FILBOX selects all atoms within a defined radius
   which might contribute to the limiting polyhedron surrounding the
   target atom. Potential defining planes of this polyhedron are
   perpendicular to the interatomic vectors between the target atom and
   the atoms in this list. The position of these planes along the vectors
   will depend on the procedure for calculation chosen at the time of
   program initiation. FILBOX sets up these planes and loads then into
   the array BOX in the order of increasing distance from the target
   atom.
   
   b) The Subroutine ATMPOL examines the list BOX and selects those
   planes which actually make up the limiting polyhedron. It computes the
   coordinates of all the vertices of the polyhedron and stores these
   coordinates, and the vertex identification numbers, in the arrays
   POLYHN AND IPOLYH. This is the heart of the program and its most
   complex component.
   
   c) The Subroutine POLVOL examines the arrays POLYHN and IPOLYH and
   computes the volume of this limiting polyhedron.
   
   d) The program then cycles through a), b) and c) until the atom list
   has been completed.
   
PROGRAM DETAILS

   A) INPUT ARRAY KEY(I): The KEY array is normally set up in the SURFACE
   program but it can be hand edited or supplied otherwise. KEY(I) = -1
   Atom I is omitted entirely from all calculations. KEY(I) = 0 Atom I is
   included as part of the protein and its volume is calculated. KEY(I) =
   1 Atom I is included as part of the protein and is thus used in
   defining the polyhedra, but its volume is not calculated.
   
   (The (-1) value can be used to asses the affect of a particular atom
   or atom group on the volume available to surrounding atoms without any
   other change in the program, for example.)Onbly the atoms of interest
   need have their volumes calculated. If the SURFACE program is used to
   generated the input file, these atoms can be selected on the basis of
   atom name, residue name, residue sequence number, or individually by
   serial number in th coordinate list.
   
   Principal Components:
   
   VOLUME Main calling program. Sets up GETNUM, input and output files,
   queries SHELL,FILBOX, for changes in default parameters ATMPOL,POLVOL
   and method of calculation. Cycles through atom list and writes output
   file. PRNTBX,PRNTPN
   
   SHELL Sets up hypothetical solvent boundary to 'define' protein
   surface.
   
   FILBOX Selects atoms from coordinate BXLOAD, list that may define the
   GETNUM limiting polyhedron. Constructs all potential face planes.
   
   ATMPOL Establishes the limiting poly- ERROR,VERTEX, hedron from the
   list supplied SAMSID by FILBOX. Provides list of coordinates of all
   vertices and their identities.
   
   POLVOL Calculates volume of the limiting VOLTET polyhedron.
   
   ERROR Puts out error messages in response to certain types of
   geometrical errors or array dimension problems found in program run.
   (i.e. three points defining a plane are colinear; three planes do not
   intersect at a point etc.)
   
   Utility Routines:
   
   GETNUM Identifies residue type number and atom type number for an atom
   specified by serial number in the coordinate list.
   
   BXLOAD From the normal components and a point P associated with atom
   J, the constant factor in the equation for the plane is calc and
   loaded in BOX(5,J)
   
   PRNTBX Prints out contents of arrays IBOX and BOX after return from
   FILBOX
   
   PRNTPN Prints out contents of arrays POLYHN and IPOLYH after return
   from ATMPOL.
   
   Mathemastical Subroutines:
   
   VERTEX Calculates the point of inter- POINT section of three planes
   defined by four specified atoms.
   
   INSIDE Logical function set to .TRUE. SAMSID if a point P is inside a
   tetrahedron formed by four specified planes.
   
   SAMSID Logical funtion set to .TRUE. None if two points P1 and P2 are
   on the same side of a specified plane.
   
   VOLTET Returns the volume of a tetra- DET3C hedron specified by its
   four vertices.
   
   PLANE Returns the equation of the plane DET3R,ERROR determined by
   three given points. (error if three points colinear)
   
   POINT Returns the point of intersection DET3R,ERROR of three given
   planes.(error if point is indeterminate)
   
   CENTRD Computes the centroid of a tetra- None hedron identified by its
   4 vertices (not used in present version of program)
   
   DET3C For the 3x4 array A, the values None of the four 3x3 unique
   determinants are returned.
   
   DET3R For the 4x3 array A, the values None of the four 3x3 unique
   determinants are returned.
   
   C) SUBROUTINE SHELL
   
   Positions in a cubic lattice, ICL, just outside of, but adjacent to,
   the protein atoms are identified. These will serve to define the
   protein surface for the purpose of the volume calculations as
   described later. In principle, there is no particular restriction on
   the size of the lattice, although the calculated volumes of the
   surface atom will depend to some extent on the lattice dimensions. In
   the current version, the default value of the lattice edge is 2.8 A
   giving a cube which is about 3/4 of the volume occupied by a water
   molecule. The uncertainty in the eventual Voronoi volume increases
   with lattice size while the computation time increases rapidly as the
   lattice size is decreased.
   
   The size of the lattice, ICL, in the three dimensions is made larger
   than the protein so that there are at least two empty cubes in each
   direction outside of the protein. The protein atoms are then loaded
   into the lattice positions. With the default size about half of the
   lattice positions that contain any protein atom contain only a single
   atom. A few cubes contain as many as five atoms. When the loading is
   complete each entry in the array ICL contains either 0 or a positive
   integer. The latter is an index to a location in the array JSERN. That
   entry in JSERN gives the number of following positions in JSERN that
   contain the serial numbers of the atoms whose centers are located in
   the lattice cube identified by the ICL array index.
   
   The entire array ICL is now checked. All positions whose 26 nearest
   neighbors are not protein-containing locations are loaded with the
   flag -1. These positions represent bulk solvent remote from the
   protein.
   
   Of the remaining positions containing 0s some may be inside the
   protein and represent potential cavities. These are identified as
   positions which have among their 26 neighbors one or more pairs of
   opposng positions both of which contain a protein atom(s). Such
   positions are loaded with the flag -2.
   
   At this point both the 0 ad -2 lattice positions, while not containing
   any protein atoms, may have the cube center inside the van der Waals
   envelope of a protein atom. This is checked and any solvent (i.e. 0)
   positions so found are flagged -3, and any such -2 positions are
   shifted to -4. The -3 and -4 positions are not considered further in
   this program but are flagged should the need arise to refer to them.
   The remaining 0 and -2 positions are now both empty and outside the
   van der Waals envelope of the protein.
   
   In most calculations the -2 positions will be disregarded and the
   space that they represent is assigned to the protein. The positions
   labeled 0 are all face, edge or corner connected to themselves and to
   cubes containing protein atoms. They thus form a connected envelope
   around the protein.
   
   If SHELL the final contents of ICL will be listed in the output file
   on LUN2. The three dimensional array is sectioned perpendicular to Z
   (K index). The X axis (I index) is horizontal and Y (J index)
   vertical.
   
   Each lattice position is labeled with -4, -3, -2, -1, 0 or **, the
   last for protein containing positions.
   
   D) SUBROUTINE FILBOX
   
   This subroutine is entered with the identity and coordinate of the
   target atom whose volume is to be calculated. Its location in the ICL
   lattice is established as are the 26 surroundng cubes which would
   contain the relevant 'solvent' positions, if any.
   
   The coordinate file is then checked and all atoms whose centers are
   within the selected distance, ARANGE, of the target atom are loaded
   into the arrays TEMP and ITEMP. Any of these atoms wich are 'solvent'
   positions have their distance adjusted such that the Voronoi plane to
   be drawn will be tangent to the van der Waals sphere. This group of
   atoms is now loaded into the array as BOX and IBOX in order of their
   increasing distance from the target atom.
   
   At this point the serial number in the coordinate lists of the atom
   and a code to indicate whether it is a 'solvent' shell position or not
   is contained in IBOX. In BOX the distance to the target atom is
   located in BOX(1,I) and the X, Y and Z components of this distance in
   BOX(2,-4, I). The latter represents the interatomic vector and are the
   direction components of the normal to the Voronoi plane. This plane is
   completely defined by specifying the point where it intersects the
   interatomic vector.
   
   One of three procedures is chosen to define this point of
   intersection. In the original Voronoi procedure the plane bisects the
   interatomic vector. In Richards' method B the ratio of van der Waals
   or covalent radii of the atoms are used. In the radical plane
   procedure only the van der Waals radii of the atoms are used whether
   they are covalently connected or not. The details of these procedures
   are discussed in Appendix A.
   
   The final section of FILBOX loads into the highest index positions of
   BOX, four hypothetical planes surrounding the target atom. These
   represent a very large tetrahedron which is simply used as a starting
   point for the interactive determination of the limiting polyhedron by
   the next subroutine.
   
   E) SUBROUTINE ATMPOL
   
   This subroutine operates on the contents of the array BOX and loads
   the arrays POLYHN and IPOLYH with the vertex positions and
   identifications of the developing polyhedron. Each vertex represents
   the point of intersection of three planes. The X, Y, Z coordinates of
   tis point are placed in POLYHN. The vertex is identified by the three
   planes, each of which, in turn, is associated with a particular atom
   surrounding the target atom. For the purpose of this subroutine, these
   atoms are identified by their index in the array BOX. The vertex can
   thus be identified by three such indices. These indices are stored in
   IPOLYH. The initial set of 4 vertices are produced from the large
   tetrahedron loaded in positions 97-100 in BOX.
   
   ATMPOL then starts checking each plane in BOX to see if it forms part
   of the limiting polyhedron. This is accomplished by examining each
   vertex with respect to the plane. If the vertex is on the same side of
   the plane as the target atom, then it remains part of the polyhedron.
   If the plane separates no vertices from the target atom, then it is
   not part of the polyhedron and is disregarded. If the plane does
   separate one or more vertices, then this vertex or vetices are
   discarded and the new vertices produced by the plane are added to the
   list. This last operaion is the most complex.
   
   For this purpose, the vertices are identified as the intersection of
   three lines (the array LINES), rather than three planes. Each line
   represents the intersection of two of the planes that form the vertex.
   Each line is represented by an index pair. When a vertex is
   eliminated, the three lines that identify that vertex form 3 new
   vertices through their interaction with the new plane. When more than
   one vertex is removed by a single plane, it is necessary to keep track
   of which lines are kept and thus form new vertices with the plane.
   Some lines will be eliminated completely, that is they do nt intersect
   the plane wthin the region of interest.
   
   As each plane is tested, the polyhedron is unaffected or made smaller.
   The total number of vertices generally increases but varies
   erratically during the computation. Normally by the end of the
   calculation less than one half of the entries in BOX actually are used
   to define the limiting polyhedron. This indicates that the limit has
   indeed been reached, and that no other atoms in the structure, which
   have not been explicity examined, would contribute to the polyhedron
   if tested.
   
   F) SUBROUTINE POLVOL
   
   This subroutine takes the contents of POLYHN and IPOLYH and calculates
   the volume of the limiting polyhedron.
   
   The vertices of each face have one index in common, the index that
   identifies the atom associated with the face normal. All index pairs
   in IPOLYH that contain that common index are collected. The other pair
   of indices associated with each vertex are then arranged in sequence
   to define the perimeter of the face. The face is then divided into
   triangles with a common apex at one vertex. The volume of the
   tetrahedra formed by these triangles and the target atom at the center
   of the polyhedron are then calculated and summed. This procedure is
   repeated for each face of the polyhedron yielding,finally, the total
   volume.
   
   It might be noted here that if one wishes to draw one or more of the
   polyhedra with a graphics program, the necessary data can be obtained
   from this subroutine. The coordinates of all the vertices are
   contained in POLYHN and the subroutine orders the vertices in the
   sequence in which the vectors would be drawn.
   
   ADDENDUM
   
   The volume of the -2 positions provided by SHELL may be calculated
   separately, treating these positions as additional "protein atoms".
   Note that such calculations, of course, will change the volume
   calculated for adjacent protein atoms. No van der Waals radius is
   assigned to these positions. The defining planes are drawn tangent to
   the surrounding protein atoms. The "cavity" volume so calculated is
   only a crude approximation to the real void space because of the
   coarseness of the lattice used. (See: F.M.Richards, Carlsberg Research
   Communications 44: 47-63 (1979)). This option has NOT been activated
   in this version of the VOLUME program.
   
SEE ALSO

   surface.
   
AUTHORS

   19-IX-92 Alliant UNIX version (mbg/kxh) of Fred Richard's VOLUME
   program.
   
EXAMPLE

#
#Volume:
#
volume xyzin surface.out     \
       xyzout volume.out3     \
       errout volume.error   \
       shellfile water.shell \
       << eof
!
! The default settings mean you can run it with
!  just the Key_Word RUN
!
EDGE 3.05      ! length of the edge of the shell (default=2.80)
SRAD 6.10      ! pick search radius              (default=6.50)
METHOD  VORO   !        ==>>  Standard Voronoi Procedure (default)
!              or  RICH ==>>  Richards" Method B
!              or  RADI ==>>  Radical Plane Procedure
OUTER  0.0     ! For Surface Volume Adjustment  (default)
NOSHELL        ! or SHELL   (default = NOSHELL)
CALCLUATE      ! or NOCALCULATE but why  (default = CALCULATE VOLUMES)
!VERBOSE       ! dont activate this unless you want a very big .error file
!               default = NOVERBOSE
!WATER          ! use this if you want to add the extra shell
!                 of water from the file SHELLFILE
NOWATER         ! default
RUN
eof
#