XDLMAPMAN (CCP4: Supported Program)
                                       
NAME

   xdlmapman - X-windows tool; manipulation, analysis and reformatting of
   electron density maps.
   
SYNOPSIS

   xdlmapman [-font1 | font2 | font3 | font4 | font5]
   [menu-driven command selection; interactive parameter input]
   
DESCRIPTION

   xdlmapman can be used to read, write, analyse and manipulate
   electron-density maps from most biomacromolecular refinement packages,
   as well as from/for CCP4, PHASES and O.
   
   The program runs in interactive mode only. It uses the XDL_VIEW
   toolkit of J.W. Campbell to provide an easy-to-use interface. Commands
   are selected by clicking on the desired menu option. Map formats are
   selected with pop-up menus; all other parameters are set in pop-up
   dialogue boxes (cut-and-paste is supported). In most cases, default
   values are given in [square brackets]. To accept these defaults, hit
   the RETURN key. If multiple numbers are to be input (e.g., cell
   constants), and if only the first one needs to be changed, for
   instance, typing the new value for this first number followed by the
   RETURN key will preserve the values for the other five numbers.
   
   There is a command line option (-font?) which will determine the size
   of the menu font. These fonts refer to the xdl fonts which are defined
   from 1 to 5. This can be useful if the window size is too large for
   the screen. The default font size is 2. The font definitions can be
   changed in the .Xdefaults file or xrdb, however all xdl programs will
   be then be effected.
   
   Output from the program is written to a separate area of the main
   window. Output can be scrolled and cut and pasted into other
   documents.
   
   For lengthy operations a progress bar shows how much of the operation
   has been completed.
   
HISTORY

   xdlmapman is a CCP4 special version of MAPMAN (part of the Uppsala
   RAVE averaging package). This version is entirely interactive and has
   a user-friendly interface. However, this version can only handle one
   map at a time, and some of the functionality of the parent program is
   absent.
   
   MAPMAN was originally written as a simple format-exchange program, to
   convert X-PLOR maps to CCP4 format etc. It has grown quite a bit to
   handle many types of map, to include MAPPAGE functionality (previously
   provided as a stand-alone program from Uppsala), and to perform
   skeletonisation (also previously provided as a stand-alone program
   from Uppsala) and peak-picking.
   
   Many (parts of) routines were written by other people including Soren
   Thirup, Morten Kjeldgaard, Wolfgang Steigemann and Phil Evans.
   
MENU OPTIONS

   Commands are issued by moving the pointer over the desired menu option
   and clicking with the left mouse button.
   
  READ A NEW MAPFILE
  
   Provide the name of the file and then select the appropriate file type
   from the pop-up menu. See FORMATS.
   
  LIST MAP STATISTICS
  
   This prints some information and statistics pertaining to the map that
   is currently in memory.
   
  MOMENTS OF THE MAP
  
   This calculates and lists statistical moments of the map (average,
   standard deviation, skewness and curtosis).
   
  MULTIPLY MAP BY A FACTOR
  
   All density values will be multiplied by the number provided (if this
   number is not equal to zero or one).
   
  DIVIDE MAP BY A FACTOR
  
   All density values will be divided by the number provided (if this
   number is not equal to zero or one).
   
  PLUS SOME VALUE
  
   The number provided (if unequal zero) will be added to all density
   values.
   
  SCALE THE MAP TO A RANGE
  
   The map is scaled such that all electron density values lie inside the
   range of numbers provided (e.g., -100 to +100).
   
  ZERO PARTS OF THE MAP
  
   All density values which lie outside the range provided are set to
   zero.
   
  NORMALISE THE MAP
  
   The map will be scaled such that the average density is zero and the
   standard deviation ("sigma") is one.
   
  UVW
  
   The axis-order in which the map is written is changed according to the
   input by the user. For example, to write out XY sections with Y
   varying fastest, then X and then Z, use UVW = 2 1 3.
   
  SPACEGROUP OF THE MAP
  
   The spacegroup *number* will be set to the number provided. For
   example, to change the spacegroup to P212121, the number 19 would be
   entered.
   
  CELL CONSTANTS
  
   The cell constants can be edited. This is normally not a good idea.
   The only exception is when a map is read with a format that does not
   precisely enough reproduce the cell constants (e.g., integer*2 DSN6
   maps). In such cases, angles of 90.0 degrees are sometimes converted
   to 89.9998.
   
  BONES SKELETONISE
  
   This is the Thirup & Jones implementation of Greer's electron density
   skeletonisation algorithm. A base level (e.g., 1.5 * sigma) and a step
   size (e.g., sigma) need to be provided. This command would normally be
   followed by BONES WRITE (quod vide). the reason to separate the two is
   to enable (1) experimentation with different skeletonisation
   parameters without having to write out the BONES file, and (2)
   experimentation with parameters of the BONES WRITE command without a
   need to redo the skeletonisation.
   
  BONES WRITE
  
   Transform the skeletonised density into a set of BONES suitable for
   use in O. Provide the filename, skeleton name and a cut-off length to
   partition bones into main-chain and side-chain fragments.
   
  PROD_PLUS FOR MAPPAGE/BRIX
  
   With this command the value of Prod and Plus for MAPPAGE and BRIX can
   be changed. These values are normally set such that the entire range
   of density can be captured by the integer*2 format of DSN6 maps.
   
  RANGE FOR MAPPAGE/BRIX
  
   Instead of supplying Prod and Plus for MAPPAGE and BRIX, the desired
   range of density values which should be covered in a DSN6 map can be
   supplied. The program will use this range to calculate appropriate
   values for Prod and Plus.
   
  MAPPAGE FILE
  
   This produces a DSN6 map ("mini-map") suitable for use with O. The map
   is in binary DSN6 format, using one byte per density value.
   
  BRIX FILE
  
   This produces a BRIX map ("mini-map") suitable for use with O. The map
   is in binary character format, which means that it can head inspected
   (using Unix commands such as cat, head, or more). In particular, the
   header record can be inspected in this fashion.
   
  SWAPBYTES
  
   This command takes an existing DSN6 map file which was created on a
   VAX, swaps the bytes, and then writes the new records back to the
   *same* file.
   
  WRITE MAP
  
   Provide the name of the file and then select the appropriate file type
   from the pop-up menu. See FORMATS.
   
  PICK PEAKS
  
   With this command, peaks above a certain level and in a user-defined
   part of the map can be picked. They are written out as a PDB file
   containing dummy water molecules (in fact, water oxygen atoms). The
   algorithm is the same as that used to pick peaks in 2D and 3D NMR
   spectra (see REFERENCES).
   
  DELETE CURRENT MAP
  
   Remove the current map from memory.
   
  HELP
  
   This prints some brief information. Subsequently, click on *any* menu
   command to get a brief explanation of what that command does.
   
  QUIT
  
   Stop working with the program.
   
FORMATS

   Supported input formats : PROTEIN FFT-Y TENEYCK2 CCP4 X-PLOR EZD MASK
   NEWEZD BINXPLOR BRICK DSN6 3DMATRIX TNT PHASES FSMASK
   
   Supported output formats : CCP4 EZD MASK NEWEZD ENVELOPE
   
   Notes on formats :
   
   
          CCP4 - seems to work okay (not masks ?)
          PROTEIN/FFT-Y/TENEYCK2 - untested
          X-PLOR - ASCII maps; works okay
          BINXPLOR - binary maps; may work on 32-bit machines
          BRICK/DSN6 - O-type map files (not BRIX !)
          EZD/NEWEZD - O-type ASCII maps
          MASK - any of the Uppsala mask formats (output: COM only)
          3DMATRIX - ASCII files from X-PLOR Rot Fun etc.
          TNT - untested
          PHASES - Furey maps; works except for scale
          FSMASK - Furey masks; not implemented yet
          ENVELOPE - CCP4-type masks; does not work ?
          
REFERENCES

    1. XDLMAPMAN:
       G.J. Kleywegt & T.A. Jones (1996), Acta Cryst. D52, 826-828.
    2. XDL_VIEW:
       J.W. Campbell (1995). "XDL_VIEW, an X-windows-based toolkit for
       crystallographic and other applications", J. Appl. Cryst. 28,
       236-242.
    3. RAVE:
       G.J. Kleywegt & T.A. Jones (1994). "Halloween ... Masks and
       Bones", in "From First Map to Final Model" (S. Bailey, R. Hubbard
       & D. Waller, Eds.), SERC Daresbury Laboratory, pp. 59-66.
    4. MINI-MAPS:
       T.A. Jones (1978). "A graphics model building and refinement
       system for macromolecules", J. Appl. Cryst. 11, 268-272.
    5. O/BONES:
       T.A. Jones, J.Y. Zou, S.W. Cowan, & M. Kjeldgaard (1991).
       "Improved methods for building protein models in electron density
       maps and the location of errors in these models", Acta Cryst. A47,
       110-119.
    6. SKELETONISATION:
       J. Greer (1974). "Three-dimensional pattern recognition: an
       approach to automated interpretation of electron density maps of
       proteins", J. Mol. Biol. 82, 279-301.
    7. PEAK-PICKING:
       G.J. Kleywegt, G.W. Vuister, A. Padilla, R.M.A. Knegtel, R.
       Boelens, & R. Kaptein (1993). "Computer-assisted assignment of
       homonuclear 3D NMR spectra of proteins. Application to pike
       parvalbumin III", J. Magn. Reson. B102, 166-176.
    8. CCP4:
       Collaborative Computational Project Number 4 (1994). "The CCP4
       suite: programs for protein crystallography", Acta Cryst. D50,
       760-763.
       
KNOWN BUGS

   Some of the map formats are untested.
   If you improve the program, please notify GJK of your changes so that
   they can be implemented in future versions and the entire community
   may benefit from them (E-mail a brief description and the relevant
   pieces of code to "gerard@xray.bmc.uu.se").
   
AUTHORS

   Originators: G.J. Kleywegt & T.A. Jones, Uppsala
   
SEE ALSO

   Companion program for reflection files:
     * xdldataman
       
   Other map/mask conversion programs:
     * mama2ccp4
     * maptona4